## Slide 1: Lesson 10: Hurricane Surge Model

## Slide 2: Lesson 10: Goal and Objectives
Goal: To provide an overview of the storm surge model within Hazus.
After completing this lesson, you will be able to:
  Discuss the causes for storm surge.
  Describe the Hazus surge model components.
  Understand the procedure for running a hurricane surge in Hazus.

## Slide 3: Hurricane Scenario Definition Options

## Slide 4: Sources of Storm Surge
  Hurricanes (i.e. Hurricane Katrina)
  Extratropical Cyclones and Nor’easters
    Edmund Fitzgerald (1975): 15-20 foot waves in Great Lakes
    Storm of the Century (1993): 12 foot waves in Atlantic
  Subtropical Storms
https://earthobservatory.nasa.gov/IOTD/view.php?id=46662

## Slide 5: What Causes a Storm Surge?

## Slide 6: Factors Influencing a Surge's Size
  Storm surge: abnormal rise of water generated by a storm, over and above the predicted astronomical tides
  Storm tide: water level rise due to the combination of storm surge and the astronomical tide

## Slide 7: Factors Influencing a Surge's Size
  Wave breaking can increase the height of the surge and is dependent on the continental shelf.

## Slide 8: Factors Influencing a Surge's Size
Wind and Storm Motion
  Strongest winds and thus highest surge (without coastline effects) occur in the right - front quadrant of hurricane
  Here the forward speed of the hurricane is added to the rotational winds of the hurricane to achieve the highest wind speeds

## Slide 9: Storm Surge Dynamics
 | The hurricane’s surface winds push against the water, and water from below moves upward to replace the displaced water. | The bulge of water and current slam into the continental shelf and are forced upward and inward.

## Slide 10: Coastline Effects and Surge Size
  Orientation of the hurricane with respect to the coastline can influence the surge magnitude.
  Water can ‘pile up’ with favorable orientations. If hurricane winds are pushing against the coastline, water is caught along the coast.
  Water can also be trapped in bays.

## Slide 11: Surge Demonstration
Hurricane Dennis Surge: https://www.nhc.noaa.gov/surge/HistoricalRuns/?large&parm=2005_dennis#contents
Hurricane Dennis (2005)

## Slide 12: Discussion 10.1: Storm Surge
Goal: Discuss the previous animation and answer the questions.
Time: 10 Minutes
Questions:
  How does the orientation of the coastline effect the storm surge depth?
  Where are the highest storm surges?
  How can a surge affect an area (geographically) that is not in close proximity to the hurricane path?

## Slide 13: Hurricane Storm Surge Overview
Hurricane Model
  Windspeed and direction
Surge Model
  SLOSH (sea, land, ocean)
  SWAN (near shore)
Wind and Surge are combined for aggregate inventory damages and losses only.

## Slide 14: SLOSH
  SLOSH = Sea, Lake, and Overland Surge from Hurricanes
  Numeric Model initialized on a grid that requires the following inputs:
    Basin selection: SLOSH is packaged with pre-defined basins that have bathymetry (NGDC) and elevation information (USGS) for each grid cell.
    Hurricane characteristics: direction of movement, radius to maximum winds, pressure, location, direction, and speed

## Slide 15: SLOSH
  Produces reasonably accurate estimates of surge and runs quickly
  Emergency management community is familiar and comfortable with using this model.
  Does not explicitly model tide.
    Tide is generalized by treating it as a fixed increase or decrease in initial water level based on predicted tide at time of landfall in the absence of storm surge and waves.

## Slide 16: SLOSH Basins

## Slide 17: Domains in SWAN Runs
Domains
  Deep Water: Red
  Near Shore: Blue

## Slide 18: SWAN
  Simulating Waves Nearshore
  Created by Delft University of Technology
  Models:
    Wave propagation
    Wave generation from wind
    Wave interactions, dissipation, transmission, and diffraction
    Others

## Slide 19: Coupled Surge and Wave Modeling
  SLOSH and SWAN codes have been coupled together.
  Methodology bridges gap between existing Hazus Hurricane Wind and Hazus Coastal Flood models
  SLOSH is run first to update water elevations.
    SWAN uses water elevations produced by SLOSH.
    Result is larger modeled wave heights in areas where waves are depth-limited.
  SWAN is run to update wave stresses.
    Wave stresses are added to wind stress in SLOSH.
    Increases modeled storm surge due to wave setup

## Slide 20: Overland Waves
  Model uses 1-D transects and simplified WHAFIS-like methodology to propagate waves inland from the shoreline.
  Where each transect intersects the coastline, use the modeled significant wave height from SWAN to estimate the controlling wave height, Hc = min(0.78 ds, 1.6 Hs) where ds = still water depth at the coast line.
  Wave crest elevation = SWEL + 0.7 Hc
    Neglect wave regeneration and wave dissipation
    Neglect wave run-up and dune erosion
  Use V-zone damage functions where Hc ≥ 1.5 ft

## Slide 21: User Work Flow

## Slide 22: Activity 10.2: Hurricane Storm Surge
Goal:
  Create a combined Flood/Hurricane study region.
Time: 10 minutes

## Slide 23: Exercise 10.2: Tasks
Task 1: Create a Surge Study Region
Task 2: Create a Surge Scenario
Task 3: Run a Surge Analysis

## Slide 24: Coastal Surge Hazard Modeling Options

## Slide 25: Initial Water Level
Pre-storm tide anomaly is the difference between:
  The observed tide
  The predicted tide approximately two days before landfall (i.e., before the effects of storm surge or waves reach the study region)

## Slide 26: Flood Hazard Type and User Data

## Slide 27: Depth Grids
  Depict variable flood depths throughout the determined flood extent for an event
  May be produced for a range of flood events
    Most commonly the 0.2-percent, 1-percent, 2-percent, 4-percent, and 10-percent annual chance flood events
  Many are available for download from FEMA MSC
  Can be created from raw data

## Slide 28: Defining Topography
  Required DEM extents automatically determined by Hazus
  You can use USGS national map DEM or provide your own more detailed DEM
  Terrain Data in Esri GRID format (Ex. High resolution community/county specific LiDAR, NED 10m or NED 30m)

## Slide 29: Delineate Floodplain
  Inundation limits
  Transects
    Depth-limited wave heights
  Zone determination
    A-zone
    Coastal A-zone
    V-zone

## Slide 30: Surge Model
  Wind losses created first in the hurricane model.
  Storm surge depths are input into the flood model.
  Flood (surge) damages and losses utilize the flood depth damage curves.
  The combined analysis utilizes a new set of curves that combine the flood and wind losses.

## Slide 31: Flood Depth-Damage Curves
Damage to buildings and infrastructure is estimated using depth-damage curves.

## Slide 32: Depth-Damage Functions
Depth-damage functions are applied to relevant depth.
  Buildings: first-floor height
  Coastal Buildings: Bottom of first finished floor
  Equipment: height above first floor

## Slide 33: Viewing Depth Damage Curves

## Slide 34: Viewing Depth Damage Curves

## Slide 35: FEMA Flood Zone A
The Special Flood Hazard Area (except coastal V Zones) shown on a community's Flood Insurance Rate Map. There are five types of A Zones:
Zone | Description
A | SFHA where no base flood elevation is provided.
A# | Numbered A Zones (e.g., A7 or A14), SFHA where the FIRM shows a base flood elevation in relation to NGVD.
AE | SFHA where base flood elevations are provided. AE Zone delineations are now used on new FIRMs instead of A# Zones.
AO | SFHA with sheet flow, ponding, or shallow flooding. Base flood depths (feet above grade) are provided.
AH | Shallow flooding SFHA. Base flood elevations in relation to NGVD are provided.

## Slide 36: FEMA Flood Zone V
The Special Flood Hazard Area subject to coastal high hazard flooding.
There are three types of V Zones:
Zone | Description
V | SFHA where no base flood elevation is provided.
V# | Numbered V Zones (e.g., V7 or V14), SFHA where the FIRM shows a base flood elevation in relation to NGVD.
VE | SFHA where base flood elevations are provided. VE Zone delineations are now used on new FIRMs instead of V# Zones.

## Slide 37: FEMA Flood Zone C
  Area of minimal flood hazard.
  Usually depicted on Flood Insurance Rate Maps as above the 500-year flood level.
  B and C Zones may have flooding that does not meet the criteria to be mapped as a Special Flood Hazard Area.
    Especially ponding and local drainage problems.

## Slide 38: GBS Flood Loss Estimation
Hazus performs an area weighted assessment of damage for aggregate inventory.
  Number of grid cells at a given depth is counted and then divided by total number of cells within census block.
  Result is used to “weight” damage at that flood depth for each occupancy.
  This approach is most appropriate for large areas.

## Slide 39: GBS Loss Estimation Methodology
  Assumes that inventory is evenly distributed across each census block.
    EX: If 25% of the block has 2 feet of water, it is assumed that 25% of the 4 single family dwellings in the block are in 2 feet of water.
  Losses reported as totals for each occupancy and building type rather than for each building.

## Slide 40: Combined Flood and Wind Losses
Table 8.132 in the Hurricane Technical Manual
Sub-Assembly | Pre-FIRM Foundation A Zone Conditions | Pre-FIRM Foundation CA/V Zone Conditions
Foundation | Start damaging foundation at 80% (first non-zero value is at 90%) damage and max damage at 50% Pre-FIRM value (e.g. 3% if foundation represents 6% of the structure value) | Start damaging foundation at 50% damage (first non-zero value is at 60%) and max at 80% Pre-FIRM value (e.g. 5% if foundation represents 6% of the structure value)
Below First Floor | Start damaging BFF at 0% damage (first non-zero value is 10%) and achieve 100% pre-FIRM value by 40% building damage | Start damaging BFF at 0% damage (first non-zero value is 10%) and achieve 100% pre-FIRM value at 20% building damage
Structure Frame | Start damaging structure frame at 70% damage (first non-zero value is 80%) and achieve 100% Pre-FIRM value at 100% building damage | Start damaging structure frame at 10% damage (first non-zero value is 20%) and achieve 100% Pre-FIRM value at 90% building damage
Roof Cover | Same as Structure | Same as Structure
Roof Frame | Same as Structure | Same as Structure
Exterior Walls | Start damaging exterior walls at 0% damage (first non-zero value at 10%) and reach maximum (100%) at 100% building damage. Ensure that exterior is always below interior. | Start damaging exterior walls at 10% damage (first non-zero value is 20%) and reach maximum (100%) pre-FIRM value at 90% building damage.
Interiors | Start damaging interior at 0% damage (first non-zero value at 10%) and reach maximum Pre-FIRM value (100%) at 80% building damage. | Start damaging interiors at 0% damage (first non-zero value at 10%) and reach maximum Pre-FIRM value (100%) at 80% building damage.

## Slide 41: Combined Flood and Wind Losses
  Losses from wind and surge are combined using the combined losses tables.
    EX: When wind losses are 50% and flood losses are 20%, the combined loss is 62.5%.
Column Headers represent Wind-Only Building Loss percentages, Row Labels represent Flood-Only Building Loss percentages.
 | 0% | 10% | 20% | 30% | 40% | 50% | 60% | 70% | 80% | 90% | 100%
0% | 0% | 10% | 20% | 30% | 40% | 50% | 60% | 70% | 80% | 90% | 100%
10% | 10% | 19.5% | 28.7% | 37.9% | 47.1% | 56.2% | 65.3% | 74.5% | 84.4% | 94.3% | 100%
20% | 20% | 29.1% | 37.5% | 45.9% | 54.3% | 62.5% | 70.9% | 79.4% | 89.1% | 98.9% | 100%
30% | 30% | 38.8% | 46.7% | 54.5% | 62.3% | 70.0% | 77.8% | 85.7% | 95.0% | 100.0% | 100%
40% | 40% | 48.4% | 55.7% | 62.8% | 69.9% | 76.9% | 84.0% | 91.2% | 100.0% | 100.0% | 100%
50% | 50% | 58.0% | 62.6% | 71.1% | 77.5% | 83.8% | 90.3% | 96.9% | 100.0% | 100.0% | 100%
60% | 60% | 67.6% | 73.5% | 79.3% | 85.0% | 90.6% | 96.4% | 100.0% | 100.0% | 100.0% | 100%
70% | 70% | 77.2% | 82.4% | 87.5% | 92.5% | 97.3% | 100.0% | 100.0% | 100.0% | 100.0% | 100%
80% | 80% | 86.8% | 91.4% | 95.7% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100%
90% | 90% | 96.4% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100.0% | 100%
100% | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100%

## Slide 42: Combined Flood and Wind Losses
  The flood model (surge) calculates losses on the census block level: in a combined hurricane/flood model the hurricane wind model will calculate losses on the block level.
  Combined losses can only be calculated on the GBS inventory: user-defined facilities and site-specific facilities cannot be analyzed using the combined analysis.
NOTE: The Set Optimization option is only available in flood/hurricane regions. If you are not interested in combined surge/wind, select this to run the hurricane model at the tract level (faster).

## Slide 43: Wind-Only Economic Loss Table

## Slide 44: Combined Wind & Flood Loss Table

## Slide 45: Combined Wind & Flood Loss Table

## Slide 46: Combined Loss Summary Report

## Slide 47: Exercise 10.3: Surge Menu
Goals:
  Explore the Surge menu items in the hurricane model and flood model. Discuss the reports and tables from the combined losses.
Time: 45 Minutes

## Slide 48: Exercise 10.3: Tasks
Task 1: Define User Data
Task 2: Create a New Scenario
Task 3: Run the Surge Analysis
Task 4: View Reports and Discuss Map Options

## Slide 49: Lesson 10: Review
  What are the causes of a storm surge?
  What are the Hazus surge model components?
  What is the procedure for running a hurricane surge in Hazus?
  How do the hurricane and flood model damage and loss analyses differ (not combined)?

## Slide 50: Questions?