## Slide 1: Lesson 11: Mitigation Analysis

## Slide 2: Lesson 11: Goal and Objectives
Goal: To provide an overview of the mitigation analysis provided in Hazus.
After completing this lesson you will be able to:
  Understand the common mitigation practices for hurricanes.
  Explain how mitigation is modeled in Hazus.

## Slide 3: Applying Mitigation
In Hazus: Modifying wind building mapping scheme Can be applied: One technique at a time Many techniques at once Can be applied geographically: Entire region Specific census tracts Applies to all building classes |  | 

## Slide 4: Possible Uses of Mitigation Options
Identify mitigation options with best return on investment.
  Answers depend on local hurricane climatology and building stock
  Additional information required: mitigation cost data
Predict impact of building stock changes:
  New building codes
  New construction trends

## Slide 5: Mitigation of Damage: Options for…
Single-Family or Multi-Family Residential:
  Roof covering
  Secondary water resistance
  Roof sheathing attachment
  Roof framing attachment
  Opening protection
Manufactured Homes:
  Tie-downs
  Opening protection

## Slide 6: Mitigation of Damage: Options for…
Commercial buildings (low-rise strip mall buildings):
  Shutters on all windows and entry doors
  Roof-wall connection clips/straps
  Superior wood roof deck attachment
  Superior metal roof deck attachment
Commercially engineered buildings, low rise industrial buildings, and pre-engineered metal buildings:
  Superior metal roof deck attachment
  Opening protection

## Slide 7: Roof Covering
  Best solution to mitigate loss of roof cover:
    Replacement of inferior products with superior ones
  Consider life span of roof:
    Shingles: 10-25 years
    Tiles: 50+ years
  Consider cost of replacement:
    Shingles: Approx. $3,000-5,000 (relatively cheap)
    Tiles: Approx. $20,000 (relatively expensive)
  Hazus model does not include models for concrete tiles or metal roofs (except Hawaii)

## Slide 8: Shingle Roof Covering Standards
Testing Standards:
  ASTM D7158 (modified to 115 mph)
  SFBC PA 107 or PA 108: Dade County test for wind resistance of shingles
  UL 997 modified to 110 mph: Make sure it is high wind version of test

## Slide 9: Secondary Water Resistance (SWR)
Applied on all plywood joints

## Slide 10: Secondary Water Resistance (SWR)
  Roof cover loss is likely.
  SWR serves as backup in event of roof covering losses.
    Self-adhering waterproof underlayment
    Meets ASTM D 1970
    Apply at time of normal re-roofing

## Slide 11: Roof Sheathing Attachment
Re-nail with tighter nail spacing:
  SSTD 10-99: Latest code requirements are 6”x6” spacing in high wind areas
  Re-nail during re-roofing option
Re-nail with stronger fasteners:
  Larger nails
  Ring shank nails
  Screws
Not a good option for expensive roof coverings such as tile or slate

## Slide 12: Roof Framing Attachment

## Slide 13: Opening Protection
Openings include:
  Windows
  Doors (including patio and French doors)
  Sliding glass doors
  Garage doors
  Skylights
Protection takes two forms:
  Replace existing fenestration with one that is impact-resistant
  Install external protection devices that are impact-resistant

## Slide 14: Opening Protection
Large Missile Impact Test:
  Firing a 2x4 at approximately 50ft/s at product
  Product passes if it remains operable after resisting impacts
Four Dominant Impact Standards:
  ASTM E 1996 - 9lm missile
  SBCCISSTD 12-97
  Dade County South Florida Building Code PA 201
  Florida Building Code TAS 201
Small Missile Impact Test:
  Approx. 20 pieces of gravel are fired with a cannon at the product
NOTE: These tests also include a pressure cycling component

## Slide 15: Opening Protection

## Slide 16: External Protection Devices (Shutters)

## Slide 17: Shutters vs. Impact Resistant
Replacement of doors/windows vs. external protection devices
Exceptions:
  Garage doors: Large spans make shuttering difficult
  Entry doors: One entry door to the building is replaced with an impact resistant product to allow for egress regulations in building code
  Skylights: Very few external protection devices exist

## Slide 18: Replacement Garage Door
Impact door features:
  Ribs to reinforce panel
  Heavy track
Alternative retrofit:
  Post system

## Slide 19: Other Information
Fortified for Safer Living:
  By Institute for Business and Home Safety
  For more information visit: disastersafety.org
Blueprint for Safety:
  By Federal Alliance for Safe Homes
  For more information visit: www.flash.org
Coastal Construction Manual:
  Principles and Practices of … Residential Buildings in Coastal Areas
  FEMA P-55, 4th Edition (2011)
  For more information visit: https://www.fema.gov/media-library/assets/documents/3293

## Slide 20: Mitigation Benefits (SE Florida)
Single-Family Homes | Reduction in Annualized Hurricane Losses (AHL)
Install Shutters | 17% to 46%
Upgrade Roof | 3% to 49%
Add Secondary Water Resistance | 3% to 35%
Upgrade Roof and Add SWR | 4% to 57%
Install Shutters and Upgrade Roof | 46% to 71%
Shutters, Upgrade Roof and SWR | 51% to 85%
Manufactured Homes | Reduction in AHL
Foundation Tie-Down | 9% to 25%

## Slide 21: Discussion 11.1: Mitigation Options
Goal:
  Discuss mitigation options.
Time: 10 minutes

## Slide 22: Exercise 11.2: Mitigation Actions
Goals:
  Run various mitigation scenarios.
  Compare and contrast the results.
Time: 45 minutes

## Slide 23: Exercise 11.2: Tasks
Task 1: Create a Study Region
Task 2: View the Pre-Mitigation Annualized Loss Estimates.
Task 3: Create and Apply a Mitigation Mapping Scheme.
Task 4: View the Post-Mitigation Annualized Loss Estimates.
Task 5: Compare the Estimated Losses

## Slide 24: Lesson 11: Review
  What are the four occupancy types that can be mitigated in Hazus?
  What are two types of opening protection?
  What is the potential reduction in loss from shuttering a structure?

## Slide 25: Questions?