## Slide 1: Lesson 12: Hazus for Response and Recovery

## Slide 2: Lesson 12: Goal and Objectives
Goal: To provide an overview of how to set up Hazus for response and recovery operations.
After completing this lesson, you will be able to:
  Read and understand a Tropical Forecast Advisory.
  Understand how to input a Tropical Forecast Advisory into Hazus.

## Slide 3: Hazus for Response and Recovery
  Predicting effects of hurricanes: Warning time of hurricanes is typically 3-5 days
  During hurricane season: Advisories are issued every six hours for all tropical storms with intermediate advisories for landfalling for rapidly changing storms
  Current position/strength and predicted position/strength can be used to make estimates of likely damage.

## Slide 4: When to Start Running Hazus

## Slide 5: Obtaining Storm Data
  Tools for manual entry of storm data:
    Designed to allow users to run analysis in Hazus based on forecast advisories.
    National Hurricane Center of the National Weather Service offers several products.
    Forecast advisories contain all information needed for Hazus.

## Slide 6: User Defined (Single Storm) Scenario
  User-Defined Scenario Type offers four options for data
  Hurrevac or Census tract data file should be used for recovery once observed data are available

## Slide 7: Typical Storm Parameters
Typical Storm Parameters
1 min mean = Hazus Input Windspeeds 3 sec gust = Hazus Output Windspeeds
Saffir Simpson Scale | 1 Min Mean (mph) | 3 sec Gust (mph) | Min Central Pressure (mb)
1 | 74-95 | 90-116 | 980 and greater
2 | 96-110 | 117-134 | 965-979
3 | 111-129 | 135-159 | 945-964
4 | 130-156 | 160-189 | 920-944
5 | 157+ | 189+ | 920 and below

## Slide 8: Using Forecast Advisories
  Forecast advisories: Text files that are available for download.
  Contain storm data:
    Lat/Long
    Central pressure
    Radius to hurricane winds
    Translation speed of storm
  Units:
    Times - UTC.
    Distances - nautical miles.
    Wind speeds - knots.

## Slide 9: Using Forecast Advisories
To run the uncertainty analysis, user must enter the times in standard advisory format (0 , 9, 21, 33, 45, 69).
Times in Standard Advisory Format | Day of Current Month | Forecast Time
0 hours Start Time | 29 | 0300Z
9 hours from Start Time | 29 | 1200Z
21 hours from Start Time | 30 | 0000Z
33 hours from Start Time | 30 | 1200Z
45 hours from Start Time | 31 | 0000Z
69 hours from Start Time | 01 | 0000Z

## Slide 10: Editing Storm Information
  Delete rows by right-clicking on header.
  Make sure there is only one blank row at bottom before clicking “Next.”
  “Time (hours)” format needed for Uncertainty Analysis.
  “Central Pressure (mbar)” and “Inland” taken from Advisory.

## Slide 11: Entering in Forecast Advisories

## Slide 12: Using NHC Advisories
Forecast advisories:
  Conservative estimates
  Don't update central pressure
  Don't update radius to wind speeds realistically
Hazus model enforces a realistic relationship between radius, central pressure, and wind speeds.

## Slide 13: Hurrevac
  HURRicane EVACuation
  Taken from NHC advisory information
  Historical storms database
  Eliminates entering information from the text-based advisories

## Slide 14: Response and Recovery Points
  There are uncertainties within Hazus.
  Forecasts are subject to changes in track and intensity.
    Causes changes in damage and loss estimations.
  Damages and losses are based on windspeeds.
    If these change, damage and loss calculations also change.

## Slide 15: Track Comparison
  Changes in position of a hurricane track can make significant changes to results.
  Discussed further in the next section
NHC official track forecasts (dashed blue lines) for Hurricane Irma from 0000 UTC 5 September 2017 to 0000 UTC 12 September 2017. The best track is given by the white line with positions given at 6 hour intervals.

## Slide 16: Errors in Forecasts
"Official forecast intensity errors were above the mean official errors for the previous 5-year period through 48 hours, then considerably lower than average after that through 5 days. A homogenous comparison of the official intensity errors with selected guidance models is given in Table 7b. The NHC intensity forecast performed better than all of the intensity model guidance at 12, 96, and 120 hours, but was worse than all of guidance at 36 and 48 hours. This unusual dichotomy appears to be due to the cyclone weakening faster than expected over land at 36 and 48 hours, but NHC correctly forecasting Harvey to stay a weak cyclone at long range, with almost every forecast point verifying over land."
NHC Tropical Cyclone Report - Hurricane Harvey, May 2018
NHC Tropical Cyclone Report – Hurricane Harvey, May 2018 https://www.nhc.noaa.gov/data/tcr/AL092017_Harvey.pdf

## Slide 17: Demonstration 12.1: Forecast Advisory Uncertainties
Goal: Discuss and demonstrate Forecast Advisory uncertainties.
Time: 45 Minutes

## Slide 18: Exercise 12.2 Forecast Advisory
Goals:
  Run various user-defined scenarios.
  Compare the results.
Time: 30 Minutes

## Slide 19: Exercise 12.2: Tasks
Task 1: Investigate Hurricane Harvey Scenarios.
Task 2: Import the Final Track using HURREVAC.
Task 3: Explore the use of H*Wind files.
Task 4: Compare the results.

## Slide 20: Hurricane Recovery Timeline
Length of recovery operations:
  Days (Short-term): Resource Allocation
  Weeks/Months (Intermediate): Clean up operations
  Months/Years (Long-term): Rebuilding
  Recovery groups: Economic, Health and Social Services, Housing, Natural and Cultural Resources

## Slide 21: Lesson 12: Review
  How many hours are between the current location of a hurricane and the first forecast point?
  What is the elapsed time sequence required to run the uncertainty analysis when entering values into Hazus from a forecast advisory?
  What is the conversion factor from nautical miles to miles?

## Slide 22: Questions?