## Slide 1: Lesson 13: Considerations When Reviewing Results

## Slide 2: Lesson 13: Goal and Objectives
Goal: To provide an overview of considerations when reviewing results in the Hazus wind model.
After completing this lesson you will be able to:
  Understand forecast errors for landfalling hurricanes.

## Slide 3: Sources of Uncertainty
Wind Speed Estimates | Only 116 years of storm data Incomplete/noisy observations
Rainfall Model | Simplified model based on limited data
Terrain Roughness | Land use is used to calculate surface roughness. Changes in land use Direction and transition effects.
Load & Resistance Model | Pressure coefficients Missile debris sources & transport Fatigue effects not modeled

## Slide 4: Sources of Uncertainty
Damage-to-Loss Model | Limited validation of implicit loss models | 
Building Stock Distribution | Model building types Incomplete or incorrect inventory data | 
Fast-Running Loss Functions | Average loss as function of peak gust | 
Business Interruption | Analysis parameters based on national averages | 

## Slide 5: Treatment of Uncertainties
  Hazus produces “best estimate results,” but there is no explicit treatment or estimation of uncertainty.
  Potential impact of uncertainties can be assessed through multiple sensitivity analyses.
    Intensity, size, speed, and track of scenario storms
    Distributions of construction characteristics
    Building valuation
    Terrain and tree coverage
    Economic and shelter model parameters

## Slide 6: Uncertainty in Hazus
  As a hurricane approaches landfall, the amount of uncertainty on its landfalling location decreases.
  In Hazus, as you import forecast advisory information (Hurrevac or from NHC) over time in the days before a hurricane landfall, the uncertainty ranges will narrow, indicating it is too close for the hurricane to miss the study region.

## Slide 7: Example: Sensitivity to Wind Speed

## Slide 8: Example: Sensitivity to Terrain

## Slide 9: Ranking of Uncertainties
Smaller storms and/or smaller study regions will generally have greater uncertainties.
  Individual building / single storm
  Regional loss / single storm
  Regional return period losses / probabilistic
  Regional annualized losses / probabilistic
(Ranked from most to least uncertain)

## Slide 10: Real-Time Hurricane Modeling
While hurricane forecasts are improving, errors still exist.
  24 hour forecasts have a positional error of approximately 40 miles.
  When compared to a city or county, this can have major consequences for damage and loss modeling.
https://www.nhc.noaa.gov/verification/verify5.shtml

## Slide 11: Real-Time Hurricane Modeling
Intensity forecasts also have errors: 24 hour forecasts (10 mph)
  120 to 130 mph
    10 mph increase, 8% increase
    WSF1 goes from 10% loss to 25%
  130 to 140 mph
    Changes from 25% to 50% loss
    See Building Loss Function Viewer
While the positional forecasts have improved considerably, the intensity forecasts have remained nearly the same.

## Slide 12: Recommendations
  Understand dependency of modules and analysis parameters.
  Enhance inventory data:
    Building value, square footage, count
    Occupancy mapping schemes
    Wind building characteristics
  Enhance terrain modeling using recent remote sensing data and/or local land use databases.
  Develop local estimates for economic and shelter parameters.
  Run sensitivity cases to see range of results.
  Present results with appropriate caveats.

## Slide 13: Exercise 13.1: Sensitivity of Hurricane Storm Parameters
Goal:
  Modify uncertain and sensitive variables in Hazus.
  Run multiple scenarios.
  Compare the results.
Time: 45 minutes

## Slide 14: Exercise 13.1: Tasks
Task 1: Create an Irma Study Region
Task 2: Run the default landfall track scenario
Task 3: Run the scenario with a modified speed.
Task 4: Run the scenario with a modified size.
Task 5: Run the scenario with a modified intensity.

## Slide 15: Lesson 13: Review
  What are two types of forecast errors for landfalling hurricanes?

## Slide 16: Questions?