## Slide 1: Lesson 2: Hazus Inventory

## Slide 2: Lesson 2: Goals and Objectives
Goal: To provide an overview of the data included with Hazus, emphasizing hurricane-specific inventory, and of the tools and processes to update the data.
After completing this lesson you will be able to:
  Describe the types of aggregate and point inventory supported by the Hazus hurricane model.
  List the options that Hazus provides for updating inventory.

## Slide 3: Inventory Components: Aggregate Inventory
Aggregate Inventory
  Demographics
  General Building Stock broken down by type (how constructed) and occupancy (how used)
Hazard-Specific Inventory (both aggregate and site-specific)

## Slide 4: Inventory Components: Site Specific Inventory
Site-Specific Inventory
Hazard-Specific Inventory (both aggregate and site-specific)

## Slide 5: Inventory Update Tools
State and Study Region Updates
  Comprehensive Data Management System (CDMS)
Study Region Only Updates
  Access databases - use import tools in Hazus
  ArcGIS editing tools
NOTE: E0317: CDMS provides considerably more detail about inventory updates.

## Slide 6: Comprehensive Data Management System
  System for integrating user provided site-specific and aggregate data into the Hazus state databases.
  CDMS supported data includes:
    Site-specific / Aggregate
    Data Types
      xls
      shp
      mdb

## Slide 7: Comprehensive Data Management System
Functions:
  Validates user provided data
  Parses data into appropriate Hazus tables
  Provides historical tracking of database updates
  Can import/export data from/to a variety of formats

## Slide 8: Demographic Data
  Aggregated at census tract (hurricane and earthquake) level
  Detailed by:
    Age
    Income
    Ethnicity
    Ownership
    Gender

## Slide 9: What is the General Building Stock?
An engineering based estimation of buildings for the US represented by:
  Floor area (Sq Ft)
  Value ($)
  Count of all structures by occupancy type
Data Sources:
  Residential: from US Census Data
  Commercial / Industrial: from Dun & Bradstreet

## Slide 10: Aggregate Inventory: General Building Stock
Specific Occupancy Categories
  33 Specific Occupancy Types
  You can view the categories from the Inventory menu
Specific Occupancy | General Occupancy | Description
AGR1 | Agriculture | Agriculture
COM1 | Commercial | Trade
COM2 | Commercial | Wholesale Trade
COM3 | Commercial | Personal and Repair Service
COM4 | Commercial | Professional/Technical Service
COM5 | Commercial | Banks
COM6 | Commercial | Hospital

## Slide 11: GBS: Building Count
Square Footage Factors
  Average square footage for each specific occupancy determined during model development
  Building counts computed by dividing floor area by average square footage
NOTE: RES1 (single family homes) and RES2 (manufactured housing) are derived from census housing unit counts.

## Slide 12: Activity 2.1: Comprehensive Data Management System
Goal: Explore the Comprehensive Data Management System.
Time: 30 minutes

## Slide 13: Activity 2.1: Tasks
Task 1: How to Use CDMS to Update Inventory.

## Slide 14: GBS: Damage States
GBS results for damage can be mapped by occupancy and building type
  Damage represented by damage states (moderate, severe, etc.)
  Damage state values represent the expected fraction of building square footage in each damage state

## Slide 15: General Occupancy Categories
Seven general occupancy classes:
  Majority of Building Stock
1. Residential
2. Commercial
3. Industrial
  Others
4. Agriculture
5. Religion
6. Government
7. Education

## Slide 16: Specific Occupancy Categories
33 Specific Occupancy Types:
  11 Residential Classes
  10 Commercial Classes
  6 Industrial Classes
  2 Government Classes
  2 Education Classes
  1 Agriculture Class
  1 Religious Class

## Slide 17: General Building Types
Five General Building Types:
1. Wood
2. Steel
3. Concrete
4. Masonry
5. Manufactured Housing (Mobile Home)

## Slide 18: General Building Type Mapping
  Mapping Scheme Management:
    View
    Copy
    Edit
    Delete
    Import
    Export

## Slide 19: Aggregated Building Stock
Building Count: By building type

## Slide 20: Specific Building Types (SBT)
Thirty-nine Specific Building Types:
  5 Wood
  9 Steel
  6 Concrete
  14 Masonry
  5 Manufactured Housing (Mobile Home)

## Slide 21: Specific Building Type Mapping
  Mapping Scheme Management:
    View
    Copy
    Edit
    Delete
    Import
    Export

## Slide 22: Hurricane-Specific Inventory
Wind-Building Mapping Schemes
Florida: 4 Regions
Hawaii: 4 Regions
Other States: 4 Regions
  Northeast Inland
  Northeast Coastal
  Southeast Inland
  Southeast Coastal
A map of the different Wind-Building Mapping Schemes for the "Other" states and Florida.

## Slide 23: Hurricane-Specific Inventory
Wind-Building Mapping Schemes
Florida building stock regions
  Different building codes
    Southeast Florida has historically stronger wind provisions for past decade
  Different building practices
    More wood frame in northern portion of Florida than southern Florida

## Slide 24: Hurricane-Specific Inventory
Wind-Building Mapping Schemes
Hawaii Building Stock Regions
  Different wall construction type
    Single wall vs. double wall
  Different roof deck construction
    Metal roof deck
  Different foundation type
  Applies only to single-family models
  All other SBT models are identical to mainland US.

## Slide 25: Hurricane-Specific Inventory: Wind-Building Mapping Schemes
  Eight Mapping Schemes
  Consider:
    Roof type
    Secondary water resistance
    Roof deck attachment
    Roof wall connection
    Shuttering

## Slide 26: Pre-FIRM Sub-Assembly Replacement Values
Reference your manual for the table of Pre-FIRM Sub-Assembly Replacement Values

## Slide 27: Post-FIRM Sub-Assembly Replacement Values
Reference your manual for the table of Post-FIRM Sub-Assembly Replacement Values

## Slide 28: Site-Specific Inventory
  Includes essential facilities, high potential loss facilities, user-defined facilities, transportation systems, utility systems, hazardous material sites
  Represents discrete points of facilities and systems of inventory
  Provides site-to-site results versus an aggregated table of damages and losses

## Slide 29: Essential Facilities
  Fire Stations
  Police Stations
  Schools
  Emergency Operations Centers (EOC)
  Medical Care Facilities

## Slide 30: Essential Facility Classes
Note the links between site-specific and GBS
Class | Category | Description | Occupancy
MDFLT | DEFAULT | Default for Medical | COM6
EFHL | Medical Care | Large Hospital (greater than 150 beds) | COM6
EFHM | Medical Care | Medium Hospital (50 to 150 Beds) | COM6
EFHS | Medical Care | Small Hospital (less than 50 Beds) | COM6
EFMC | Medical Care | Medical Clinics and Labs | COM7
PDFLT | DEFAULT | Default for Police | GOV2
EFPS | Emergency Response | Police Station | GOV2
FDFLT | DEFAULT | Default for Fire Station | GOV2
EFFS | Emergency Response | Fire Station | GOV2
EDFLT | DEFAULT | Default for Emergency Response Facility | GOV2
EFEO | Emergency Response | Emergency Operation Centers | GOV2
SDFLT | DEFAULT | Default for School | EDU1
EFS1 | School | Grade Schools (Primary/High Schools) | EDU1
EFS2 | School | Colleges/Universities | EDU2

## Slide 31: User-Defined Facilities
  Used to perform site-specific analysis of types of buildings found in the General Building Stock
  Required fields for hurricane:
    ID
    Census Tract
    Occupancy
    Wind Building Type
    Wind Building Scheme Name
    Location

## Slide 32: Other Inventory Table Options
  Metadata
  Data Dictionary
  Export
  Map

## Slide 33: Inventory Table Features: Metadata
  Metadata can be accessed through context menu.
  Metadata is essentially reference information.
    Includes description, source, spatial reference, etc.

## Slide 34: Inventory Table Features: Data Dictionary
  The data dictionary can be accessed through the context menu.
  The data dictionary describes the table (name, field definitions, etc.)
  Also used to build a table for import.

## Slide 35: Inventory Table Features: Export
  The option to export can be accessed through the inventory menu.
  Inventory can be exported to two file formats: txt and csv.
    Used to manipulate data outside of Hazus.

## Slide 36: Inventory Table Features: Map
  Click on the column heading to select the field you wish to map.
  Click “Map.”
  Inventory item map layer is created and symbology is automatically populated.

## Slide 37: Exercise 2.2: Comprehensive Data Management System
Goals:
  Update state database using CDMS.
  Create a new study region.
Time: 35 minutes

## Slide 38: Exercise 2.2: Tasks
Part 1: Update State Database
Task 1: Start CDMS and Set State Database to be Updated.
Task 2: Delete Existing Medical Care Facilities in State Database.
Task 3: Import New Medical Care Facilities into CDMS Repository.
Task 4: Transfer Medical Care Facilities to Statewide Database.
Part II: Update the Aggregate Inventory:
Task 1: Import the assessor’s data into the CDMS repository.

## Slide 39: Lesson 2: Review
  What is the purpose of the wind building characteristics distribution mapping scheme?
  What two states have their own set of mapping schemes?
  What types of buildings are considered by Hazus to be essential facilities?
  What is the tool provided by Hazus for updating the state databases?
  What are the only two site-specific dataset groups that are analyzed by the hurricane model?

## Slide 40: Questions?