## Slide 1: Lesson 3: Hurricane Wind Model

## Slide 2: Lesson 3: Goal and Objectives
Goal: To provide an overview of the hurricane wind model within Hazus.
After completing this lesson you will be able to:
  List the key components of hurricane development.
  Describe the areas of the U.S. mainland that have the highest risk to major hurricanes.
  Provide four scenario types that a user can select to run the hurricane model.
  Understand two databases unique to the hurricane model.

## Slide 3: Hurricane Basics
  Rotate counter-clockwise in the Northern Hemisphere
  Require ocean temperatures around 80° F or 27° C or above
  Occurs between 5°N and 40°N in the Atlantic Ocean
  Hurricane season: June 1 through November 30 (Atlantic Basin)

## Slide 4: Tropical System Basics
Type of Tropical Cyclone | Maximum Sustained Winds
Tropical Depression | 38 mph (33 knots) or less
Tropical Storm | 39-73 mph (34-63 knots)
Hurricane Category 1 | 74-95 mph (64-82 knots)
Hurricane Category 2 | 96-110 mph (83-95 knots)
Hurricane Category 3 | 111-129 mph (96-112 knots)
Hurricane Category 4 | 130-156 mph (113-136 knots)
Hurricane Category 5 | 157 mph (137) knots or greater
Tropical Cyclone Category 1 | 77 mph (67 knots) or less
Tropical Cyclone Category 2 | 78-102 mph (68-89 knots)
Tropical Cyclone Category 3 | 103-139 mph (90-121 knots)
Tropical Cyclone Category 4 | 140-173 mph (122-150 knots)
Tropical Cyclone Category 5 | 174 mph (151 knots) or greater
Super Typhoon | 150 mph (130 knots) or greater

## Slide 5: Hurricane Intensity
Saffir-Simpson Hurricane Wind Scale for the Continental United States
http://www.weather.govfos/hurricane/resources/TropicalCyclones11.pdf
Scale Number (Category) | Sustained Winds (MPH) | Typical of Damage Due to Hurricane Winds | Hurricanes
1 | 74-95 | Very dangerous winds will produce some damage: Well-constructed frame homes could have damage to roof, shingles, vinyl siding and gutters. Large branches of trees will snap and shallowly rooted trees may be toppled. Extensive damage to power lines and poles likely will result in power outages that could last a few to several days. | Florence (2018), near Wilmington, North Carolina
2 | 96-110 | Extremely dangerous winds will cause extensive damage: Well-constructed frame homes could sustain major roof and siding damage. Many shallowly rooted trees will be snapped or uprooted and block numerous roads. Near-total power loss is expected with outages that could last from several days to weeks. | Frances (2004) in coastal Port St. Lucie, Florida
3 | 111-129 | Devastating damage will occur: Well-built framed homes may incur major damage or removal of roof decking and gable ends. Many trees will be snapped or uprooted, blocking numerous roads. Electricity and water will be unavailable for several days to weeks after the storm passes. | Irma (2017) second landfall near Marco Island, Florida
4 | 130-156 | Catastrophic damage will occur: Well-built framed homes can sustain severe damage with loss of most of the roof structure and/or some exterior walls Most trees will be snapped or uprooted and power poles downed. Fallen trees and power poles will isolate residential areas. Power outages will last weeks to possibly months. Most of the area will be uninhabitable for weeks or months. | Harvey (2017) near Aransas, Texas
5 | >157 | Catastrophic damage will occur: A high percentage of framed homes will be destroyed with total roof failure and wall collapse. Fallen trees and power poles will isolate residential areas. Power outages will last for weeks to possibly months. Most of the area will be uninhabitable for weeks or months. | Andrew (1992) in coastal parts of Cutler Ridge, Florida

## Slide 6: Hurricane Anatomy
  Rain bands or “feeder bands”
  Eye
  Eye wall
  Counterclockwise rotation
Hurricane Harvey. Source: NOAA
*NOTE: A second outer eye wall may develop, but it can be difficult to differentiate from the inner eye wall.

## Slide 7: Hurricane Anatomy: Symmetry
  Each quadrant is symmetric
  Strongest winds and highest surge (without coastline effects) occur in the right-front quadrant of hurricane
  Forward speed of the hurricane + Rotational winds of the hurricane = highest wind speeds
Image: Satellite image of Celia (2010) Cooperative Institute for Meteorological Studies (CIMSS), University of Wisconsin

## Slide 8: Hurricane Irma, Maria, and Michael
  Hurricane Irma, 2017
    Approaching the coast of Florida
  Hurricane Maria, 2017
    At its strongest point, approaching Puerto Rico.
  Hurricane Michael, 2018
    Making landfall in Florida's Panhandle.

## Slide 9: Hurricane Climatology
Atlantic Hurricane Season:
June 1st – November 30th
Peak of the hurricane season
  Peak September 10th
  Second peak approx. October 15th
Peaks are related to:
  Peak ocean temperatures
  Peak of ideal weather patterns

## Slide 10: Hurricane Geography
  Hurricanes impacting the US mainland often follow one of two general paths:
    Staying in the Atlantic and tracking up the East Coast
    Tracking west of Florida and entering the Gulf of Mexico

## Slide 11: Hurricane Geography
Major hurricane U.S. strikes:
  Florida has the greatest number
  North Carolina, Louisiana, Mississippi, Alabama, and Texas are also high frequency areas

## Slide 12: Hurricane Damages and Losses
Possible hurricane effects:
  Hurricane Winds*
  Hurricane Storm Surge*
  Rainfall / Inland Riverine Flooding*
  Tornadoes
  Rip Currents and High Waves
Hurricane and Tropical Storms winds can extend far inland from the coast.
* Modeled by Hazus

## Slide 13: Additional Hazards
  Tornadoes and severe thunderstorms are common for tropical systems.
  Heavy rainfall produces additional riverine and coastal flooding.
  Hurricane effects are felt much further inland.
Hurricane Harvey (2017) Rainfall

## Slide 14: Additional Hazards
Katrina: approximately 53 tornadoes in 6 states

## Slide 15: Discussion 3.1: Hurricane Hazard
Goal: Review the Hurricane Hazard and the Hazus Hurricane Model.
Groups: 3-5
Time: 15 minutes

## Slide 16: Discussion 3.1: Hurricane Hazard
Questions:
1. What are the implications of not modeling some of the hazards not traditionally generated by a hurricane, such as tornadoes, severe thunderstorms, rip currents?
2. Given what we have seen in the previous slide, where (geographically) in relationship to the hurricane path are communities at greatest risk of a landfalling hurricane?

## Slide 17: Wind Field Model
Solves full non-linear equations of motion for translating hurricane; then establishes parameters for fast running simulation
  Storm asymmetries
  Changing sea-surface roughness
  Air-sea temperature difference

## Slide 18: Components of Hazus Hurricane Wind Model

## Slide 19: Building Damage and Loss Methodology

## Slide 20: Hurricane Model States
  Hurricane model only applies to 23 coastal states
  These are the only states which can be modeled by the Hurricane Wind model AND surge model
  Puerto Rico and US Virgin Islands wind model is in development and may be provided in a future update.

## Slide 21: Components of Hurricane Model
  Hurricane Database/Model
  Inventory with Wind-Specific Features
  Surface Roughness (Terrain) Database*
  Tree Database*
  Damage/Loss/Debris Functions
  Shelter Model
*NOTE: The surface roughness (terrain) and tree databases are unique to the Hurricane model.

## Slide 22: Hurricane Wind Hazard Model: Track
Track Model
  Affecting Gulf Coast, Atlantic Coast, or Hawaii
  Storm curvature
  Multiple landfalls
  Changes in intensity

## Slide 23: Hurricane Wind Hazard Model
Wind Field Model
  Updated version of model used for design wind speeds in ASCE-7-98
  Used in International Building Code Series
  Allows for asymmetries (or unevenly distributed wind fields)
Asymmetric Hurricane Irene - 2011, NOAA

## Slide 24: Hurricane Wind Model Scenarios
 | Probabilistic wind speed database: 100,000 years of simulated storms | Deterministic Historical Forecast/Advisory User-defined

## Slide 25: Damage and Loss Modeling
Damage includes effects of
  Wind pressures
  Wind-borne debris
  Tree blow-down
  Rainfall
  Storm duration
Models damage explicitly to
  Roof cover
  Roof deck
  Whole roof failures
  Window and door failures
  Wall damage
Hurricane Irene (2011) damage in Washington, NC

## Slide 26: Damage and Loss Modeling
Loss model based on:
  Insurance loss data
  Correlation of financial damage with water infiltration and building damage
Current model now includes storm surge:
  Hurricane wind and flooding analysis is coupled
Debris from Hurricane Irma in Marathon, Florida has been scheduled for removal to clear waterway in this canal, which is surrounded by a full time commercial trailer park.

## Slide 27: Fast-Running Damage & Loss Functions
  Includes 1,884 unique building models
  45 damage/loss functions for each building model
  Total of ~240,000 unique damage/loss curves

## Slide 28: Mitigation of Buildings
  Hazus:
    Uses a load and resistance approach to estimate damage and ensuing loss
    Is able to model effects of mitigation
  Hurricane model includes mitigation options for all building types
  Mitigation methods include:
    Addition of hurricane straps
    Application of window protection
    Effects of re-nailing roof sheathing on damage/loss
    Application of secondary water resistance
    Combinations of the above

## Slide 29: Hurricane Wind Simulation
Why Hurricane Categories Make a Difference: https://www.youtube.com/watch?v=lqfExHpvLRY
Why Hurricane Categories Make a Difference – The Weather Channel

## Slide 30: Hurricane Damage Simulation

## Slide 31: Terrain Database
  Surface Roughness = Terrain
    Higher Roughness = Lower Damage (generally)
  Hazus terrain database
    Derived from Land Use Data
      National Land Cover Data (NLCD) database
      Florida Water Management District (FWMD) data
  Roughness parameters averaged for each census tract

## Slide 32: Tree Database
Trees:
  Increases roughness but also increases damage
  Building/content loss
  Debris removal
Tree Coverage Database is derived from:
  MRLC land use coverage database
  Forest Inventory Analysis Database

## Slide 33: Shelter Models
Two estimates for each census tract
  Number of displaced households
  Number of people requiring short-term public shelter
    Function of income class, ethnic class, ownership class, population age class
Similar to model used for earthquake model
  Uses building loss ratios instead of building damage states to estimate proportion of uninhabitable housing units

## Slide 34: Hurricane Loss Estimation Outputs
 | Building damage state probabilities General Building Stock Essential facilities User-defined facilities Capital-related loss ($) Building Contents Income-related losses ($) Relocation Business Income Rental Income Wages | Social losses Displaced households Short-term shelter requirements Debris (tons) Building debris Tree debris Summary reports Inventory Damage Loss

## Slide 35: Activity 3.2: Explore the Inventory
Goals:
  Explore Inventory
Time: 15 minutes

## Slide 36: Activity 3.2 – Explore the Inventory
Task 1: Explore the General Building Stock (GBS) inventory.

## Slide 37: Lesson 3: Review
  What are the key components for hurricane development?
  What areas of the US mainland have the highest risk to major hurricanes?
  List four scenario types that a user can select to run the hurricane model.
  Which two databases are unique to the hurricane model?

## Slide 38: Questions?