## Slide 1: Lesson 4: Deterministic Storm Parameters

## Slide 2: Goal and Objectives
Goal: To provide an overview of the set of storm scenarios available to users in Hazus.
After completing this lesson, you will be able to:
  Describe the Historical Scenario options.
  Understand the process for creating a user-defined scenario in Hazus.
  Discuss the differences in the probabilistic analyses in Hazus.

## Slide 3: Scenario Operations
Hazus has six choices for defining hurricane scenarios:
  Historic
  Probabilistic
  Create New:
    Define Storm Track Manually
    Import from Exported File (storm created in previous Hazus Study Region)
    Import Census Tract Data File
    Import a Hurrevac Storm Advisory

## Slide 4: Hurricane Scenario Definition Options

## Slide 5: Determining Risk
Typically the risk of hazard occurrence is translated into a probabilistic recurrence interval (e.g., 1% annual change or 100-year event).
Two approaches:
  Historic record
  Modeling methods

## Slide 6: Using the Historic Record for Risk
Recurrence Interval = (n+1)/m
  n: number of years on record
  m: rank of the event being considered
When a good historical record exists, the Recurrence Interval and its annual chance probability can be computed.
Year | Maximum Winds (kt) | Rank | Recurrence Interval
1989 | 120 | 3 | 7.00
1991 | 90 | 8 | 2.63
1992 | 145 | 1 | 21.00
1993 | 100 | 6 | 3.50
1995 | 100 | 6 | 3.50
1996 | 100 | 6 | 3.50
1997 | 70 | 12 | 1.75
1998 | 95 | 7 | 3.00
1999 | 100 | 6 | 3.50
2002 | 80 | 10 | 2.10
2003 | 90 | 8 | 2.63
2004 | 130 | 2 | 10.50
2005 | 110 | 5 | 4.20
2007 | 80 | 10 | 2.10
2008 | 95 | 7 | 3.00
2011 | 75 | 11 | 1.91
2012 | 70 | 12 | 1.75
2014 | 85 | 9 | 2.33
2016 | 75 | 11 | 1.91
2017 | 115 | 4 | 5.25

## Slide 7: Using the Historic Record for Risk
Potential Problems:
  The historic record has a short timescale (e.g. Atlantic hurricane records collected from 1851-2019 and Northeast and North Central Pacific hurricane records collected from 1949-2019).
    This map shows the total number of hurricane strikes by county from 1900-2010.
  Some hazards have wide geographic variations.
    EX: County X has been missed by landfalling hurricanes since 1900, but adjacent County Y has had 14.

## Slide 8: Historic Storm Scenario
Potential Problems:
  Pre-computed wind fields and storm tracks
  Only storms that affected the study region can be selected

## Slide 9: Historic Storm Region Filter
  Region Filter button: Filters to select only the storms in which the storm track intersects the study region.
  Peak Gust: Largest modeled gust speed over land anywhere in US.

## Slide 10: Exercise 4.1: Historic Scenarios
Goal:
  Create multiple historic storm scenarios
  Review the results
Time: 45 minutes

## Slide 11: Exercise 4.1: Tasks
Task 1: Open the Region and Define a Historic Scenario.
Task 2: Run the Analysis.
Task 3: View the Results.

## Slide 12: User-Defined Scenario
  Import from
    Hurrevac
    .dat file
    Exported file (other Hazus users)
  Define manually*
*Define manually should only be used if data are not available anywhere else, including Hurrevac.

## Slide 13: Hurricane Data Sources: Hurrevac
  HURRicane EVACuation – storm tracking and decision support tool developed off Hurricane Evacuation Studies and NHC data.
  Translates forecast track and wind extent information from NHC text-based products into interactive maps and produces storm files.
  Best available data for Hurricane Wind Loss estimation prior to landfall and until observed wind fields are developed.
  Direct dynamic link within Hazus
  Hurrevac can be used to create exercise scenarios

## Slide 14: Hurrevac Import
  Hurrevac data is integrated into the Hazus interface
  Click on the hurricane of interest and click "Next"

## Slide 15: Hurrevac Download
  Hazus is dynamically linked to Hurrevac FTP site to provide real-time data availability
  Advisories are available in Hazus as they become available in Hurrevac
  Searching for the year and first letter of the storm's name will provide download options
  Continuous update of advisories is crucial during response phase
  Make sure to click the refresh button before selecting the updated Hurrevac advisory for an active storm

## Slide 16: Activity 4.2: HURREVAC Scenario – Hurricane Harvey
Goals:
  Import Hurricane Harvey data using HURREVAC.
Time: 10 minutes

## Slide 17: Activity 4.2: Tasks
Task 1: Import the HURREVAC file.

## Slide 18: Import Census Tract Data File
  User-defined scenario option.
  Import a hurricane wind data file in the .dat format with information at the census tract level.
  Storm track data table will not populate because wind speeds are assigned to census tracts directly.
  Also known as H*Wind.

## Slide 19: Exercise 4.3: Harvey .dat Model
Goals:
  Create a scenario with .dat data.
Time: 15 minutes

## Slide 20: Exercise 4.3: Tasks
Task 1: Create a scenario from a .dat file.

## Slide 21: Import from Exported File
  User-defined scenario type
  Previously saved file from prior Hazus run
  Default name will be the date of import but scenario can be renamed
  Storm track input
  Wind field calculation will run before activating the scenario

## Slide 22: Exercise 4.4: Importing .bin Files
Goal:
  Import Hurricane Irma data using a .bin file.
Time: 10 minutes

## Slide 23: Exercise 4.4: Tasks
Task 1: Create the Study Region.
Task 2: Import the .bin File.

## Slide 24: Define Storm Track Manually
How fast is the storm moving?
  Elapsed time for each point along the storm track
  Forward translation speed of the storm at each point
What is the size of the storm?
  Radius to maximum winds
  Radius to hurricane force (64kt, 50kt, or 34kt winds)
What is the intensity of the storm?
  Maximum wind speed
  A Holland B profile parameter
NOTE: Answers to these questions will depend on the format of the information you have.

## Slide 25: Parameters - Translation Speed
How fast is the storm moving?

## Slide 26: Translation and Rotation Speeds
Increase in rotation speed means different % increase on right and left side of storms.
For example below:
  10 mph increase in rotation speed (100 to 110 mph)
  8% increase in windspeed on right side of storm (120 to 130 mph)
  12% increase in windspeed on left side of storm (80 to 90 mph)

## Slide 27: Converted Wind Speeds
Typical Storm Parameters
1 min mean = Hazus Input Windspeeds 3 sec gust = Hazus Output Windspeeds
Saffir Simpson Scale | 1 Min Mean (mph) | 3 sec Gust (mph) | Min Central Pressure (mb)
1 | 74-95 | 90-116 | 980 and up
2 | 96-110 | 117-134 | 965-979
3 | 111-129 | 135-159 | 945-964
4 | 130-156 | 160-189 | 920-944
5 | 157+ | 189+ | 920 and below

## Slide 28: Parameters: Storm Size
Radius to max winds and radii can be adjusted in the settings.xml

## Slide 29: Parameters: Storm Intensity
Maximum Wind Speed
Profile Parameter (B)
  Parameter that describes the rate of pressure drop in the storm
  Pressure drop determines the maximum wind speed

## Slide 30: Typical Storm Parameters
Hurricane and Station | Measured Peak Gust at 10m (m/sec) | Anemometer Height (m) | Wind Speed Averaging Time (sec) Mean | Wind Speed Averaging Time (sec) Gust | Holland's B Parameter | Radius to Maximum Winds (km)
Fran (1996), FPSN7 | 48.3, 37.7 | 44.2 | 600 | 5 | .95 | 85
Fran (1996), DSLN7 | 29.6 | 46.6 | 600 | 5 | .95 | 85
Bertha (1993), FPSN7 | 45.1 | 44.2 | 600 | 5 | 1.2 | 70
Emily (1993) DSLN7 | 51.0, 56.7 | 46.6 | 600 | 5 | 1.7 | 39
Andrew (1992), NGW LMS | 58.6 | 13.7 | 120 | 5 | 1.6 | 19
Bob (1991), 41001 | 30.6 | 5.0 | 600 | 5 | 1.4 | 35
Hugo (1989), FPSN7 | 31.7 | 42.2 | 600 | 5 | 1.0 | 40

## Slide 31: Storm Track Definition
  Manually enter storm parameters

## Slide 32: Hurricane Data Sources: Hurdat
  Good to manually define storm track
  National Hurricane Center’s HURricane DATabase: https://www.nhc.noaa.gov/data/#hurdat
    Enhanced collection of historical meteorological data
  HURDAT2: Best Track Data
    Atlantic and Pacific
    Comma-delimited, text format
    Six-hourly information on location, maximum winds, central pressure, and size of all known tropical and subtropical cyclones

## Slide 33: Show Current Scenario
Select Hazard > Show Current

## Slide 34: Lesson 4: Review
  What are the deterministic options for hurricane scenarios in Hazus?
  Where (geographically within a hurricane) are the greatest hurricane windspeeds located and why?

## Slide 35: Questions?