## Slide 1: Lesson 5: Probabilistic Storm Parameters

## Slide 2: Goal and Objectives
Goal: To provide an overview of the set of probabilistic storm scenarios available to users in Hazus.
After completing this lesson, you will be able to:
  Discuss the differences in the probabilistic analyses in Hazus

## Slide 3: Scenario Operations
Hazus has six choices for defining hurricane scenarios:
  Historic
  Probabilistic
  Create New:
    Define Storm Track Manually
    Import from Exported File (storm created in previous Hazus Study Region)
    Import Census Tract Data File
    Import a Hurrevac Storm Advisory

## Slide 4: Probabilistic vs. Deterministic
Probabilistic wind speed database (Left)
  100,000 years of simulated storms
Individual Storms (Right)
  Historical
  Forecast/Advisory
  User-defined

## Slide 5: Modeling Risk
  The hurricane wind model was run to simulate 100,000 hurricane seasons.
    Storms can vary in size, strength, speed, direction
  Provides objective way to compare risk of different areas

## Slide 6: Probabilistic Windspeeds
  The probabilistic windspeeds in the Table of Contents window (next slide) show the overall wind risk to the US and are the same windspeeds as in Figure 4.28
  These layers were created from the 100,000 years worth of simulated storms.
  Windspeeds were ranked for each tract and recurrence intervals were determined.
Figure 4.28 in Hurricane Technical Manual

## Slide 7: Probabilistic Windspeeds (Cont'd.)
These layers answer the question:
  What is the windspeed for this tract that equates to a given recurrence interval?
  For example, 115 MPH winds for tract 12103024901 for the 1% annual chance

## Slide 8: Probabilistic Windspeeds
  For an actual hurricane:
    Windspeeds are not uniform across the storm.
    Windspeeds are higher at eyewall and lower farther away.
  Using these layers:
    Assume the recurrence interval (100 year) at every location in the study region
    Good for building codes, but may not be best for planning

## Slide 9: Probabilistic Scenario: Scenario Driven
  Table of Contents windspeed probabilities should not be confused with the probabilistic scenario.
  Table of Contents layers:
    Provide communities with the recurrence interval windspeed for each tract.
  Probabilistic scenario:
    Provide communities with a representative recurrence interval event based on loss for the study region.
    Losses are representative of the specific event, not the recurrence interval windspeeds.

## Slide 10: Probabilistic Scenario: Scenario Driven
For planning purposes:
  A community needs to understand damages and losses from an actual hurricane for each recurrence interval.
  This method answers questions such as "What would the damages and losses be for our community from a return period (e.g. 100-year) hurricane event?"

## Slide 11: Probabilistic Scenario: Scenario Driven
  Hazus searches through 100,000 year simulated database for all storms that intersect the study region.
  The total losses for the region based on each storm are ranked.
  Loss is selected, then the hurricane event is used to generate damages and losses.

## Slide 12: Seven Return Period Events
Events Sorted by Total Loss for the study region

## Slide 13: Discussion 5.1: 500-Year Event
Goal: Discuss the windspeed distribution for this 500 year event.
Time: 5 minutes

## Slide 14: Discussion 5.1: 500-Year Event
Discuss the windspeed distribution for this 500 year event.
  Where do you expect the highest and lowest losses?
  Is every Census tract experiencing a 500 year event (individually)?

## Slide 15: Outputs: Return Period Event
Seven Return Period Events
  Seven single storm scenarios from 100,000 year storm database
  Representation of the return period losses for study region: 10, 20, 50, 100, 200, 500, 1,000 years
  Return periods are based on total direct economic loss for entire study region
Full set of results provided
  Damage, debris, shelter, etc.
  Dollar losses

## Slide 16: Study Region Characteristics & Losses
There are many different ways to produce a 100-year loss for a given study region.
*These very different storms can produce identical dollar losses for the same study region.

## Slide 17: Study Region Characteristics & Losses
Even though both of these study regions contain Charlotte County, Florida, they will have very different probabilistic scenarios because the events are selected by finding all probabilistic events that intersect the study region and ranked based upon the losses to the study region.

## Slide 18: Uses of Probabilistic Layers
Wind speed Maps in Table of Contents window
  Mitigation plan: identifies the windspeed each location individually plans for with respect to each probabilistic interval (10 yr, 100 yr, etc.)
  Construction design: identifies the windspeed buildings should be able to withstand
NOTE: Wind building characteristics distributions can model changes in construction wind resistance.

## Slide 19: Uses of Probabilistic Layers
Probabilistic Event Scenarios
  Layers used in mitigation and planning situations to understand overall losses to the jurisdiction for each recurrence interval event.
  Demonstrate the damages and losses if an actual hurricane affected the area
  Example: debris planning, sheltering planning, and response and recovery exercises

## Slide 20: Probabilistic Losses
Building Economic Losses
  Seven Return Period Events
  Annualized: the estimated long-term value of losses to the general building stock averaged on an annual basis for a specific hazard type
All other results
  Seven Return Period Events

## Slide 21: Exercise 5.2: Probabilistic Scenario
Goal: Run a Probabilistic Scenario.
Time: 45 Minutes

## Slide 22: Exercise 5.2: Tasks
Task 1: Open the Region and Define a Probabilistic Scenario.
Task 2: Run the Analysis.
Task 3: View the Results.

## Slide 23: Annualized Hurricane Loss (AHL)
  The expected value of future losses averaged on an annual basis
  Formula expression
    m = events
    n = years
  Formula description
    Sum of expected loss for each event, divided by number of years in simulation (n= 100,000 years)
  Uses
    Fundamental measure of the risk for mitigation strategy
    Unbiased basis for relative ranking and resource allocation
    Benefit-cost analysis of mitigation options

## Slide 24: Annualized Hurricane Loss (AHL)
Annualized Hurricane Losses are provided for
  Building Economic losses ($)
  Output and Employment losses ($)
Not provided for
  Damage
  Debris
  Shelter
Called "Annualized" in direct economic results tables

## Slide 25: Probabilistic Return Intervals vs. AHL
  Probabilistic scenarios work inherently different from event based AHL estimates
    Probabilistic scenarios look at a specific return interval
    AHL looks at all potential events and is a combined value of events and years
    Probabilistic scenarios are not calculating the impact of an event in all regions; it is specific to whatever is defined

## Slide 26: Review
  Where can you find the two different types of probabilistic datasets?
  What return periods are used in probabilistic hurricane scenarios in Hazus?

## Slide 27: Questions?