## Slide 1: Economic Loss Methodology

## Slide 2: Lesson 6: Goal and Objectives
Goal: To provide an overview of the damage and loss methodology for hurricane wind models in Hazus.
After completing this lesson you will be able to:
  Discuss the wind damage and loss methodology in Hazus.

## Slide 3: The Building Envelope
  Damages and losses begin with the building envelope performance, the amount of resistance to hurricane force winds.
    Walls
    Roofing
    Windows
    Doors
  Failures to these components lead to more extensive damage.
Mitigation Assessment Team Report: Hurricane Ivan in Alabama and Florida (FEMA 489)

## Slide 4: Sub-Assembly Inventory Wind Model
  Sub-assembly cost ratios separate the individual building components.
  Represents the percentage of the replacement cost for each component
    EX: if Hazus modeled a roof 100% damaged on a $100,000 one story residential structure, the total loss would be $3,000.
Table of Default Residential Subassembly Cost Ratios
Hurricane winds do not affect all components equally, and therefore individual components must be modeled
Subassembly | 1 Story | 2 Story | 3 Story
Site Work | 1% | 1% | 1%
Foundation | 13% | 8% | 5%
Framing | 13% | 11% | 14%
Exterior Wall | 22% | 25% | 26%
Roofing | 3% | 2% | 1%
Interiors | 32% | 38% | 39%
Specialties | 4% | 4% | 4%
Mechanical | 9% | 8% | 7%
Electrical | 3% | 3% | 3%
Total | 100% | 100% | 100%

## Slide 5: Sub-Assembly Inventory Flood Model
  Sub-assembly cost ratios were created for the surge model for combined losses.
  5 categories were created, but they are different than the hurricane model.
  Therefore the hurricane sub-assemblies were aggregated into the same 5 categories, which prevents double counting of losses.
Pre-FIRM
Specific Occupancy or General Building Type | Foundation | Below First Floor | Structure Frame | Roof Covering | Roof Framing | Exterior Wall | Interiors | Total
RES1: Single | 6% | 2% | 13% | 5% | 5% | 20% | 49% | 100%
RES2: MH | 6% | 2% | 10% | 3% | 5% | 20% | 54% | 100%
RES3A: Duplex | 6% | 2% | 13% | 5% | 5% | 20% | 49% | 100%
RES3B: 3-4 Units | 6% | 2% | 13% | 5% | 5% | 20% | 49% | 100%
RES3C: 5-9 Units | 5% | 1% | 10% | 2% | 3% | 10% | 69% | 100%

## Slide 6: Sub-Assembly Inventory Flood Model
Post-FIRM
Specific Occupancy or General Building Type | Foundation | Below First Floor | Structure Frame | Roof Covering | Roof Framing | Exterior Wall | Interiors | Total
RES1: Single | 11% | 3% | 10% | 5% | 5% | 19% | 47% | 100%
RES2: MH | 8% | 2% | 10% | 3% | 5% | 20% | 52% | 100%
RES3A: Duplex | 11% | 3% | 10% | 5% | 5% | 19% | 47% | 100%
RES3B: 3-4 Units | 11% | 3% | 10% | 5% | 5% | 19% | 47% | 100%
RES3C: 5-9 Units | 10% | 1% | 9% | 2% | 3% | 9% | 66% | 100%

## Slide 7: Damages from Hurricane Winds
  Wind pressure: the effect of the force of the wind on a building
  Windborne Debris (Missiles): damage caused by building debris being airborne and damaging other structures
  Roof types are referred to as “ballasted.”

## Slide 8: Damages from Hurricane Winds
Duration: longer durations (more damage) vs. shorter durations (less damage) of hurricanes when the windspeeds are equal
Rainfall: after roofing materials or openings fail, water can damage the inside of a structure
Atmospheric pressure: difference in atmospheric pressure causing damage

## Slide 9: Damage States
Damage results are reported by average percentage of buildings in each damage state:
  None
  Minor
  Moderate
  Severe
  Destruction
Damage state:
  Function of amount of damage to key components

## Slide 10: Damage States
  Different damage state definitions for each building type
  See the Hazus Hurricane Model Technical Manual
Damage States for Residential Construction Classes
Damage State | Qualitative Damage Description | Roof Cover Failure | Window Door Failures | Roof Deck | Missile Impacts on Walls | Roof Structure Failure | Wall Structure Failure
0 | No Damage or Very Minor Damage Little or no visible damage from the outside. No or very limited water penetration. | Less than or equal to 2% | No | No | No | No | No
1 | Minor Damage Moderate roof cover loss that can be covered to prevent additional water entering the building. Marks or dents on walls requiring painting or patching for repair | Greater than 2% and less than or equal to 15% | One window, door, or garage door failure | No | <5 Impacts | No | No

## Slide 11: Damage States
  Different damage state definitions for each building type
  See the Hazus Hurricane Model Technical Manual
Damage States for Residential Construction Classes
Damage State | Qualitative Damage Description | Roof Cover Failure | Window Door Failures | Roof Deck | Missile Impacts on Walls | Roof Structure Failure | Wall Structure Failure
2 | No Damage or Very Minor Damage Little or no visible damage from the outside. No or very limited water penetration. | >15% and less than or equal to 50% | Greater than 1 and less than or equal to the larger of "20%" and "3" | 1 to 3 panels | Typically 5 to 10 impacts | No | No
3 | Severe Damage Major window damage or roof sheathing loss. Major roof cover loss. Extensive damage to interior from water. | >50% | greater than the larger of "20%" and "3" and less than or equal to 50% | >3 panels and Less than or equal to 25% | Typically 10 to 20 impacts | No | No
4 | Destruction Complete roof failure and/or failure of wall frame. Loss of more than 50% of roof sheathing. | Typically > 50% | >50% | >25% | Typically >20 impacts | Yes | Yes

## Slide 12: Examining Damage and Loss Curves
Analysis Menu
  Damage
  Loss
  Loss of use
  Debris

## Slide 13: Damage Curve Viewer
  Select a Building Type
  Click to Select different parameters
  For 140 mph speed, there is a 35 percent chance that the building will have at least severe damage

## Slide 14: Four Curve Viewers
  Building Damage
  Building Loss
  Building Loss of Use
  Debris

## Slide 15: Demonstration 6.1: Curve Viewers
Goal: Review and discuss curve viewers
Time: 10 minutes

## Slide 16: Tree Blow-Down Model
Tree effects during wind storms:
  Positive
    Provide shelter to structures
    Reduces wind pressure
  Negative
    Falling trees produce strike hazard to structure
    Fallen trees add to amount of debris to dispose of after storm

## Slide 17: Tree Model

## Slide 18: Hazus Tree Coverage Database
Tree Inventory Database is derived from: Multi-Restoration Land Consortium (MRLC) land use coverage database Same data used for terrain database Forest Inventory Analysis (FIA) Database Developed by U.S. Forest Service (USFS) Updated every 5 years Nationwide inventory by species Field survey and statistical analysis Contains tree count and tree diameter distribution | 

## Slide 19: Tree Database in Hazus
Tree types
  Deciduous
  Coniferous
  Mixed Tree Density (stems per acre)
Tree height
  Distribution between 3 broad categories:
    30 - 40 ft
    40 - 60 ft
    60 + ft

## Slide 20: Damage Resulting from Trees
Simulations of amount of damage:
  Tree drop tests at Clemson University
  Derived relationship of impact energy and damage severity
  Cost estimated using data from RSMeans 2018

## Slide 21: Tree Damage from Hurricane Irma (2017)
Hazus tree model accounts for different types of tree damage that may occur.
Photo taken in Gospel Island, FL after Hurricane Irma, September 2017

## Slide 22: Loss Curves as Function of Tree Density

## Slide 23: Loss Curves as Function of Tree Height

## Slide 24: Loss Curves as Function of Tree Type

## Slide 25: Exercise 6.2: Surface Roughness
Goal:
  Modify the surface roughness parameters in order to see the effect on the damages and losses.
Time: 30 minutes

## Slide 26: Exercise 6.2: Tasks
Task 1: Define the default scenario.
Task 2: Adjust the Surface Roughness to a Rural setting.
Task 3: Adjust the Surface Roughness to an Urban setting.
Task 4: View and Compare Results.
Task 5: Restore the Census Tract to the default setting.

## Slide 27: Lesson 6: Review
  What parameters define the Hazus wind damage models?
  How does Hazus display damage curves?

## Slide 28: Questions?