## Slide 1: Lesson 8: Economic Loss Methodology

## Slide 2: Lesson 8: Goal and Objectives
Goal: To provide an overview of the economic loss methodology in the hurricane wind model.
After completing this lesson you will be able to:
  Discuss the economic loss outputs.
  Understand the parameters associated with this methodology.
  Describe the appropriate use of these outputs.

## Slide 3: Direct Economic Loss Outputs
 | Building Loss Contents Loss Business Inventory Loss Relocation Expense Loss of Income Rental Income Wage Income Output Loss Employment Loss | 

## Slide 4: Building/Content Loss Model: Development
  Physically-based damage-to-loss model
  Computes direct economic losses using
    Explicit costing
      Windows, doors, sheathing, roof cover, etc.
    Implicit costing
      Estimates of volume of water entering through failed windows, doors, etc.
  Details of loss models found in Section 8 of the Hurricane Technical Manual

## Slide 5: Loss Model
Hazus loss models are based upon building types:
  Residential
    Exterior vs. interior losses
  Manufactured homes
    Includes damage to foundation and frame
    Includes serviceability replacements (85% of ultimate capacity)
  Commercial buildings
    Total cost distributed differently
    Sub-assembly costs used instead of unit costs

## Slide 6: Residential Damage-to-Loss Methodology

## Slide 7: Loss of Use
  Building Loss Ratio: Loss to the building divided by the replacement cost of the building.
  Building loss ratio is used as an indicator of reconstruction time.
  A multiplier is applied to the total reconstruction time to determine the loss of use to a structure.
Occupancy | 0% Building Loss Ratio | 2% Building Loss Ratio | 10% Building Loss Ratio | 50% Building Loss Ratio | 100% Building Loss Ratio
RES1 | 0 | 0 | 0.5 | 1 | 1
COM1 | 0.05 | 0.1 | 0.1 | 0.3 | 0.4

## Slide 8: Loss of Use
Loss of Use Multiplier
  Reflects ability of business to relocate and thus minimize impact on income loss
  At low levels of loss, business continues to operate in existing facility
  At high levels of loss, business will decide to relocate and resume operation

## Slide 9: Loss of Use Model

## Slide 10: Business Inventory Losses
  Function of contents loss ratio and square footage
  Estimated for following occupancies:
    COM1: Retail Trade
    COM2: Wholesale Trade
    IND1: Heavy
    IND2: Light
    IND3: Food/Drugs/Chemicals
    IND4: Metals/Minerals Processing
    IND5: High Technology
    IND6: Construction
    AGR1: Agriculture
INV = FA x SALES x BI x CL
  FA: Floor Area
  SALES: Annual gross sales per square foot
  BI: Business Inventory %
  CL: Content Loss Ration (0-1)

## Slide 11: Business Inventory Losses
  National Averages
    May not apply to your community
    Updates can be obtained from U.S. Department of Commerce’s Bureau of Economic Analysis or local state.

## Slide 12: Discussion 8.1: Loss Estimates
Goal: Participate in a class discussion about loss estimates.
Time: 10 minutes
Questions:
1. How are loss of use estimates and business inventory losses used in mitigation planning or response and recovery planning?
2. Where are potential sources from which we might obtain credible values to put in the analysis tables?

## Slide 13: Rental Income Loss
Addresses the remainder of population in census tract that is not owner-occupied.
RYi = FAi x (1-00%i) x RENTi x LOUi
FAi = Floor Area 1-00%i = % of Renter-Occupied RENTi = RENT (sq.ft/day) LOUi = Loss of Use in Days

## Slide 14: Relocation Loss
Costs associated with moving out of an unusable building:
  Disruption costs: cost of shifting business to new facility
  Rental costs: cost of renting new facility while old facility is repaired
Assumptions:
  Building owners incur expense of moving tenants
  Renter has no new rental expenses
  The following occupancies will not relocate
    COM8: Entertainment & Recreation
    COM9: Theaters
    COM10: Parking
    IND1: Heavy Industry

## Slide 15: Relocation Loss
RELi = FAi x DCi x pi(damage > Minor) + FAi x 00%i x RENTi x LOUi
FAi = Floor Area DCi = Disruption cost per square foot pi(damage > Minor) = Fractino of buildings with damage state of at least moderate 00%i = % of Owner-Occupied RENTi = RENT (sq.ft/day) LOUi = Loss of Use in Days

## Slide 16: Loss of Income
  Business income (profit) loss occurs when building damage disrupts economic activity.
  Data is based on IMPLAN system from U.S. Department of Commerce Bureau of Analysis.
YLOSi = (1-RFi) x FAi x INCi x LOUi x MODi
RFi = Recapture Factor FAi = Floor Area INCi = Income per day (per sq. ft.) LOUi = Loss in Use in Days MODi = Loss of Use Multiplier

## Slide 17: Loss of Income
Occupancy | Description | Recapture Factor
RES1 -3 | Private Residences | 0
RES4 -6 | Hotel/Motel Institutions | 0.6
COM1 -2 | Retail/Wholesale Trade | 0.87
COM3 | Personal & Repair Service | 0.51
COM4 -5 | Financial | 0.9
COM6 -10 | Hospital, Entertainment, Parking | 0.6
IND1 -6 | Industrial | 0.98
AGR1 | Agricultural | 0.75
EDU1 | Education | 0.6
EDU2 | College/university | 0.6
GOV1 | General Service | 0.8
GOV2 | Emergency Response | 0
REL1 | Churches | 0.6

## Slide 18: Wage, Employment, and Output Losses
Same as business income loss:
LOSSi,n = (1-RFi) x FAi x INCi x LOUi x MODi
Replace INCi with:
Wage Losses: WAGEi = $/SF/day Employment Losses: EMPLOYi = work day/SF/day Output Losses: OUTPUTi = $/SF/day

## Slide 19: Loss Model Validation
  Comparison to insurance claim data
  Five sets of insurance loss data from three insurance companies
    Bhinderwala (1995)
    Two proprietary data sets

## Slide 20: Loss Model Validation

## Slide 21: Loss Model Validation: Comparison
Validation completed by performing analysis of specific storms:
  Hurricane Andrew
  Hurricane Hugo
  Hurricane Erin
  Hurricane Opal
Simulation:
  Wind field and wind loads
  Terrain model
  Damage, loss models
  Inventory

## Slide 22: Loss Function Viewer

## Slide 23: Exercise 8.2: Economic Loss Parameter
Goals:
  Run a historical scenario.
  Modify the economic loss parameters.
Time: 60 minutes

## Slide 24: Exercise 8.2: Tasks
Task 1: Run the default Historic Hurricane Michael Scenario.
Task 2: Modify Annual Gross Sales Parameter.
Task 3: Modify the Business Inventory Parameter.
Task 4: Modify the Rental and Disruption Costs Parameter.
Task 5: Modify the Percent Owner Occupied Parameter.
Task 6: Modify the Wages and Capital Related Income Parameter.
Task 7: Compare the Results of Modifying the Economic Loss Parameters.

## Slide 25: Lesson 8: Review
  Why are the Building Loss of Use results important for planning?
  Where can you find the input parameters that determine the economic loss results?
  What confidence should you place on results that use the default inputs for economic losses? Why?

## Slide 26: Questions?