## Slide 1: Lesson 9: Shelter and Debris Models

## Slide 2: Lesson 9: Goal and Objectives
Goal: To describe the shelter and debris models.
After completing this lesson, you will be able to:
  Understand the shelter and debris parameters.
  Demonstrate how to modify the parameters.

## Slide 3: Shelter Model
Follows model used for earthquake hazard.
  Uses building loss ratios instead of building damage states to estimate proportion of uninhabitable housing units
Two estimates for each census tract
  Number of displaced households
  Number of people requiring short-term public shelter
    Function of income class, ethnic class, ownership class, population age class
NOTE: Discussed in Technical Manual (Chapter 11)

## Slide 4: Shelter Model Methodology
Step 1: Estimate number of uninhabitable households resulting from wind damage.
  Mean loss ratio (loss/building value) used to predict fraction of uninhabitable units
  Function derived from simulations of damage and loss for single-family and multi-family buildings
  Analyzed for each census tract

## Slide 5: Shelter Model Methodology
Step 2: Calculate number of displaced households.
  Add displaced houses from previous step
  Multiply by occupancy rate
    Estimated from census data
Step 3: Repeat for each census tract.

## Slide 6: Shelter Model Methodology
Step 4: Estimate number of people in shelters.
  Based on fraction of displaced households

## Slide 7: Shelter Estimates: Weighting Factors
  Same factors as earthquake model
  Defaults to only income and ethnicity affecting shelter estimates

## Slide 8: Shelter Estimates: Income Weighting Factors
Proportion of people in a given class that will go to a public shelter:
Excerpt of Table 11.2-2 for Household Income weighting factors
Symbol | Description | Default Value
(Fi)1 | Income < $10000 | 0.62
(Fi)2 | $10000 < Income < $15000 | 0.42
(Fi)3 | $15000 < Income < $25000 | 0.29
(Fi)4 | $25000 < Income < $35000 | 0.22
(Fi)5 | $35000 < Income | 0.13

## Slide 9: Shelter Estimates: Ethnicity Weighting Factors
Excerpt of Table 11.2-2 for Ethnicity weighting factors
Symbol | Description | Default Value
(Fe)1 | White | 0.24
(Fe)2 | Black | 0.48
(Fe)3 | Hispanic | 0.47
(Fe)4 | Asian | 0.26
(Fe)5 | Native American | 0.26

## Slide 10: Shelter Estimates: Weighting Factors
Weight factor is a product of two sets of factors
  Weighting Factors
  Modification Factors

## Slide 11: Debris Model
Eleven categories of debris resulting from wind events (Public Assistance Program and Policy Guide, 2018):
  Vegetative Debris
  Construction and Demolition Debris
  Hazardous Waste
  Household Hazardous Waste
  White Goods
  Electronic Waste
  Soil, Mud, and Sand
  Vehicles and Vessels
  Putrescent Debris
  Infectious Waste
  Chemical, Biological, and Nuclear – Contaminated Debris
NOTE: Chapters 10 and 12 in the Hurricane Model Technical Manual

## Slide 12: Building Debris Model
Development of debris curves
  Based on load-resistance damage states
  Component unit weights
  Typical density of debris type
  Debris type distribution of damaged components

## Slide 13: Component Unit Weight
  Exterior building components: Weights from RS Means 2018
  Interior building components: Weights from RS Means 2018
  Contents: Estimated based on sustained live loads from ASCE 7-98

## Slide 14: Viewing Building Debris Curves
  Each specific building type has a set of debris functions related to terrain.
  Rougher terrains: Less building debris

## Slide 15: Debris Model: Validation
  Statistics reported in published papers
  Limitations of comparisons
    Hugo South Carolina comparison region may be larger than assumed from paper
  Hazus debris model = ~ +/- 30%
Storm | Region | Actual Weight (tons) | Actual Volume (cubic yards) | Modeled Weight (tons) | Modeled Volume (cubic yards) | Model/Actual Weight | Model/Actual Volume
Hugo | South Carolina | - | 15,500,000 | 951,009 | 9,130,843 | - | 0.59
Hugo | USACE Admin. Region | - | 4,589,559 | 782,480 | 7,366,394 | - | 1.61
Andrew | Dade County | 2,900,000 | 40,000,000 | 3,396,991 | 35,323,080 | 1.17 | 0.88

## Slide 16: Tree Debris Model
  Estimates based on
    Tree coverage database
    Tree blow-down model
  Expected green weight of tree stems for trees greater than 30 ft. tall
  Eligible tree debris
    Debris estimates made for all areas.
    Unpopulated areas may not be collected.
  Volume based on 10 cubic yards / ton.

## Slide 17: Demonstration 9.1 – Shelter and Tree Parameters
Goal:
  Show how to view shelter and tree parameters
Time: 10 Minutes

## Slide 18: Exercise 9.2: Tree and Sheltering Parameters
Goal:
  Explore the impact of altering tree and sheltering parameters.
Time: 45 Minutes

## Slide 19: Exercise 9.2: Tasks
Task 1: Open the Study Region
Task 2: Explore Sensitivity to Shelter Parameters.
Task 3: Compare Shelter Parameter Modification Results.
Task 4: Explore Sensitivity of Debris to Tree Damage.
Task 5: Compare Tree Density Modification Results.

## Slide 20: Lesson 9: Review
  What are the four factors modeled in Hazus that impact sheltering estimates?
  What are the only types of debris modeled in the Hazus Hurricane Model?

## Slide 21: Questions?