## Slide 1: Lesson 1: Introductions and Overview

## Slide 2: Let's Get Acquainted!
Participant introductions
  Name
  Organization
  Role in organization
  GIS and hazard analysis experience
  Goals and expectations for this class
Instructor introduction

## Slide 3: Course Agenda
Day One: Lesson 1: Introductions and Overview Lesson 2: Flood Model Inventory Lesson 3: Flood Hazard Data Lesson 4: Data Integration into Hazus Lesson 5: User-Defined Riverine Hazard: Part 1
Day Two: Lesson 5: User-Defined Riverine Hazard: Part 2 Lesson 6: Running the Analysis Lesson 7: Reviewing the Results Lesson 8: Hazus Flood Internal H&H Methodology: Part 1 (Riverine) Capstone Exercise Preparation
Day Three: Lesson 8: Hazus Flood Internal H&H Methodology: Part 2 (Coastal) Lesson 9: User-Defined Coastal Hazard Lesson 10: Combined Flood Analysis Capstone Exercise Preparation
Day Four: Lesson 11: Capstone Exercise Capstone Presentations Lesson 12: Course Wrap-Up

## Slide 4: Course Prerequisites
  Have a broad understanding of the goals of loss estimation and flood hazards.
    Course provides an introduction to assessing risks associated with natural hazards and orients participants to Hazus capabilities
    Course focuses on Basic and Intermediate analyses
  Familiar with ArcGIS
  Completed E0313 Basic Hazus

## Slide 5: Hints for Success
Ask LOTS of questions! There are NO "silly" questions.
Share your experiences with the rest of the class - they will learn from you and you from them.
Try to apply the concepts presented in class to your own needs. If you don't see applicability, ask for an example.
Practice the skills that you learn in class right away.
  In class (exercises and activities)
  After class (use it or lose it)

## Slide 6: Course Tasks
  Lecture
  Discussion
  Demonstration: Instructor-Only
    Students observe instructor completing task
  Activity: Instructor-Led
    Guided Practice
    Students follow along and complete task with instructor
  Exercise: Student-Led
    Individual or Small Group Practice
    Hands-on
    Shows how to apply material from this course to an actual incident

## Slide 7: Lesson 1: Goal and Objectives
Goal: To provide an overview of the course design and a review of the Hazus flood model purpose and design.
After completing this lesson, you will be able to:
  List the major topics addressed in this course.
  List the four hazards supported by Hazus.
  Explain the differences in Hazus analysis levels.

## Slide 8: What is Hazus?
  Software tools and support system designed by FEMA for the purpose of providing communities with the means to identify and reduce risk from natural hazards
  Used by a variety of communities and organizations
  Available from FEMA free of charge (requires ArcGIS license with Spatial Analyst extension)

## Slide 9: Supported Hazards

## Slide 10: History

## Slide 11: Supporting Emergency Management
  Identify vulnerable areas
  Estimate potential impacts of hazards
  Prioritize mitigation measures
  Assess level of readiness and preparedness
  Inform resource allocation
  Inform response and post-disaster recovery efforts

## Slide 12: Loss Estimation Process
  Produce maps, tables, and reports
  Analyze social and economic impacts
  Consider what is at risk
  Identify hazard
  Identify physical landscape

## Slide 13: User Levels

## Slide 14: Inventory (Exposure)
General building types and occupancies
  Lifelines
  Replacement costs
  Demographics
Hazard-specific
  Specific building types
  First floor elevations
  Building configurations

## Slide 15: Integrating User-Provided Data
Non-Hazard Data Integration Tools
  Comprehensive Data Management System (CDMS) enables integration of locally developed non-hazard data
  CDMS validates that user data are compliant with Hazus requirements
Hazard Data Integration
  ShakeMap and Hurrevac hazard data integration
  Each model includes tools for integrating user-provided hazard data
Techniques for integrating user-provided data are covered in other courses

## Slide 16: Hazus 4.2 Capabilities
Hazus 4.2 Capabilities | Earthquake | Flood | Hurricane | Tsunami
Inputs | Ground Shaking Ground Failure | Frequency ¦ Depth Riverine ¦ Coastal Surge | Wind Surge | Depth ¦ Momentum Flux Runup ¦ Velocity
Historic | x |  | x | 
Deterministic | x | x | x | x
Probabilistic | x | x | x | 
User-supplied | x | x | x | x
Other supported inputs | Real-time & scenario USGS ShakeMaps | Risk MAP, User-supplied depth grids (ArcGRID, GeoTIFF, IMAGINE), HEC-RAS (.FLT) | Hurrevac, User-supplied wind files (.dat) | NOAA PMEL SIFT, State models

## Slide 17: Hardware and Software Requirements
  Memory: 4 GB or higher
  Disk space: 10GB for one multi-hazard large urban study region, plus inventory data size (varies by state), or 70 GB to store entire U.S. inventory data
  Graphics Adaptor: 24-bit capable video card with at least 128 MB of video memory, resolution of 1078 x 768 or higher
  Operating Systems: 64-bit versions of Windows 10 Professional and Enterprise, Windows 8.1, and Windows 7 Professional
  Supporting Software: Appropriate version of Esri ArcGIS and the Spatial Analyst extension for the flood model

## Slide 18: FEMA Hazus Website
Primary FEMA resource for updated information related to Hazus: FEMA Hazus Website (www.fema.gov/hazus)

## Slide 19: Installation
  Log in with a full Administrator account
  Download Hazus from the Map Service Center’s website. (msc.fema.gov/portal/resources/hazus)
  Unzip the downloaded file
  Right-click on setup.exe file and select “Run as Administrator” option
  “Administrator Rights” can vary - consult the “Getting Started.pdf” document to ensure a proper installation

## Slide 20: State Inventory Data
  Download Hazus provided data (aggregated by each state) at the FEMA Hazus Download site: msc.fema.gov/portal/resources/hazus
  Each State dataset is wrapped into a .exe file
  Extract state(s) files of interest to Data Path folder by double-clicking the .exe file and selecting the data path folder
  C:\HazusData\Inventory

## Slide 21: What is a Study Region?
The area for which you are conducting a loss estimation study.
Can be defined by state, county, or census tract. Flood only or flood-tsunami regions can also be defined by census block, community, or watershed.
Questions to consider:
  What type of hazard(s) are you studying?
  What area(s) is the hazard likely to impact?
  Do you need to understand impacts outside your immediate jurisdiction?
No damage is assessed outside the study region - even if it exists!

## Slide 22: Study Region Size
  Size limit of 10 GB per database for SQL Server 2014 Express
  The success of a Hazus analysis will depend on the available system resources of the PC
  Large flood (riverine or coastal) and combined flood/wind analyses require large amounts of system resources even for small geographic areas (e.g., a single county)

## Slide 23: Study Region Location
  All study regions will be created in the folder specified in this window
  All data related to the Study Region will be stored in this location
  Default location is C:\HazusData\Regions

## Slide 24: Study Region Options
Hazus Startup Window
  Create a new region
  Open a region
  Delete a region
  Duplicate a region
  Export/Backup a region
  Import a region

## Slide 25: Discussion 1.1: Hazus Applications
Goal: Identify two ways that you would like to apply the information that Hazus generates in support of one or more of the following emergency management activities:
  Mitigation
  Preparedness
  Response
  Recovery
Groups: 3 to 6 people
Time: 10 minutes

## Slide 26: Exercise 1.2: Flood Study Region
Goal: Create a flood study region of Mecklenburg County, North Carolina.
Time: 10 minutes

## Slide 27: Lesson 1: Review
  What is Hazus?
  What are the four hazards supported by Hazus?
  Provide an example of a basic and an advanced analysis using the Hazus flood model.

## Slide 28: Capstone Exercise Preview
Goal: Help a county assess flood risk in order to develop flood mitigation strategies*
Planning:
  Day 1 Afternoon - form groups and develop project scope
  Day 1 and 2 Afternoon (briefly)
  Day 3 Afternoon
  Day 4 Morning
Presentation: Day 4 Afternoon
*The results of your study will be presented to the county mitigation planning team

## Slide 29: Capstone Exercise Preview
Use one or more of the Hazus flood model tools discussed in this course to identify risks to the community you selected on the first day of the class as well as possible options for mitigating those risks.
  Keep your study area manageable; less than 10 reaches if you are doing a “Basic” analysis.

## Slide 30: Capstone Exercise Preview
Presentation Guidelines:
  Should be prepared using PowerPoint.
  Include maps, tables, or other media you deem appropriate and helpful for conveying your message.
  Information should be primarily derived from Hazus, but may be supplemented by other sources.
  10-15 minutes in length; allowing 5 minutes for questions.
Planning Team Guidelines:
  Class and instructor will assume the role of the planning team.
  Planning team may ask questions related to the presentation.

## Slide 31: Capstone Exercise Preparation
Goals:
  Divide into groups of 3-6 people.
  Start discussing roles, strategies and the community you want to assist.
Time: 20 minutes

## Slide 32: Questions?