## Slide 1: Lesson 10: Combined Analysis

## Slide 2: Lesson 10: Goal and Objectives
Goal: To explore the Hazus options related to storm surge, hurricane wind, coastal flooding, and tsunami modeling.
After completing this lesson you will be able to:
  Understand the Hazus combined hurricane wind and storm surge modeling approach.
  List the steps necessary to complete a combined hurricane wind and storm surge model.

## Slide 3: Causes of Hurricane Storm Surge
http://www.comet.ucar.edu/nsflab/web/hurricane/313.htm

## Slide 4: Factors Influencing a Surge’s Size
  Storm Surge: Abnormal rise in the water level by a storm that is above the predicted astronomical tide.
  Storm Tide: Storm surge at combined with the local tide conditions at landfall.
  Wave breaking can increase the height of the surge and is dependent on the continental shelf.
http://www.comet.ucar.edu/nsflab/web/hurricane/313.htm

## Slide 5: Storm Surge Dynamics
The hurricane’s winds push against the surface of the water, pulling water from below to replace the displaced water.
The bulge of water and current slam into the continental shelf and are forced upward and inward.

## Slide 6: Factors Influencing Surge Size
  Wind speed, storm direction and motion, and coastline.
  Strongest winds and highest surge (without coastline effects) occur in the right-front quadrant of hurricane.
  Forward speed of the hurricane + rotational winds of the hurricane = highest wind speeds.

## Slide 7: Coastline Effects and Surge Size
  The orientation of the hurricane with respect to the coastline can influence the surge magnitude.
  Water can ‘pile up’ with favorable orientations; if hurricane winds are pushing against the coastline, water is caught along the coast.
  Water can also be trapped in bays.

## Slide 8: Discussion 10.1: Storm Surge
Goal: Discuss various concepts of storm surge.
Questions:
  How does the orientation of the coastline effect the storm surge depth?
  Where are the highest storm surges?
  How can a surge affect an area (geographically) that is not in close proximity to the hurricane path?
Time: 10 minutes

## Slide 9: Hurricane Storm Surge Overview
Hurricane Model:
  Windspeed and direction
Surge Model:
  SLOSH (sea, land, ocean)
  SWAN (near shore)
Wind and Surge are combined for aggregate inventory damages and losses only.

## Slide 10: SLOSH
  SLOSH = Sea, Lake, and Overland Surge from Hurricanes
  Numeric model initialized on a grid that requires the following inputs.
    Basin selection: SLOSH is packaged with pre-defined basins that have bathymetry (NGDC) and elevation information (USGS) for each grid cell.
    Hurricane characteristics: direction of movement, radius to maximum winds, pressure, location, direction, and speed.

## Slide 11: SLOSH
  Produces reasonably accurate estimates of surge and runs quickly.
  Emergency Management community is familiar with and comfortable.
  Does not include waves or tide.
    Tide treated as a fixed increase or decrease in initial water level based on predicted tide at time of landfall in the absence of storm surge and waves.

## Slide 12: Demonstration 10.2: SLOSH Depth Grid
Goal: Download SLOSH data to create a storm surge depth grid for use in Hazus and a short example of the SLOSH program.
Time: 45 minutes

## Slide 13: Demonstration 10.2: Tasks
Task 1: Download Datasets from SLOSH Website.
Task 2: Use SLOSH Display Program.
Task 3: Use ArcMap to Convert SLOSH Grid to Useable Hazus Format.

## Slide 14: Domains in SWAN Runs
Domains
Deep Water: Red
Near Shore: Blue

## Slide 15: SWAN
  Simulating WAves Nearshore
  Created by Delft University of Technology.
  Models:
    Wave propagation
    Wave generation from wind
    Wave interactions, dissipation, transmission, and diffraction
    Others
http://www.wldelft.nl/soft/swan/

## Slide 16: Coupled Surge and Wave Modeling
  SLOSH and SWAN codes have been coupled together.
  Methodology bridges gap between existing Hazus Hurricane Wind and Hazus Coastal Flood models.
  SLOSH is run first to update water elevations.
    SWAN uses water elevations produced by SLOSH.
    Result is larger modeled wave heights in areas where waves are depth-limited.
  SWAN is run to update wave stresses.
    Wave stresses are added to wind stress in SLOSH.
    Increases modeled storm surge due to wave setup.

## Slide 17: Overland Waves
  Model uses 1-D transects and simplified WHAFIS-like methodology to propagate waves inland from the shoreline.
  Where each transect intersects the coastline, use the modeled significant wave height from SWAN to estimate the controlling wave height, Hc = min(0.78 ds, 1.6 Hs) where ds = still water depth at the coast line.
  Wave crest elevation = SWEL + 0.7 Hc
    Neglect wave regeneration and wave dissipation.
    Neglect wave run-up and dune erosion.
  Use V-zone damage functions where Hc ≥ 1.5 ft

## Slide 18: Alternative Input: CERA
  Coastal Emergency Risks Assessment (CERA)
  ADCIRC Coastal Circulation and Storm Surge Model + SWAN Wave Model
  Depth grids can be integrated into Hazus

## Slide 19: Demonstration 10.3: CERA
Goal: To review CERA and how to use its outputs in Hazus.
Time: 15 minutes

## Slide 20: Hurricane Storm Surge Steps
  Storm Surge runs in the Hurricane Model during the damage and analysis.
  Surge is imported (automatically) into the Flood Model.
  DEM is combined with flood elevations for a final depth grid.
  Flood damages and losses are created.
  Combined wind and flood damages and losses are analyzed in the Flood Model (viewable in both models).

## Slide 21: Hurricane Scenario Definition Options

## Slide 22: Hurricane Data Sources (Hurrevac)
  HURRicane EVACuation
  Taken from National Hurricane Center advisory information
  Historical storms database
  Eliminates need to manually enter information

## Slide 23: Coastal Surge Hazard Modeling Options
  Surge with coupled deep water and near shore waves (SLOSH+SWAN).
  Surge with coupled near shore waves (SLOSH+SWAN).
  Surge only (SLOSH).

## Slide 24: Initial Water Level
Pre-storm tide anomaly is the difference between:
  The observed tide.
  The predicted tide approximately two days before landfall (i.e., before the effects of storm surge or waves reach the study region).

## Slide 25: Flood Hazard Type and User Data

## Slide 26: Exercise 10.4: Hurricane Surge Model
Goals:
  View surge depth grid.
  View flood, wind, and combined losses.
  View the combined losses table.
Time: 65 minutes

## Slide 27: Exercise 10.4: Tasks
Task 1: Create Storm Surge Study Region.
Task 2: Setup Hurricane Component of Storm Surge Analysis.
Task 3: Import a Partially Completed Hurricane Surge Model.
Task 4: Open Imported Region and confirm Surge Analysis is Complete.
Task 5: Switch to Flood Hazard and Generate Depth Grid.
Task 6: Explore Combined Losses.
Task 7: Switch to Hurricane Hazard and Explore Combined Losses.

## Slide 28: Tsunami Overview
  A series of long-period waves usually generated by an impulsive disturbance that displaces massive amounts of water
  Tsunamis can be triggered by:
    earthquakes​
    volcanic activity​
    submarine landslides​
    onshore landslides in which large volumes of debris fall into the water
  All of these triggers can occur in the United States.
  88% of tsunamis in the Global Historical Tsunami Database were generated by earthquakes or landslides caused by earthquakes.

## Slide 29: Hazus Tsunami Model
  Loss estimation model.
  Provides state-of-the-art decision support software for estimating potential losses from tsunamis.
  Available for:
    5 Very High-Risk states: AK, WA, OR, CA, HI
    5 High-Risk U.S. territories
  Earthquake/Tsunami combined analysis functionality available for the 5 states and PR.

## Slide 30: National Structure Inventory
  U.S. Army Corp of Engineers’ National Structural Inventory point data.
  Developed with FEMA.
  Creates notional structures, or ‘points,’ in the developed portion of each census block.
    Represent the numbers and types of buildings that occur based on size, occupancy type, construction materials, etc.

## Slide 31: Near Source: Deformed DEM
  Post-earthquake event deformed topography should be used in the case of a near source scenario.
  Earthquake could result in several meters of ground deformation.
  May substantially change the inundation area and affect potential losses resulting from a tsunami.

## Slide 32: Distant Source
  Tsunamis generated far away
    (>1,000 km) from a locality
  No ground shaking precedes the tsunami
  Lead time – few to several hours

## Slide 33: Coastal Flooding and Tsunami
  Consideration and use of DEM
  Tsunami runup height R: the height at the maximum tsunami penetration
  Boundary layers: entire Inundation area where depth > 0
  Combined analysis

## Slide 34: Lesson 10: Review
  What is one location where you can obtain the 100 year stillwater elevation along a coastline?
  What are the three factors that influence a storm surge’s size?
  What are four ways a user can view the combined wind and surge losses?

## Slide 35: Capstone Exercise Reminders
Use one or more of the Hazus flood model tools discussed in this course to identify risks to the community you selected on the first two days of the class as well as possible options for mitigating those risks.
  Keep your study area manageable; less than 10 reaches if you are doing a “Basic” analysis.
  Assign the members of your group to different tasks to ensure everyone stays busy.
  Make sure that everyone has at least some experience running Hazus.

## Slide 36: Capstone Exercise Reminders
Presentation Guidelines:
  Should be prepared using PowerPoint.
  Include maps, tables, or other media you deem appropriate and helpful for conveying your message.
  Information should be primarily derived from Hazus, but may be supplemented by other sources.
  10-15 minutes in length; allowing 5 minutes for questions.
Planning Team Guidelines:
  Class and instructor will assume the role of the planning team.
  Planning team may ask questions related to the presentation.

## Slide 37: Capstone Exercise Preparation
Goals:
  Continue downloading required data.
  Continue processing data.
Time: 3 hours
NOTE: Break as needed.

## Slide 38: Questions?