## Slide 1: Lesson 2: Flood Model Inventory

## Slide 2: Lesson 2: Goal and Objectives
Goal: To provide an overview of the data included with Hazus, as well as an overview of tools and processes to update the data.
After completing this lesson, you will be able to:
  Describe the types of aggregate and point inventory supported by the Hazus Flood Model.
  List the options Hazus provides for updating inventory.

## Slide 3: What is the General Building Stock?
  An estimate of building type and attribute distribution across the US
    Represented by:
    Floor area (Sq Ft)
    Replacement values ($)
    Building count of structures by occupancy and type
  Data sources:
    Residential from US Census Data
    Commercial / Industrial from various sources

## Slide 4: General Building Stock
Flood Specific Features:
  Depreciated value of structures (used for insurance purposes)
    Takes into account building age and construction quality
  Flood Model uses general building types and does not use detailed structural categories as in other models (e.g. earthquake, hurricane)
    Flood specific occupancy mapping does model foundation types and first floor height

## Slide 5: Aggregate Inventory
  Specific Occupancy Categories
    33 Specific Occupancy Types
    You can view the categories from the Inventory menu
  Aligned with but not identical to International Building Codes
Specific Occupancy | General Occupancy | Description
AGR1 | Agriculture | Agriculture
COM1 | Commercial | Retail Trade
COM2 | Commercial | Wholesale Trade
COM3 | Commercial | Personal and Repair Service
COM4 | Commercial | Professional/Technical Service
COM5 | Commercial | Banks
COM6 | Commercial | Hospital

## Slide 6: General Building Stock
Building Count:
  Most of the building counts in the General Building Stock are derived from the square footage factor table that provides average square footage for each specific occupancy determined from the Census and DOE data.
NOTE: RES1 (single family homes) and RES2 (manufactured housing) are derived from Census housing unit counts.
Occupany | Square Footage
RES1 | 1,800.00
RES2 | 1,475.00
RES3 | 2,200.00
RES3B | 4,400.00
RES3C | 8,000.00
RES3D | 15,000.00
RES3E | 40,000.00
RES3F | 80,000.00
RES4 | 135,000.00
RES5 | 25,000.00
RES6 | 25,000.00
COM1 | 110,000.00
COM2 | 30,000.00
COM3 | 10,000.00
COM4 | 80,000.00
COM5 | 4,100.00
COM6 | 55,000.00
COM7 | 7,000.00
COM8 | 5,000.00

## Slide 7: GBS - Building Valuations
Valuations:
Valuation models based on industry standard cost data* (Square Foot Costs)
RES1 is subdivided
Finished basements
*published by R.S. Means 2018

## Slide 8: General Building Stock
Valuations:
  Means published replacement values represent a national average
  Monetary parameters have been scaled from 2000 using ratios from the annual Consumer Price Index (CPI)
    https://www.bls.gov/cpi/
  When applied locally, costs are adjusted using local/regional multipliers (typically range from 0.7 to 1.4)
  General effect: GBS valuations in southern U.S. are reduced, while valuations along West Coast and Northeast increase
Year | Annual CPI
2000 | 172.40
2001 | 178.00
2002 | 179.90
2003 | 183.70
2004 | 189.70
2005 | 194.50
2006 | 202.9
2007 | 208.35
2008 | 218.81
2009 | 215.70
2010 | 217.96
2011 | 225.72
2012 | 229.48
2013 | 233.50
2014 | 238.34
2015 | 238.64
2016 | 241.02
2017 | 245.12
2018 | 251.11

## Slide 9: General Building Stock
Full vs. Depreciated Replacement Value:
  Full replacement value = engineering cost to rebuild a structure (labor, materials, overhead and profit)
    Not the assessed value, market value, or the retail value of new structures
    Does not include the value of the land
  Depreciated replacement value = remaining value of a structure based on age and general condition
    More closely reflects the insured value of property
    Not linked with square footage and building count

## Slide 10: General Building Stock
Residential Depreciated Building Values:
  Means full replacement cost models based on construction: economy, average, custom, luxury
  Means depreciation cost models based on condition: good, average, poor in 1 year increments
  Estimates single family residential buildings at the census block group level
Non-residential Depreciated Values:
  Formulas are based on construction type: wood frame, masonry, steel
  Depreciation based on “observed age” (renovation reduces deterioration of structure)
  Ages of structures assumed similar to the ages of residential structures in census block
Model default depreciation tables do not assume rise in value that may occur in some communities.

## Slide 11: Activity 2.1: General Building Stock
Goals:
  Modify the General Building Stock.
  Modify Depreciation Parameters.
  Observe change in Depreciated Exposure table.
Time: 10 minutes

## Slide 12: Activity 2.1: Tasks
Task 1: Modify General Building Stock and Depreciation Parameters.
Task 2: Observe change in Depreciated Exposure table.

## Slide 13: Flood-Specific Inventory
Dasymetric Inventory:
  Flood Model only
  A refined view of the building stock to reduce the overestimation of building damages in areas with low population density.
  Removal of undeveloped areas in census blocks changes their shape and reduces their size in these areas.

## Slide 14: Flood-Specific Inventory
Dasymetric Inventory:
  Assumes building exposure only exists within areas where satellite and land-use data confirm an existing built environment.
  2011 National Land Cover Dataset (NLCD)
  Highlighted classes in legend are kept.

## Slide 15: Homogenous vs. Dasymetric Blocks

## Slide 16: Dasymetric Inventory
  Removes undeveloped areas from the census blocks
    Bodies of water, wetlands, forests
  Still assumes equal distribution of inventory in remaining area of census block
  Modern disaster mitigation and analysis is completed in urban areas or areas that are developed
  Helpful when:
    Site-specific data is unavailable
    Coarser resolution of loss estimation is preferred
    Distributing GBS data only where people or buildings are

## Slide 17: Mapping Schemes
  Flood Specific Occupancy Mapping:
    Applies only to general building stock inventory
    Describe the distribution of foundation types within each census block
  Sources
    Heinz Center Study
    Department of Energy Statistics
  Differ for Riverine, Coastal, and Great Lakes census blocks by region.

## Slide 18: Editing Mapping Schemes
  For user-defined facilities: Occupancy to building type schemes that reflect the study region area
  May require supplemental information such as information about local building practices or input from local experts
  Data will likely require pre-processing

## Slide 19: Demonstration 2.2: Mapping Scheme Menu
Goals:
  Demonstrate the mapping scheme menus.
  Modify a mapping scheme.
Time: 10 minutes

## Slide 20: Exercise 2.3: Mapping Scheme Menu
Goals:
  Create a new mapping scheme that reflects changes in foundation type.
  Apply the new scheme to a census block.
Time: 10 minutes

## Slide 21: Agriculture
National Resource Inventory Data (1980 to 2000)
  Done every 5 years by USDA
  Compiled into sub-county polygons: 8 digit HUCs (watersheds) intersected with county boundaries
  Data on crop types and crop quantities (bushels)
    Top 20 crops for each NRI Regions
    Does not include livestock
  Only agricultural areas considered: using land use, land cover data, Hazus removes urban areas, wetlands, forests, etc.
  Not available in Alaska and U.S. territories

## Slide 22: Agriculture
National Agricultural Statistical Survey Data (NASSD)
  Done annually by USDA
  Data includes
  Crop production: 2002 average yield in bushels per acre
  Harvest cost: 2002 $ per bushel (e.g., the cost per bushel to raise corn)
  Harvest price: 2002 $ per bushel

## Slide 23: Vehicles
  Vehicle count estimates based in part on typical building square footage to vehicle ratios as used by MPO’s.
  Valuation based on average new and used vehicles.
    Three “occupancy” classifications: car, light truck, and heavy truck

## Slide 24: Activity 2.4: Essential Facility, Agricultural, and Vehicle Inventories
Goals:
  Explore the Agricultural and Vehicle inventories.
  Map the schools.
  Add an imagery basemap layer.
  Assess the accuracy of the school inventory.
Time: 15 minutes

## Slide 25: Activity 2.4: Tasks
Task 1: Explore the Agricultural and Vehicle inventories.
Task 2: Map the schools.
Task 3: Assess the accuracy of the school inventory.

## Slide 26: Site-Specific Inventory
  Essential Facilities (Police and Fire Stations, EOCs, Schools, Hospitals)
  Transportation Infrastructure
    All inventory can be entered, but only bridges are analyzed
  Utilities
    Additional classifications include control vaults, control valves, and control stations
  User-Defined Facilities (site-specific)

## Slide 27: Difference Between GBS and UDF
General Building Stock: an engineering based estimation of structures by occupancy
  Aggregate data by Census geography according to hazard type
  Reported by square footage, dollar exposure, building count
  Linked during development, but not in software
User-Defined Facilities: building or structure specific data
  Must be imported through CDMS by the user
  Provides actual locations of buildings
  Replacement value rather than appraisal value of buildings
Site-Specific Data: building or structure specific data
  Some data included in Hazus inventory, such as hospitals, fire stations, and schools
  May include user-defined, AEBM, high potential loss, essential, transportation and utility facilities
  Damages assessed on an individual building basis

## Slide 28: Site-Specific Inventory: UDF
User-Defined Facilities:
  Used to perform a more refined site-specific or building by building analysis of inventory found in the General Building Stock.
  This table is not populated unless the user does so.

## Slide 29: User-Defined Facilities
Required Fields:
Hazus requires minimal construction design characteristics to select the correct damage curve for damage and loss analysis for each facility.
  Foundation Type
  Number of stories
  First floor elevation
  Specific occupancy*
  Building and Contents Valuations
*Only field required when uploading through CDMS. CDMS can fill the remaining attributes with Hazus defaults

## Slide 30: User-Defined Facilities
  Damages are determined by the depth of water at the location of the point representing a facility.
  Building and content damages and losses are reported on a structure-by-structure basis.
  Losses do not include business interruption, only direct loss UDFs are not designed to replace engineering models or knowledge.
  UDF results are best used by summing all the UDF results for an area rather than using individual structure results.

## Slide 31: Applications of User-Defined Facilities
Explore the impact of having fewer homes in the floodplain.
Explore the outcome of elevating at-risk homes.

## Slide 32: Inventory Update Options
  Comprehensive Data Management System (CDMS)
  Study Region Update Tools
NOTE: The E0317: Comprehensive Data Management for Hazus course provides more detail about inventory updates.

## Slide 33: Comprehensive Data Management System
  System for integrating user provided site specific and aggregate data into the Hazus state databases
  CDMS supported data includes:
    Site specific
    Aggregate
    Building specific

## Slide 34: Comprehensive Data Management System
Functions:
  Validates user provided data
  Parses data into appropriate Hazus tables
  Provides historical tracking of database updates
  Can import/export data to/from a variety of formats

## Slide 35: Comprehensive Data Management System
  CDMS allows the user to edit state database information.
    Study regions created after edits in CDMS will reflect new information.
    Old study regions will not be updated.
  Hazard specific data can be entered for Earthquakes, Hurricanes, and Floods.

## Slide 36: Exercise 2.5: Update Inventory using CDMS
Part 1: Update site-specific data.
Part 2: Update aggregated data.
Part 3: Import user-defined facilities.
Part 4: Create a new study region with the updates

## Slide 37: Exercise 2.5 Part 1: Updating Inventory Data Using CDMS
Goals:
  Update site-specific data.
  Update state fire station database using CDMS.
Time: 15 minutes

## Slide 38: Study Region Update Tools
Edit Individual Records
  Most site specific and aggregate inventory tables can be edited within the study region GUI.
  Useful for adding or editing individual records, not practical for large inventory update projects.

## Slide 39: Study Region Update Tools
  Within Hazus:
    For individual record updates or imports
    Must import a personal geodatabase
    Need to map imported table fields to the fields in Hazus table structure
  Within CDMS:
    For large dataset updates or imports
    CDMS will parse data to required fields
    Can import a field mapping file
    Supports both site-specific inventory and aggregated data

## Slide 40: Exercise 2.5 Part 2: Updating Inventory Data Using CDMS
Goals:
  Update aggregate data.
Time: 15 minutes

## Slide 41: Study Region Update Tools
Import Inventory
  Import MS Access or Excel tables or feature classes
  Hazus provides field mapping capability

## Slide 42: Exercise 2.5 Part 3: Updating Inventory Data Using CDMS
Goals:
  Import User-Defined Facilities into a state database.
Time: 15 minutes

## Slide 43: Exercise 2.5 Part 4: Updating Inventory Data Using CDMS
Goals:
  Create new study region with CDMS updates.
Time: 5 minutes

## Slide 44: Exercise 2.5 Part 5: Updating Inventory Data Using CDMS
Goals:
  Import inventory data from a study region into CDMS.
Time: 5 minutes

## Slide 45: Lesson 2: Review
  What is the purpose of a flood specific occupancy mapping scheme?
  What type of building value is the engineering cost to rebuild a structure? (Full Replacement or Depreciated Replacement)
  Name two types of aggregate inventory that are unique to the flood model.
  What types of buildings are considered by Hazus to be essential facilities?
  What is the name of the tool provided by Hazus for updating the state databases?

## Slide 46: Questions?