## Slide 1: Lesson 3: Flood Hazard Data

## Slide 2: Lesson 3: Goal and Objectives
Goal: To review sources of flood hazard data.
After completing this lesson, you will be able to:
  List the types of flood hazard data.
  Describe how to coordinate flood hazard data.

## Slide 3: Risk MAP
  Risk Mapping, Assessment and Planning program
  High quality flood maps from the Map Service Center
  Provide community with flood information and tools
  Inform decisions about reducing risk
  Flood risk products:
    Flood Risk Map (FRM)
    Flood Risk Report (FRR)
    Flood Risk Database (FRD)

## Slide 4: Flood Risk Map (FRM) & Flood Risk Report (FRR)
Flood Risk map (FRM):
  Depicts flood risk data for a flood risk project area
  Typically used to illustrate an overall picture of flood risk for the area
  Maps might include:
    potential flood losses associated with the one-percent annual chance flood event for each census block
    areas planned for new or revised maps
    key watershed features that affect local flood risk
    information about potential or successful past projects to reduce flood risk
Flood Risk Report (FRR):
  Provides community and watershed specific flood risk information extracted from the Flood Risk Database (FRD)
  Explains the concept of flood risk
  Identifies useful tools and reference materials
  A good tool for communities to use for raising local flood risk awareness

## Slide 5: Flood Risk Database (FRD)
  Stores all flood risk data for a flood risk project
    Including information shown in the FRR and FRM
  Datasets include:
    Changes since last Flood Insurance Rate Map (FIRM)
    Areas of Mitigation Interest
    Flood Depth and Analysis Grids
    Flood Risk Assessment Data*
  To order data from the FEMA Engineering Library follow the instructions provided here: https://www.fema.gov/how-order-technical-administrative-support-data
  Data can also be downloaded from the MSC https://msc.fema.gov/portal/home
* Flood Risk Assessment Data includes data for baseline Hazus assessment and UDF data if it's available.

## Slide 6: Depth Grids
  Raster surface with flood depths defined for each pixel
  Are produced for specific events or return periods
  Most commonly:
    Created using GIS or H&H modeling
    Many are available from the FEMA MSC

## Slide 7: Depth Grid Data Sources
  FEMA Digital Flood Insurance Rate Map (DFIRM) Database
    One of the products available
    Base flood elevation or cross sections from the H&H studies
    Cross sections can be interpolated to create a flood surface
  High Water Mark (HWM) data
    Point data collected using high resolution Real time Kinematic (RTK) GPS systems
    Points used as foundation for interpolating maximum flooding extent
  H&H Model
    Simulates rainfall runoff flow
    Predicts the extent of creek and river water levels, flooding, and tests ways to reduce the flooding
    H&H models inform decisions around selecting and implementing flood reduction and restoration projects

## Slide 8: Base Flood Elevation (BFE)
  Computed elevation to which floodwater is anticipated to rise during the base flood
  Shown on Flood Insurance Rate Maps (FIRMs)
  Regulatory requirement for the elevation or floodproofing of structures
  Users can supply BFE data
    Coastal users will also supply polygons attributed with the BFE

## Slide 9: Digital Terrain or Elevation Model (DEM)
  USGS's The National Map is the source of DEM data
  National Elevation Dataset (NED): default for flood model
  Seamless map server
  Hazus will generate DEM download links
  Users can bring their own DEM, but data must completely cover coordinate extent

## Slide 10: National Elevation Dataset (NED)
  Seamless dataset of raster elevation data of the conterminous United States, Alaska, Hawaii, and territorial islands produced by the USGS:
    1 Arc-second (about 30 meter) resolution for most of US (except Alaska)
    1/3 Arc-second (about 10 meter) for most of the US
    1/9 Arc Second (about 3 meter) for limited areas
  Projection is in decimal degrees, vertical units, meters
  Data downloaded directly from the National Map are in meters

## Slide 11: HEC-RAS
  Hydrologic Engineering Center's (CEIWR-HEC) River Analysis System (HEC-RAS)
  Developed in 1995 by Army Corps of Engineers (ACOE)
  Hydraulic modeling software published by USGS
  A dialog enables HEC-RAS users to import hydraulic output floating-point binary grids (.flt files)
  Very commonly used in H&H Floodplain modeling

## Slide 12: External H&H Modeling
  Not a component of Hazus, but H&H models are used by FEMA to support NFIP and outputs define Special Flood Hazard Areas (SFHA)
  GIS-based
    ArcHydro tool summarizes terrain and hydraulic and hydrologic characteristics of a watershed for input data
  HEC-HMS (Hydrologic)
    Modeling of precipitation-runoff processes
  HEC-RAS (Hydraulic)
    Open steady and unsteady flow calculations

## Slide 13: Discharge or Stream Gage Data
  Delineates the floodplain (hydraulics)
  Historical discharge values have been recorded by USGS at over 22,000 stream locations
  Fit a line to the annual peak discharge data to determine the discharges for varying flood frequencies
  Discharge-frequency curve
  Technique described in “Guidelines for Determining Flood Flow Frequency, Bulletin 17B” (Hydrology Subcommittee of Interagency Advisory Committee on Water Data, 1982)

## Slide 14: Discharge Values: FEMA
USGS: real-time water data
http://waterdata.usgs.gov/nwis/rt
FEMA: Flood Insurance Studies
Flooding Source
Location
10% Annual Chance
4% Annual Chance
2% Annual Chance
1% Annual Chance
0.2% Annual Chance
Central Reservoir
Flood County
12.6
-
14.5
15.2
17
Lily Pond
Metropolis
8.6
-
11.6
12.6
13.3

## Slide 15: Discharge Values: AHPS
  The National Weather Service provides:
    Hydrologic forecasts for 8,000+ locations across the United States.
    Historical crests and impacts
    Forecasted flood stages
    Discharge values (note the units)
  Data is updated twice daily giving users nearly real-time gage data.
http://weather.gov/ahps/

## Slide 16: USGS Flood Event Viewer
  Provides observed stream gage data for flood events
  Source of customized discharge data in Hazus models
  Event HWMs are downloadable and can be used to make depth grids
https://stn.wim.usgs.gov/fev/

## Slide 17: Demonstration 3.1: Discharge Data
Goals:
  Navigate the USGS website to identify discharge values for use in Hazus.
Time: 10 minutes

## Slide 18: Demonstration 3.1: Tasks
Task 1: Find discharge points for an event.

## Slide 19: Coastal Hazard Data
National shoreline
  Includes a smoothed shoreline for transect development
Attribution of census blocks as coastal or great lakes.

## Slide 20: Modeled Wave Effects
Wave setup:
  Increase in the stillwater level caused by waves breaking near the shoreline.
Simplified overland waves:
  Affected by water depth.
  Results from wave height analyses combined to develop a single water surface.

## Slide 21: Storm Surge Data
  Sea, Lake and Overland Surges from Hurricanes (SLOSH)
    A computerized numerical model developed by the National Weather Service (NWS) to estimate storm surge heights resulting from historical, hypothetical, or predicted hurricane
    Account for atmospheric pressure, size, forward speed, and track data
    Creates a model of the wind field which drives the storm surge
  Coastal Emergency Risks Assessment (CERA)
    Utilizes ADCIRC storm surge model, a hydrodynamic simulation model
    Water height and inundation above mean sea level

## Slide 22: Site-Specific Data: Tax Assessor Data
  Source of additional data to increase the level of analysis
  Often available at the county level
  Only covers taxable structures
  May provide details on:
    Parcel information
    Address
    Occupancy type
    Year built
    Square footage
    Number of stories
    Foundation and/or structure type
  Hazus defaults can fill in missing information with occupancy type

## Slide 23: Lesson 3: Review
  Describe the RiskMAP program
  How is DEM data incorporated into Hazus?
  What other flood hazard data does Hazus utilize?

## Slide 24: Questions?