## Slide 1: Lesson 4: Integration of User-Defined Flood Hazard Information into Hazus

## Slide 2: Lesson 4: Goal and Objectives
Goal: To review integration options and methods for flood hazard data.
After completing this lesson, you will be able to:
  Outline integration options for data.
  Identify what data are necessary for various parts of the flood model.

## Slide 3: Input Data

## Slide 4: Study Region and Hazard Selection
  Riverine and coastal hazards have different requirements in terms of the development of the hazard and the digital elevation data required to support the analysis.
  Think carefully about which hazard type (or both) you want to analyze.
  Both Riverine and Coastal analyses can be run with only a depth grid.

## Slide 5: Terrain
  Users can import custom depth grids into Hazus to replace USGS DEMs and using Hazus to model the floodplain
  Must define the Units and Return Period of the depth grid
  Multiple depth grids can be imported
  File formats supported: GRID, IMAGINE (IMG), HEC-RAS (FLT), TAGGED IMAGE FILE (TIF), and fGDB
  Hazus will also automatically re-project any user-defined depth grids which are not in WGS84

## Slide 6: Depth Grid Production
  Requires Spatial Analyst toolbox in ArcGIS
  Interpolation to create water surface elevation grid and subtract from terrain or DEM
  Using DFIRM data
    Should use an area of interest (AOI) to reduce processing time
    Utilizes FEMA defined flood zones (e.g. AE, AO, AH) and BFEs or Cross Sections.
  Using HWM data
    Elevation above ground of the flood (seed or dirt lines)
    Great for post flood event analysis
  Depth grids should only be creating using GIS in the absence of advanced H&H models

## Slide 7: HEC-RAS
  Users can import HEC-RAS models into Hazus as the flood hazard.
  Floating-point binary (.flt) grids used primarily for riverine modeling
  .flt grid floodplain boundary must be located partially within the study region

## Slide 8: User-defined Data from Hydraulic Models
  Specific flood hazard information can be provided from other hydrologic and hydraulic models other than HEC-RAS
  HEC-RAS requires .flt data, however, raster data sets from other models can also be inserted
  The flood model does not validate the integrity between the imported grid and the floodplain boundary polygon
  Imported data can impact the riverine/coastal geometry, flood plain results, and terrain data

## Slide 9: User-supplied inventory data
  Inventory can be updated using the Comprehensive Data Management System (CDMS)
  Analysis results are improved with inventory such as:
    Locally available data such as first floor heights or square footage of buildings in different occupancy classes
    Use of local expertise to modify, primarily by judgment, the databases concerning percentages of model building types associated with different occupancy classes
    Preparation of a detailed inventory for all Essential Facilities
    Collection of detailed inventory and cost data to improve the evaluation of losses
    Development of inundation maps
    Gathering of information concerning critical infrastructure

## Slide 10: Storm Surge
  The abnormal rise in seawater level during a storm.
  Measured as the height of the water above the normal predicted astronomical tide.
  After running the hurricane model for the study region, storm surge data is calculated in the flood model
  Results are shown for each hazard type individually and the weighted combination.

## Slide 11: Storm Surge
  Combined losses are weighted based on how each hazard type contributes to overall damages:
    Flood hazards typically damage lower portions of a structure (foundation, lower floors)
    Hurricane wind hazards typically damage upper portions of a structure (roof, upper floors)
  User data menu for integration:
    User-supplied Depth Grid (SLOSH or ADCIRC outputs)
    Surge Elevation Grid (SLOSH) appears as surge.flt and surge.hdr
    Significant Wave Height Grid (SWAN) appears as waveht.flt and waveht.hdr

## Slide 12: Additional Notes
Hydrologic analysis is NOT necessary if you are providing results from another flood study or user-defined depth grid.
These might include:
  Entering discharges (single discharge)
  Quick Look: drawing a polygon having a constant flood depth
  Enhanced Quick Look: providing a flood plain boundary and DEM
  Providing a user-defined flood depth grid
  HEC-RAS output

## Slide 13: Lesson 4: Review
  What is an external source of data that is integrated into Hazus?
  How can users augment the default data integration?

## Slide 14: Questions?