## Slide 1: Lesson 5: User-Defined Riverine Hazard

## Slide 2: Lesson 5: Goal and Objectives
Goal: To introduce the options that Hazus offers for integrating user-defined riverine flood hazard information into a Hazus study region.
After completing this lesson, you will be able to:
  Use each of the available tools that Hazus provides for defining a flood hazard with user provided input.
  List both the advantages and limitations of each user-defined hazard tool available in Hazus.

## Slide 3: User-Defined Riverine Hazard Options
  Quick Look
  Enhanced Quick Look
  User-Defined Flood Depth Grid
    Importing process
    How to create a depth grid in GIS
  HEC-RAS

## Slide 4: Quick Look
  Allows user to estimate damage without running hydrology and hydraulics analysis.
  User creates flood boundary and enters flood depth.
  Estimates GBS damage assuming uniform flood depth within polygon.
  No DEM input is required.
NOTE: This feature can only be used in a study region in which no scenarios are open.

## Slide 5: Enhanced Quick Look (EQL)
  User supplies both a DEM and a flood boundary.
  Hazus creates a depth grid within the boundary and estimates GBS building damage.
  NOTE: This feature can only be used in a study region in which no scenarios are open.

## Slide 6: Quick Look and EQL Analysis
  The Quick Look and the Enhanced Quick Look analysis are both run by selecting Quick Analysis.
  Only General Building Stock is analyzed, so no options exist for which analysis components to run.

## Slide 7: Activity 5.1 Quick Look Analyses
Goals:
  Perform Quick Look Analysis.
  Perform Enhanced Quick Look Analysis.
Time: 10 minutes

## Slide 8: Activity 5.1: Tasks
Part I: Quick Look Analysis
Task 1: Import a Study Region.
Task 2: Define a Quick Look Polygon.
Task 3: Run the Quick Look Analysis.
Task 4: Explore the Quick Look Output.
Part II: Enhanced Quick Look
Task 1: Identify the Enhanced Quick Look Input.
Task 2: Run the Quick Look Analysis.
Task 3: Explore the Quick Look Output.

## Slide 9: User-Defined Flood Depth Grid
Hazus allows users to point to one or more existing flood depth grids.
  File formats supported: GRID, IMAGINE (IMG), HEC-RAS (FLT), TAGGED IMAGE FILE (TIF), and fGDB
  Depth units are defined by user
  Can use any projected coordinate system
  Must cover entire geographic study region
This option represents the most accurate representation of a flood hazard, assuming the depth grid has been created with appropriate methods.

## Slide 10: User-Defined Flood Depth Grid
  Assign the depth grid to a scenario.
  All analysis output options available.

## Slide 11: User-Defined Depth Grids
High Water Marks:
  A measure of the water surface elevation
  During periods of high water, elevations may be collected.
    As close to the peak elevation as possible.
  These values represent the most accurate depiction of the flood event.
NOTE: High water mark locations and values in feet.

## Slide 12: User-Defined Depth Grids
High Water Marks:
  Using GIS the high water marks can then be interpolated into a water surface elevation grid.
  This represents the elevation of the water during the flood event above sea level and 'fills in' the gaps where water marks are not present.

## Slide 13: User-Defined Depth Grids
High Water Marks:
  Once the water surface is created, it is subtracted from a DEM or topography.
  Next, negative values are removed, the resulting surface is the flood depth.
NOTE: Flood events are often not accurately depicted by risk maps, such as 1% annual choice maps. High water mark flood depth grids reflect historic flood events more closely.

## Slide 14: Exercise 5.2: High Water Marks
Goal: Create a depth grid from High Water Marks.
Time: 45 minutes

## Slide 15: Exercise 5.2: Tasks
Task 1: Interpolate the Water Surface and Create a Depth Grid.
Task 2: Subtract Water Surface Grid from the DEM.
Task 3: Remove Negative Values.
Task 4: Create the Flood Boundary.

## Slide 16: Capstone Exercise Preparation
  This is the end of today's material, tomorrow will resume the rest of Lesson 5.
  Capstone Exercise Strategy
    Everyone needs a role and to work with Hazus.
    Make sure group goals are achievable within the time frame
  Past Group Presentation Examples
  Continue Preparation
    Assign Group Roles
    Discuss strategies
    Choose a community that your group can use the Hazus assist with flood mitigation strategies.

## Slide 17: Capstone Exercise Preparation
Goals:
  Download the state data for your study region from the MSC at https://msc.fema.gov/portal/resources/hazus.
  Continue planning and preparation.
Time: 30 minutes

## Slide 18: Exercise 5.3: DFIRM Depth Grid
Goal: Create a flood depth grid from a DFIRM Dataset and a DEM.
Time: 25 minutes

## Slide 19: Exercise 5.3: Tasks
Task 1: Prepare the Data.
Task 2: Interpolate the Water Surface
Task 3: Prepare the Depth Grid

## Slide 20: HEC-RAS Depth Grids
  Hydrologic Engineering Center’s River Analysis System.
  A software package from the US Army Corps of Engineers.
  Enables users to perform one or two-dimensional hydraulic calculations.
  Hazus integrates HEC-RAS output in version 4.1 or later of HEC-RAS.
  The floating-point binary (.flt) file needed to import into Hazus.
  Depth grids can be exported from HEC-RAS and brought into Hazus

## Slide 21: HEC-RAS Depth Grids
  Output will show flood boundaries.
  NOTE: Hazus only computes still water damages; damages related to velocity from a dam or levee break is not calculated.

## Slide 22: Exercise 5.4: Importing HEC-RAS
Goal: Import User-Supplied HEC-RAS Output.
Time: 45 minutes

## Slide 23: Exercise 5.4: Tasks
Task 1: Import the depth grid.
Task 2: Define the scenario.
Task 3: Run analysis.

## Slide 24: Hazus Flood Assessment Structure Tool (FAST)
  Open source, standalone flood risk assessment tool
  Uses Hazus depth damage functions to calculate flood impacts at structures
  No software or mapp
  ing skills required
  Makes flood risk assessment faster, cheaper, & simpler

## Slide 25: FAST - The Specs
  Planned to be hosted on GitHub
  Calculates 10,000 structures/second

## Slide 26: FAST Case Study - NYC Mitigation Plan Update
  NYC mitigation plan update required a citywide multi-hazard risk assessment
  Planners used a regulatory 100-year depth grid from FEMA and an 800K structure dataset from tax assessor
  FAST calculated 100-year economic losses at all NYC structures in under a minute and a half
  FAST results help planners strategically distribute risk reduction efforts to the highest-risk areas

## Slide 27: Lesson 5: Review
  Place the options for defining a flood hazard in order based on the accuracy of the method assuming each option uses the best available input.
  Place the options in order from least to most based on the amount of user input required.
    Quick Look Enhanced
    Quick Look
    User-Defined Depth Grid
    HEC-RAS

## Slide 28: Questions?