## Slide 1: Lesson 6: Analysis Methodology and Options

## Slide 2: Lesson 6: Goal and Objectives
Goal: To explore the methodologies Hazus uses to assess losses from a flood hazard.
After completing this lesson, you will be able to:
  Understand the depth-damage function concept.
  Understand the direct economic loss parameters.
  Become familiar with the Hazus Technical Manual as a resource to understand the model.

## Slide 3: Levels of Analysis

## Slide 4: Depth-Damage Functions
Default depth-damage functions are assigned based on building characteristics.

## Slide 5: Depth-Damage Functions
Depth-damage functions are applied to relevant depth.
  Buildings: first-floor height (bottom of first finished floor for coastal)
  Equipment: height above first floor

## Slide 6: Demonstration 6.1: Damage Function GUI
Goals:
  Explore the damage function GUI.
  Explore the Results Menu in the Flood Model.
Time: 15 minutes

## Slide 7: General Building Stock Damage
Buildings and user-defined facilities use adapted functions from several sources including:
  USACE District Functions: Chicago, Galveston, New Orleans, New York, Philadelphia, St. Paul, and Wilmington
  USACE IWR: “national standard” residential function (2000); other functions under development
  FIA: CWDD, V Zone
  BCAR (Benefit-Cost Analysis Re-engineering)
  Other Coastal: Tampa Bay Regional Planning Council, Delaware

## Slide 8: GBS Loss Estimation Methodology
Hazus performs an area weighted assessment of damage for aggregate inventory.
  Number of grid cells at a given depth is counted and divided by total number of cells within census block.
  Result is used to “weight” damage at that flood depth for each occupancy.
DEM Grid Points
This approach is most appropriate for large areas.

## Slide 9: GBS Loss Estimation Methodology
  Assumes that inventory is evenly distributed across each census block.
  Example: If 25% of the block has 2 ft. of water, it is assumed that 25% of the four single-family dwellings in the block are in 2 ft. of water.
  Losses are reported as totals for each occupancy and building type rather than for each building.

## Slide 10: GBS Loss Estimation Methodology
Dasymetric Modeling:
  Hazus continues to assume an even distribution of buildings in a dasymetric approach.
  The census block area is decreased (removed) if the block contains a land use / land cover classification that is not one of the accepted classes.
  Only distributes GBS in areas that are populated parts of the census block vs the entire block.

## Slide 11: Essential Facilities Damage
Essential facility damages are assessed by applying the same functions as those used for similar general building stock facilities.
Occupancy Class | Description | Age | Model Building Type | Basement | First Floor Elevation | Building Height | Damage Function | Depth Threshold for Functionality
EFHS | Small Hospital | Median | Concrete | Yes | 3 | Low | COM6 | 0.5
EFHM | Medium Hospital | Median | Concrete | Yes | 3 | Mid | COM6 | 0.5
EFHL | Large Hospital | Median | Concrete | Yes | 3 | Mid | COM6 | 0.5
EFMC | Medical Center | Median | Concrete | Yes | 3 | Low | COM7 | 0.5
EFFS | Fire Station | Median | Concrete | No | 0 | Low | GOV2 | 2
EFPS | Police Station | Median | Concrete | Yes | 0 | Low | GOV2 | 1
EFE0 | Emergency Operations | Median | Concrete | Yes | 0 | Low | GOV2 | 1
EFS1 | School | Median | Brick | No | 0 | Low | EDU1 | 0.5
EFS2 | University | Median | Concrete | No | 0 | Low | EDU2 | 0.5

## Slide 12: Bridge Damage
Bridges are the only transportation facility modeled in Hazus Flood Model.
NOTE: Bridge analysis is not possible on mixed return periods or single discharge.
Occupancy | Specific Occup Id | Source | Description | Scour Potential | Bridge Type | 0 yr | 25 yr | 50 yr
HWB1 | HWB1SU | Hazus Dflt | Continuous Span | U | Continuous Span | 0 | 0.003 | 0.006
HWB1 | HWB1S1 | Hazus Dflt | Continuous Span | 1 | Continuous Span | 0 | 0.003 | 0.006
HWB1 | HWB1S2 | Hazus Dflt | Continuous Span | 2 | Continuous Span | 0 | 0.001 | 0.003
HWB1 | HWB1S3 | Hazus Dflt | Continuous Span | 3 | Continuous Span | 0 | 0.001 | 0.001
HWB2 | HWB2SU | Hazus Dflt | Continuous Span | U | Continuous Span | 0 | 0.003 | 0.006
HWB2 | HWB2S1 | Hazus Dflt | Continuous Span | 1 | Continuous Span | 0 | 0.003 | 0.006
HWB2 | HWB2S2 | Hazus Dflt | Continuous Span | 2 | Continuous Span | 0 | 0.001 | 0.003

## Slide 13: Bridge Damage
Based on return period and probability of failure due to scour for bridges with scour potential of “U,” 1, 2, or 3 as defined by DOT.
Highway Single Span Bridge Damage Relationship
Highway Continuous Span Bridge Damage Relationship
Flood Return Period | 1 | 2 | 3 | 4-8 | 9
100 Year | 5 | 2 | 1 | 0 | N/A
500 Year | 10 | 4 | 2 | 0 | N/A
1000 Year | 15 | 6 | 3 | 0 | N/A
Flood Return Period | 1 | 2 | 3 | 4-8 | 9
100 Year | 1.25 | 0.5 | 0.25 | 0 | N/A
500 Year | 2.5 | 1 | 0.5 | 0 | N/A
1000 Year | 3.75 | 1.5 | 0.75 | 0 | N/A

## Slide 14: Utility Facility Damage
  Damage functions for selected utility facilities
  Damage based on:
    Damage to critical flood vulnerable components
    Average equipment height
  Functions derived based on expert opinion.
(%damage) = damage at (depth of water - equipment height) ($ Loss) = (% Damage) * (Inventory $ value)
Occupancy | Specific Occup Id | Source | Description | Equipment Ht | Comment
PDFLT | PDFLT | Hazus Dflt | Hazus Dflt | 3 | 
PPPL | PPPL | Hazus Dflt | Large Pumping Plant Below Grade (>50 MGD) | 3 | Entrance is 3 feet above grade
PPPM | PPPM | Hazus Dflt | Medium Pumping Plant Below Grade (10-50 MGD) | 3 | Entrance is 3 feet above grade
PPPS | PPPS | Hazus Dflt | Small Pumping Plant Below Grade (<10 MGD) | 3 | Entrance is 3 feet above grade
PSTAS | PSTAS | Hazus Dflt | Elevated Tanks | 80 | 

## Slide 15: Vehicle Damage Functions
  Damage functions = step functions based on increasing component damage as flood depth increases
  Based on average vehicle height above the road
  Functions based on expert opinion and historical data
NOTE: Inventories are split between new and used vehicles.
Flood Level | Car | Light Trk | Heavy Trk | % of Damage
Below Carpet | < 1.5 | < 2.7 | < 5 | 15
Between Carpet & Dashboard | 1.5-2.4 | 2.7-3.7 | 5-7.5 | 60
Above Dashboard | > 2.4 | > 3.7 | > 7.5 | 100

## Slide 16: Agriculture Damage
  Based on USACE’s AGDAM (Agriculture Damage Model) method
  Damage functions account for:
    Crop type
    Date of flood
    Duration of flood
  Model assumes short duration, slow rise flood when estimating agricultural losses
  Area (not depth) of impacted crop is determined

## Slide 17: Agriculture Damage
  User must input calendar date (e.g., 27 of May)
  Date converted to Julian Calendar to define location in crop cycle and appropriate damage function
  Flood Model estimates flood durations of 0-days, 3-days, 7-days, and 14-days
Crop | Source | JulianDay | Percent Damage to Crop | Duration Modifier 0-days | Duration Modifier 3-days | Duration Modifier 7-days | Duration Modifier 14-days
Alfalfa Hay | USACE | 1 | 37 | 0 | 1 | 1 | 1
Alfalfa Hay | USACE | 2 | 37 | 0 | 1 | 1 | 1
Alfalfa Hay | USACE | 3 | 37 | 0 | 1 | 1 | 1
Alfalfa Hay | USACE | 4 | 37 | 0 | 1 | 1 | 1
Alfalfa Hay | USACE | 5 | 37 | 0 | 1 | 1 | 1

## Slide 18: Restoration Functions
  Restoration functions provide an indication of maximum restoration time for 100% operations.
  Flood model assumptions:
    Inventory is usually a total loss; cannot dry and sell
    Restoration time often greater in a flood than in an earthquake; cannot move stock into parking lot and sell
Essnt Flty Class | Flty Description | Minimum Depth | Maximum Depth | MaxDays ToRestoration | Functional Depth
EDFLT | Default for Emergency Response Facility | -4 | 0 | 360 | 0.5
EDFLT | Default for Emergency Response Facility | 0 | 4 | 480 | 0.5
EDFLT | Default for Emergency Response Facility | 4 | 8 | 630 | 0.5

## Slide 19: Debris Estimation
  The Flood Model focuses on building-related debris.
  Identifies building components requiring replacement at various water depths and estimates their weight.
  Debris classes:
    Building finishes
    Structural components
    Foundation materials
  Analysis does not include vegetation, sediment, or building content debris.

## Slide 20: Casualties
Hazus does not generate casualty estimates for the following reasons:
  Available casualty data for floods limited to fatalities (injury information not widely available)
  A fatality model for floods proposed, but deferred by the oversight committee
    Few storm events
    Not validated with the same level of scientific vigor as rest of the Flood Model
    Flood casualties not nearly as significant in magnitude to earthquake casualties

## Slide 21: Shelter
  Based on Hazus earthquake model algorithms
  Displaced population based on displacement and evacuation
  Sheltering needs based on displaced population, which is based on the inundation area
  Percentage of displaced households seeking shelter based on:
    Income: lower income, greater shelter needs
    Age: young and elderly families have greater shelter needs
    Home ownership: currently assumed to have no impact because of evacuations but can be edited
    Ethnicity: research shows no correlation with shelter needs for flood events but can be edited

## Slide 22: Shelter
Evacuation factors:
  Typical curb height: 6 inches
  Vehicles can be shifted by 12 inches of moving water

## Slide 23: Shelter
Weighting and modification factors are based on demographics
  Income is typically the most important consideration.
  Local information on income/age is typically not available due to privacy; therefore, use the defaults in most cases.
Note: Weighting factors must add up to 1, while modification factors can equal 1 or less
Class | Description | Importance Factors
IW | Income Weighting Factor | 0.8
AW | Age Weighting Factor | 0.2
EW | Ethnic Weighting Factor | 0
OW | Ownership Weighting Factor | 0
IM1 | Household Income < $10,000 | 0.4
IM2 | $10,000 < Household Income < $15,000 | 0.3
IM3 | $15,000 < Household Income < $25,000 | 0.15
IM4 | $25,000 < Household Income < $35,000 | 0.1
IM5 | $35,000 < Household Income | 0.05

## Slide 24: Direct Economic Loss Estimates
General Building Stock
Key Components
  Content value (percent of building replacement cost) for different occupancies
  Annual gross sales by occupancy
  Typical rental costs
  Relocation expenses
  Income by occupancy
  Replacement values for the various transportation and utility facilities

## Slide 25: Direct Economic Loss Estimates
  General Building Stock
  Inventory estimates based on 2006 U.S. dollars
  Restoration times based on building damage, clean-up, inspections, permits, approval, and contractor availability
Specific Occupancy | Annual Gross Sales Per SqFt
COM1 | 53
COM2 | 77
IND1 | 713
IND2 | 226
IND3 | 697
IND4 | 656
IND5 | 437
IND6 | 768
AGR1 | 148

## Slide 26: Direct Economic Loss Estimates
  General Building Stock
  Income losses depend on restoration time for business operations.
Specific Occupancy | Rental Costs Per SqFt Per Month | Rental Costs Per SqFt Per Day | Disruption Costs Per SqFt
RES1 | 0.79 | 0.03 | 0.94
RES2 | 0.55 | 0.02 | 0.94
RES3A | 0.71 | 0.02 | 0.94
RES3B | 0.71 | 0.02 | 0.94
RES3C | 0.71 | 0.02 | 0.94
RES3D | 0.71 | 0.02 | 0.94
RES3E | 0.71 | 0.02 | 0.94
RES3F | 0.71 | 0.02 | 0.94
RES4 | 2.36 | 0.08 | 0.94

## Slide 27: Direct Economic Loss Estimates
User-Defined Facilities:
  Damage functions are assigned individually to each structure based-upon the occupancy, number of stories, first floor height, foundation type and hazard zone.
  Hazus computes the percentage of damage to each structure, contents, and inventory.
  Based-upon the percentage of damage, Hazus will calculate the flood losses for the building, contents, and inventory.
  Other results that are available for GBS inventories (e.g., business interruption losses, debris, combined losses) are not available for user-defined structure analysis

## Slide 28: Running the Analysis
  The types of data provided for your study region limit the analysis modules that you can run
  Analysis can be re-run to reflect changes in inventory
  New analysis overwrites previous results

## Slide 29: Running the Analysis
When creating a new scenario, select all depth grids Choose the analysis type "Full Suite of Return Periods" |  | 

## Slide 30: Activity 6.2: User-Defined Depth Grid
Goals:
  Create the study region.
  Review analysis options.
  Run the analysis.
  Review damage functions.
Time: 20 minutes

## Slide 31: Activity 6.2: Tasks
Task 1: Create a new study region.
Task 2: Import depth grid(s).
Task 3: Select analysis options and run the analysis.
Task 4: View and modify the damage functions.

## Slide 32: Annualized Loss (AAL)
  An estimate of future direct economic losses that are presented as the average cost per year
  Provides a community with a common economic frame of reference they can use to compare flood losses against other hazards
  Can be used in determining the financial feasibility of mitigation projects

## Slide 33: Annualized Loss: Methodology
  Hazus calculates the losses for each return period in all damaged census blocks.
  AAL = L10C10 + L25C25 + L50C50 + L100C100 + L500C500
  The losses (L10→500) for each return period are weighted by the frequency constant (C10→500) and then added together.
Return Period | Frequency Constant
C10 | 0.03
C25 | 0.04
C50 | 0.015
C100 | 0.009
C500 | 0.006

## Slide 34: Annualized Loss: Example
Shorter return period losses have a greater contribution to AAL total than longer return periods.
Direct Economic Loss for Buildings
Return Period | Building Loss | RP Constant | AAL Loss
10 | $41,094,000 | 0.03 | $1,232,820
25 | $60,589,000 | 0.04 | $2,423,560
50 | $72,826,000 | 0.015 | $1,092,390
100 | $85,298,000 | 0.009 | $767,682
500 | $113,565,000 | 0.006 | $681,390

## Slide 35: Annualized Loss
  General Building Stock AAL: produces the full suite of results for each census block.
  User-Defined Facility AAL analysis: creates structure-by-structure results for the entire inventory.
  Only building, content, and inventory losses are available.

## Slide 36: Exercise 6.3 Annualized Losses
Goal:
  Find annualized losses based on varying return periods.
Time: 30 minutes

## Slide 37: Exercise 6.3 Tasks
Task 1: Open study region and create new scenario.
Task 2: Find average annualized losses for the full suite of return periods.
Task 3: View and map results.

## Slide 38: Lesson 6: Review
  Give examples of factors that impact the accuracy of the general building stock analysis.
  What are the parameters that can be modified to increase the accuracy estimates of the need for public shelter?
  Name an example of a type of debris that is not modeled by Hazus.
  For which types of inventory are loss estimates based on the presence of water rather than the depth of water?
  What return periods are used to calculate the AAL?

## Slide 39: Questions?