## Slide 1: Lesson 7: Flood Model Results

## Slide 2: Lesson 7: Goal and Objectives
Goal: To explore the loss estimations that the flood model produces.
After completing this lesson, you will be able to:
  Navigate through the Results menus.
  Interpret the results.
  Identify ways to avoid misusing the results produced by the Flood Model.

## Slide 3: Review of Results
  Hazard maps:
    Flood depth
    Floodplain boundary
  Building losses:
    By occupancy, building type, full replacement and depreciated replacement value
    Building, content, and inventory losses
    Costs of relocation, wage, income, and rental loss
    Direct employee output losses and employment loss (days)

## Slide 4: Review of Results
  Essential facilities:
    Building and content losses
    Functionality assessment (yes/no)
    Restoration time to 100% functionality
  Lifeline losses (for selected components):
    Losses to structures and equipment
    Functionality assessment (yes/no)
  Vehicles and agriculture losses
  Shelter requirements

## Slide 5: Viewing Results
  Analysis results can be viewed for a specific scenario.
  Options are enabled after the results category (return period or mixed) is selected.

## Slide 6: Mapping Tables
  Click on a column header to highlight the column.
  Click Map to create a layer in your map document.

## Slide 7: Exercise 7.1: Viewing Results
Goals:
  View the analysis results.
  Map the results.
Time: 35 minutes

## Slide 8: Exercise 7.1: Tasks
Task 1: Open the previous scenario for Mecklenburg County.
Task 2: View and map three results options.
Task 3: Discuss in your group.

## Slide 9: Interpreting Results
General Building Stock (GBS) tables populate only for damaged inventory / blocks.
  All GBS result tables will have the same number of records; a block only has to show damage in one table.
  Total columns represent potentially damaged inventory based on portion of the block that is flooded
‘Total’ columns represent potentially damaged inventory based on portion of block that is flooded.
  Subtract ‘None’ column to get actually damaged inventory

## Slide 10: Interpreting Results
Why is the results table blank?
  You did not select the module in the Analysis Options window.
  The computer ran out of disk space.
  There is no damage.

## Slide 11: Interpreting Results
  General building stock reports summarize individual census block values.
  Review the tables to identify any possible overestimates, especially in scenarios that occupy small geographic areas.

## Slide 12: Interpreting Results
Aerial photography can be a valuable resource for assessing the reliability of the loss estimations for GBS inventory.

## Slide 13: Exercise 7.2: Mitigation Options
Goals:
  Update the General Building Stock inventory in a mitigation scenario and review the reduction of losses.
Time: 15 minutes

## Slide 14: Exercise 7.2 Tasks
Task 1: Apply mitigation to damaged structures
Task 2: Re-run the analysis
Task 3: Review the updated results

## Slide 15: Exporting Tables
  Export tables to multiple formats: TXT, CSV, XLS, HTML, XML
  Right-click on any table for the context menu.
  Save in any of the formats to view, modify, and edit information in external software.

## Slide 16: Export to Shapefile or Geodatabase
  Right-click on the layer in the table of contents.
  Select data and then export data.
  Change the save as type to shapefile.
  Change to geodatabase feature class if saving to a geodatabase.

## Slide 17: Hazus Export Tool
  Python script and an ArcToolbox (.tbx) file
  Located in the Hazus program files directory (\Hazus-MH\BIN\Tools) on the computer’s hard drive
  Create a folder named “ExportResults” in the HazusData directory to store export results, if it does not already exist.

## Slide 18: Reports

## Slide 19: Interpreting Results
Remember that the loss estimations are based on three key inputs:
  Accuracy of the hazard
  Accuracy of the inventory
  Reliability of the damage functions
Avoid quoting exact numbers from reports or tables, especially to people who are not familiar with how models work.

## Slide 20: Discussion 7.3: Economic Impacts
Goal: Discuss how you would use Hazus to answer the following question:
Question: What is the economic impact of the flood?
Groups: 3-6 people
Time: 15 minutes

## Slide 21: Communication Tips
Tips for effective communication:
  Speak clearly without technical jargon.
  Be patient.
  Listen attentively.
  Ask for clarification needed.
  Remember all participants involved are here to help others.
  Remind partners of limitations of Hazus model.

## Slide 22: Lesson 7: Review
  Provide examples of methodologies to prepare flood risk information.
  What are possible reasons for no losses being reported in a results table?
  What is the best source of information for obtaining detailed (census block level) information about General Building Stock economic losses?
  What are the outputs of the User-Defined Facility analysis?
  What options exist for validating the outputs of the Hazus flood model?

## Slide 23: Questions?