## Slide 1: Lesson 8: Hazus Flood Internal H&H Methodology

## Slide 2: Lesson 8: Goal and Objectives
Goal: To review the Level 1 flood hazard methodology for the Hazus Flood Model.
After completing this lesson, you will be able to:
  Outline the steps of running a level 1 scenario.
  Identify the Hazus inputs for the flood model.
  Identify differences between riverine and coastal flood hazard modeling.
  Create flood hazard information without a user-defined depth grid.

## Slide 3: Type of Floods in the Hazus Flood Model
  The Hazus Flood Model analyzes both riverine and coastal flood hazards
  Flood hazard is defined by a relationship between depth of flooding and the annual chance of inundation to that depth
  Options exist for enhancing the ‘Basic’ hazard options.
    EX: specific discharges, LiDAR derived DEMs
  Hazus does not model dam breaks

## Slide 4: Input Data

## Slide 5: Riverine Floods
  Occur when water in the river rises and overflow its banks
  Heavy rainfall or snowmelt can cause riverine flooding

## Slide 6: Hazus Flood Hazard Determination
The value of Hazus generated flood hazard options:
  Many communities with flood risk do not have detailed studies.
  Hazus can often provide a reasonable estimate of flood inundation area as a starting point.
    Flood boundary may exist, but lack a flood grid.
    No flood elevations exist or a lack of flood-frequency information.

## Slide 7: Riverine Flood Hazard Process
Return Period and Discharge

## Slide 8: Default Riverine Hazard Data
  Data/FL/Hydro folder
  3.75 GB of other default flood hazard data
  Riverine Geodatabase = “FlAnRivInput.mdb”
  Extent of watersheds intersecting the study region sufficient for riverine hazard calculations
  Coastal Geodatabase = “FlAnCoastInput.mdb”
  Feature classes/tables
    Shoreline
    Dune reservoirs
    Wave parameters

## Slide 9: Required Input Data
  Topography/Terrain (Digital Elevation Model)
    Esri grid processed to bare-earth conditions.
    Tutorials aid in conversion of various topographic data (spot elevations, contours, TINs) to the grid format.
    The User Data interface within Hazus can determine the required DEM for your study region.
  The Level 2 user should note that in some cases they will need to bring in a DEM layer sufficient to meet the extent requirements defined for Level 1 users

## Slide 10: Terrain Surface
  Required DEM extents are automatically determined by Hazus.
  Supplied by The National Map (TNM), formerly known as National Elevation Dataset (NED)
  Terrain Data in Esri GRID format (Ex. High resolution community/county specific LiDAR, NED 10m or NED 30m)

## Slide 11: Download DEM from TNM
  NED data can be downloaded through the User Data window.
  1 Arc Second resolution for most of US
  You may select a higher resolution from the “Select NED Resolution” drop-down list if other resolutions are available.
  Recommend 30m DEM for this type of analysis
  Additional data can be downloaded from USGS National Map and imported.

## Slide 12: Other DEM Resources - Earth Explorer
Space Shuttle Radar Topography Mission (STRM)
In late 2014, the United States government released the highest resolution SRTM DEM to the public. This 1-arc second global digital elevation model has a spatial resolution of about 30 meters. Also, it covers most of the world with absolute vertical height accuracy of less than 16m.
ASTER Global Digital Elevation Model (ASTER GDEM-2)
ASTER GDEM-2 (https://earthexplorer.usgs.gov/) has a global resolution of 90 meters with a resolution of 30 meters in the U.S.. ASTER GDEM-2 is considered a more accurate representation than the SRTM elevation model in rugged mountainous terrain

## Slide 13: User Provided DEMs
  User DEM can be used in lieu of NED.
    User needs to provide DEM to cover the entire watershed analysis area for riverine analysis.
    All input data must be in the same coordinate system and vertical units.
    ‘Coarse’ DEMs will be resampled to resolution of higher resolution DEM.
** Reminder:
  DEM now accepted in FLT and IMG formats if downloaded through USGS in-Hazus.
  The DEM must cover the entire study area.
  LiDAR can be used, however users should use caution as LiDAR tends to be very high-resolution and may not work.
  Hazus may have trouble processing a high-resolution LiDAR DEM for a study region larger than a few census tracts.

## Slide 14: Hazus DEM Processing
Processes applied to input DEM(s):
  Merge
  Clip
  Project
  Convert vertical units to feet
  Hillshade
Output DEM always has vertical units of feet which means flood depth grid units are in feet.

## Slide 15: DEM Output Datasets
Output stored in the study region RegionDEM folder
Grids
  ClipDEM
  Hillshade
Feature classes
  ReqDEMPolygon

## Slide 16: Required Input Data
Flood Elevation Cross Sections
  Line feature class.
  Cannot intersect each other but should intersect floodplains.
  Must be attributed with flood surface elevation for desired return period.
  Discharge values are not used except for interpolating additional flood depth grids.
BFE Polygons:
  Polygon feature class attributed with 100-yr flood elevations and 100-yr flood zones.
  Users should attribute polygons with AO depths if AO zones exist.

## Slide 17: Required Input Data
Floodplain/Analysis Boundary:
  Polygon feature class
  Must be single contiguous polygon
  Helps define the limits of analysis
  Potential source: DFIRM
  Riverine: floodplain boundary
  Coastal: analysis boundary

## Slide 18: Riverine Centerline
  “Ball” expands and contracts along flood plain boundary in conveyance areas.
  Centerline represents the center of the floodplain, not the center of the stream.

## Slide 19: Riverine Cross Sections
  Define your own upstream and downstream limits to tailor your study area
  Extensions: a series of buffers created between the centerline and the bounding polygon
  Cross sections are extended to bounding polygon if necessary

## Slide 20: Riverine Flood Elevation Points
  Points: Flood elevation points at regular intervals are interpolated between cross sections
  Grid: Flood surface is interpolated from elevation points

## Slide 21: Riverine Flood Elevation Points
Flood Depth Grid = Water Surface Elevation - Ground Elevation

## Slide 22: Riverine Flood Elevation Points
  Requires pairs of discharges and elevations for at least three return periods.
  Can build depth grids for return periods not included in input flood elevation data.

## Slide 23: Additional Depth Grid Resources
  FEMA Digital Flood Insurance Rate Map (DFIRM)
    Base flood elevation or cross sections from the H&H studies
    Cross sections can be interpolated to create a flood surface
  High Water Mark (HWM) data
    Point data collected using high resolution Real time Kinematic (RTK) GPS systems
    Points used as foundation for interpolating maximum flooding extent

## Slide 24: Generate Stream Network
  Necessary for riverine flooding scenarios.
  Not required if you are only running Scenarios with user-supplied flood hazard data.
  Process includes:
    Stream delineation
    Consideration of flow direction and accumulation
    Generation of drainage network

## Slide 25: Stream Delineation
Build a synthetic stream network from the DEM
  Fill sinks
  Flow direction
  Flow accumulation
  Determine threshold streams
  Stream to feature (raster to vector conversion)
  Process log named “FlHazardLog.txt” in the study region folder
NOTE: Additional datasets used in hydrologic modeling: Flow length, Watersheds

## Slide 26: Flow Direction and Accumulation
  Flow direction: Direction in which water would flow if poured at that cell onto the terrain.
  Flow accumulation: Represents total amount of water flowing through each grid cell and depends on the directions.

## Slide 27: Drainage Network
  Includes grid cells for which the flow accumulation is higher than a certain threshold.
  Each grid cell represents an area (cell size)².
  Threshold is defined in terms of number of grid cells or drainage area.
  Threshold streams: Collection of grid cells meeting the accumulation threshold are streams.

## Slide 28: Drainage Network
  Density of network determined by user-defined drainage area
  Larger drainage area generates fewer, larger streams
  Smaller drainage area generates more, smaller streams

## Slide 29: Scenario Definition
  Select stream reaches for riverine flooding.
  Select lengths of coastline for coastal flooding.
  Consider your plans for the flood model when defining your scenario:
    Users that plan on modifying the functions/parameters in the Damage & Loss Estimate Analysis should use the “Save As” capability to compare results between scenarios, otherwise they are overwritten.
    Users that plan on modifying the Hazard analysis do not need to use the “Save As” capability.

## Slide 30: Riverine Scenario Definition
  Identify the reaches to be analyzed through definition of a Scenario.
  Subsequent computations through the hazard and analysis menus will be performed only on scenario reaches.

## Slide 31: Riverine Scenario Definition Output
  Output stored in the scenario Riverine folder
  Geodatabase “CaseOutput.mdb”
  Feature dataset “Hydrology”
  Feature class “ChosenReaches” added to the map in red

## Slide 32: Hydrologic Analysis
  Hydrology option in Riverine submenu appears after scenario definition.
    Scenario definition identifies the reaches to be analyzed.
  Recommended watershed-by-watershed basis creates two options:
    One scenario for every affected watershed.
    Edit a single scenario adding one watershed at a time.

## Slide 33: Hydrologic Analysis
  Common methods:
    Numerical modeling: Precipitation, DEM, soil conditions, rainfall data
    Stream gage data: USGS discharge values
    Regression analysis: Derived topographic parameters and default databases
  Hazus approach: determine discharge-frequency relationship for each reach in scenario
    Step 1: USGS regression equations
    Step 2: Gage adjustment
    Step 3: Main stream adjustment

## Slide 34: Hazus Hydrologic Analysis
  Output = peak discharges, not hydrograph
  No rainfall-runoff modeling
  Hydrologic analysis is not necessary if you are providing results from another flood study. These might include:
    Entering discharges
    Quick Look: drawing a polygon having a constant flood depth
    Enhanced Quick Look: providing a flood plain boundary and DEM
    Providing a flood depth grid
    HEC-RAS input

## Slide 35: Hydrology Process Output
Chosen Reaches
QFreq

## Slide 36: Floodplain Delineation Options
  Select level of flood to analyze for each selected stream reach.
  Analysis Options
    Suite of return periods
    Single return period
    Single discharge

## Slide 37: Hazus Hydraulic Approach
  Modeling input data:
    Peak discharges (Used in Hazus)
    Cross section description (Used in Hazus)
    1-D and 2-D flow field (Used in Hazus)
    Manning’s n (defaults are created from NLCD)
    Bridge geometries
    Expansion/contraction coefficients
    Boundary conditions
  Hazus accounts for both conveyance and backwater areas.
    Conveyance: Water flows upstream to downstream, flood elevations decay between adjacent cross sections
    Backwater: Water backs up from the main channel to a tributary or low-lying area

## Slide 38: Hazus Hydraulic Outputs
  Flood elevations at cross-sections
  Flood depths
  Identification of the floodplain boundary

## Slide 39: Hydraulics Output Datasets
  Depth grid stored in the scenario Riverine\Depth folder
  Naming convention
    RPD[x] for return period analysis
    Mix0 for discharge or mixed return periods

## Slide 40: Riverine Output Datasets
  CaseOutput geodatabases are stored in the Scenario\Riverine folder
  Floodplain boundary in the "Hydrology" feature dataset
    Boundary polygon
    Chosen reaches
    Problem reaches
    ShedMask

## Slide 41: Riverine Output Datasets
  Reach outputs stored in Hydraulics folder
  Feature datasets named by reach number
    Cross sections
    Conveyance boundary
    Water surface elevation points

## Slide 42: Riverine Output Datasets
  A: Depth grid in blue (units are in feet)
  B: Floodplain boundary cross-hatched in orange
  C: Floodplain will contain islands if appropriate

## Slide 43: Exercise 8.1: Discharge Data
Goal: Navigate the USGS discharge site to identify discharge values for use in Hazus.
Time: 15 minutes

## Slide 44: Exercise 8.1: Tasks
Task 1: Find Discharge Points for an Event

## Slide 45: Exercise 8.2: Riverine Discharge Analysis
Goal:
  Create a study region
  Set up the stream features
  Import Finished Stream Delineations and Create a Scenario
  Run analysis and view results
Time: 35 minutes

## Slide 46: Exercise 8.2: Tasks
Task 1: Create Study Region
Task 2: Set up Stream Features in El Paso
Task 3: Import Finished Stream Delineation and Create a Scenario
Task 4: Run the Analysis and View the Results

## Slide 47: Capstone Exercise Preparation
  This is the end of today's material, tomorrow will resume the rest of Lesson 8.
  Begin Groupwork
    Begin analysis

## Slide 48: Capstone Exercise Preparation
Goals:
  Choose an analysis to run.
  Download required data.
  Begin processing data.
Time: 1 Hour 30 minutes

## Slide 49: Coastal Floods
  Occur along the coast
  Low-lying coastal areas are more prone
  High intensity storms can cause coastal flooding (think Hurricane or Nor'easter)
  Tsunamis can cause coastal flooding

## Slide 50: Modeling of Coastal Floods
  Hazus has two methods for generating the rise of water due to storm winds:
  Coastal Model:
    Can be used along the Atlantic, Pacific, Gulf of Mexico, and Great Lakes.
    Nor’Easters, mid-latitude cyclones, sub-tropical storms – types of weather events that can create this type of coastal water rise.
  Hurricane Storm Surge Model:
    Can only be used in the 22 coastal states that can be modeled with the hurricane wind model.
    Only simulates ocean rise from hurricanes.

## Slide 51: Coastal Model Overview
Basic Analysis Process

## Slide 52: Coastal Hazard Overview

## Slide 53: Default Coastal Hazard Data
  National shoreline
  Coastal dune reservoir tables for each major coastline (Pacific, Atlantic, Great Lakes)
  Default wave parameters

## Slide 54: Default Shoreline
  Shorelines are generalized. Islands that are close to each other are grouped together.
  Narrow bay entrances or river mouths less than ½ mile in size are closed off – prevents shoreline from following rivers upstream.
  Transects capture DEM under closed off areas so that hazard can be calculated.

## Slide 55: Transects
  Approx. 1000 feet spacing.
  Lengths vary by county as specified by a default table.
  Query DEM along the transect with an interval of cell size / 2.
  Transect profiles are generated to be used in simplified WHAFIS calculations.

## Slide 56: Coastal Transect Analysis
  Analyses performed along shore-normal transects, affected by an increased inference line.
  Transect spacing is uniform based on shoreline characteristics that are closer in complex terrain.

## Slide 57: Build 100-Year Elevation Grid
  Define attribute fields for flood elevation and hazard zone of the 100-year flood.
  Identify AO zone depth field (if applicable).
  Compute 100-year flood elevation and hazard zone grids.
  NOTE: FEMA flood zone definitions can be found at http://msc.fema.gov

## Slide 58: Shoreline Wizard
  Shoreline Definition
  Draw generalized shoreline at mean sea level (tidal areas) or IGLD chart datum (Great Lakes):
    Used to orient transects.
    NOTE: Avoid following small-scale changes in shoreline orientation.

## Slide 59: Shoreline Characterization
  Segments shoreline into pieces of common shoreline characteristics and wave conditions.

## Slide 60: Shoreline Characterization
  100-Year Flood Conditions
  User must enter 100-year stillwater elevation and vertical datum.
  Auto-calculated (or user specified) based on default ratios.
    Other stillwater elevations
    Significant wave height
    Peak wave period

## Slide 61: Shoreline Characterization
  Find the table in your flood insurance study with stillwater elevations
  Note if the SWEL includes wave setup
Order from the FEMA Map Service Center

## Slide 62: Wave Effects
  Wave setup: Increase in the stillwater level caused by waves breaking near the shoreline.

## Slide 63: Hazus Wave Height Modeling
  Overland waves are affected by local wind conditions, water depth, and obstructions (buildings, trees).
  Wave regeneration algorithm is based on regional wind speeds and return periods.
  Same basic principles as FEMA’s WHAFIS model:
    Wave heights are depth-limited
    Wave height = 0 when (SWEL+Setup-DEM) = 0
    Assume 70% of the controlling wave height lies above the SWEL + wave setup

## Slide 64: Frontal Dune Analysis
  FEMA has developed guidelines for dune analysis

## Slide 65: Frontal Dune Analysis
  Frontal Dune Analysis tool permits you to change location of dune peak and toe
  Locations affect erosion calculations

## Slide 66: Coastal Output Datasets
  Output stored in the scenario\Coastal\Depth folder
  Grids: Flood depth
  Naming convention:
    RPDxxx for return period analysis, where xxx=500 for 500 year event
    Mix0 for other analysis

## Slide 67: Coastal Output Datasets
  Scenario\Coastal folder
  Geodatabase = “CaseOutput.mdb”
  Floodplain boundary and hazard zones located in the “Coastal” feature dataset

## Slide 68: Output Dataset
  Depth grid = blue
  Floodplain boundary cross-hatched = orange

## Slide 69: Coastal Dataset
  Output coastal dataset raster

## Slide 70: Additional Notes
  Flood depths are converted to feet, regardless of vertical units of the input DEM(s)
  Repeated analysis will overwrite existing output
  Process log named “FlHydraulicsLog.txt” stored in the scenario folder
  Floodplain boundary oriented to flow centerline, not reach centerline

## Slide 71: Activity 8.3: Coastal Hazard
Goal: Perform a basic coastal hazard shoreline characterization and hazard computation
Time: 25 minutes

## Slide 72: Activity 8.3: Tasks
Task 1: Create a New Study Region
Task 2: Select the Flood Hazard Type
Task 3: Create a New Scenario and Define the Shoreline Limits
Task 4: Define the Flood Hazard
Task 5: Perform the Loss Estimation

## Slide 73: Lesson 8: Review
  What are the major steps in running a Level 1 flood model?
  What are inputs for the flood model?
  How do the riverine and coastal methodologies differ?

## Slide 74: Questions?