## Slide 1: Lesson 9: User-Defined Coastal Hazard

## Slide 2: Lesson 9: Goal and Objectives
Goal: To introduce the options that Hazus offers for integrating user-defined coastal flood hazard information into a Hazus study region.
After completing this lesson you will be able to:
  Use each of the available tools that Hazus provides for defining a flood hazard with user provided input.
  List both the advantages and limitations of each user-defined hazard tool available in Hazus.

## Slide 3: User-Defined Coastal Hazard Options
  Quick Look
  Enhanced Quick Look
  User-Defined Flood Depth Grid
    Import
    Create

## Slide 4: Coastal Hazard Output
Model calculates:
  Flood surface, considering wave height
  Flood depth
Flood model develops:
  A zones
  Coastal A zones
  V zones

## Slide 5: Quick Look and Enhanced Quick Look
  Same process as riverine – not dependent on flood type

## Slide 6: Coastal Hazard Causes and Depth Grids
  Coastal floods can be caused by hurricane storm surge, tsunamis, and rising sea level.
  Storm surge can be predicted by SLOSH or CERA depth grids
  Rising sea level has been predicted by NOAA depth grids
  Hazus is capable of modeling tsunami inundation.

## Slide 7: Sources for Depth Grids
  CERA - Coastal Emergency Risks Assessment
  NOAA’s Sea Level Rise Data
  SLOSH Display Program
  FEMA Flood Map Service Center

## Slide 8: Base Flood Elevation
  BFEs can be found on Flood Insurance Rate Maps (FIRMs) in the FEMA Flood Map Service Center
  Modeled elevation to which floodwater is anticipated to rise for a base flood
  A flood insurance premium is determined based on the BFE and a structure’s elevation

## Slide 9: Activity 9.1: Coastal Flood with SLOSH
Goal:
  Model a coastal flood using a SLOSH Depth Grid.
Time: 30 minutes

## Slide 10: Activity 9.1: Tasks
Task 1: Import SLOSH Depth Grid.
Task 2: Create New Hazus Flood Scenario.
Task 3: Run Analysis and View Results.

## Slide 11: Coastal Flood Erosion
  Coastal floods can cause beach erosion, which must be considered when subsequent floods occur.
  These places can have deformed DEMs and cause more flooding and wave impact in the future

## Slide 12: DEM Deformation
  After an oceanic earthquake event, coastal deformation can occur.
  This event can trigger tsunamis to occur, resulting in even more impacts in the deformed areas.

## Slide 13: Sea Level Rise
  NOAA has predicted the sea level rise and its depth in coastal areas for the United States
    Coastal flood viewer: https://coast.noaa.gov/digitalcoast/tools/slr.html

## Slide 14: Exercise 9.2: Combined Riverine and Coastal
Goal:
  Model a combined user-defined coastal and riverine flood scenario.
Time: 30 minutes

## Slide 15: Exercise 9.2 Tasks
Task 1: Create a new study region
Task 2: Download sea level rise data
Task 3: Define the hazard
Task 3a: Develop the Riverine Depth Grid
Task 4: Import Depth Grids
Task 5: Create and run the scenario

## Slide 16: Lesson 9: Review
  What are the inputs required to complete a coastal analysis?
  What are possible sources of the information required to do a coastal Level 2 analysis?
  Which of the available options for defining a coastal hazard offers the most potential for accuracy?

## Slide 17: Questions?