## Slide 1: Lesson 10: Advanced Tsunami Analysis

## Slide 2: Goal and Objectives
Goal
This lesson will describe how to conduct advanced tsunami analyses for losses and casualties.
After completing this lesson you will be able to:
  Discuss advanced tsunami analysis options
  List parameters that may be edited
  Understand inputs for combined earthquake tsunami scenarios

## Slide 3: Hazard Analysis User Input

## Slide 4: User Defined Inventory Data
  Inventory | User-defined Facilities menu option enables user-specific datasets to be analyzed through the Hazus methodologies, providing more accurate results.
  Use CDMS to populate the UDF tables.
  On aggregation, the data will be added to a new tsunami UDF table (tsUserDefinedFlty).

## Slide 5: User Defined Inventory Data (cont.)
Attribute | Description | Why is it needed?
Record Identifier (ID) | A unique identifier for each record. Hazus will create its own primary key (it does not prompt the user for one since there is no guarantee it is unique). Map this identifier to any column that is not used: COMMENT is a good candidate. | Hazus will output all results keyed by the ID it generates on import. If a join to the original data is needed, this attribute will be the only way to link the results to the original data.
Occupancy | Occupancy type per the Hazus classification. Map it to OCCUPANCY. | Analyses are based on the occupancy and/or building type.
Building Type | Occupancy type per the Hazus classification. Map it to OCCUPANCY. | Analyses are based on the occupancy and/or building type.
Design Level | Seismic Design Level. Map to DesignLevel. CDMS default is PC. | To assess lateral strength of structure for building damage.
First floor height | Top of Finished Floor Relative to Adjacent Grade (ft). Map to FirstFloorHt. CDMS default is 1, which represents slab on grade. | To assess content damage.
Building replacement cost | Cost ($) to replace the building in case of damage. Used by economic loss model. Map it to COST. CDMS will estimate based on RS Means table. | To assess building economic loss.
Content replacement cost | As above (in Building replacement cost) relating to building content. Map to Content Cost. CDMS will estimate based on % of building replacement. | To assess content economic loss.
Location | The location of the structure/facility can be supplied as latitude/longitude (in that case, Hazus will create the geospatial points), or directly when the table imported is a feature class. | Hazus needs location of structure to calculate the hazard. Hazus uses the location at import time to filter the points that do not fall within the study region (i.e., discarding any point that falls outside the study region).

## Slide 6: User Defined Depth Grids
  Sample Data are prepared for each level of analysis based on data provided for five of the PMEL forecast inundation model communities: http://nctr.pmel.noaa.gov/sim.html
  The hazard data (runup and velocity) were developed using NOAAs SIFT (Short-term Inundation Forecasting for Tsunamis) system found at http://nctr.pmel.noaa.gov/tsunami-forecast.html
  For additional information, including access to SIFT products, see http://nctr.pmel.noaa.gov.

## Slide 7: User Defined Casualty Data
  The Level 2 Casualty Analysis leverages the output from the USGS Pedestrian Evacuation Analyst (PED) ArcGIS tool, which assesses evacuation times to high ground.
  The tool can be found at: http://geography.wr.usgs.gov/science/vulnerability/tools.html
  Input data required:
    Travel Time to Safe Zone (depth = 0)
    Travel Time to Partially Safe Zone (depth < 2 meters)

## Slide 8: Advanced Tsunami Scenarios
Level 2: Depth-Above Ground Level (AGL) and Velocity
Level 3: Depth (H) and Momentum Flux (HV2)

## Slide 9: AGL and Velocity (Level 2)
Input:
  Maximum Depth grid and Velocity grid dat in raster format, OR
  Maximum Depth and Velocity NetCDF NOAA SIFT (.nc) files
Units are defined using the drop down tabs under Metadata.

## Slide 10: Depth and Momentum Flux (Level 3)
Input:
  Median Depth grid in raster format
  Median Momentum flux grid
Must be in raster format.
Assumes user-provided data are already in required units.

## Slide 11: Activity 10.1
Student Activity
  In this activity, you will run a Level 2 and 3 Tsunami scenario.

## Slide 12: Casualty and Evacuation Parameters
Casualty Estimation Parameters
  The travel time for people to evacuate tsunami danger zones (evacuation travel time).
  Evacuation travel time provides information on how long it will take people to safely reach higher ground.
  Travel time can be estimated once a safe haven is identified.
Evacuation Parameters
  Only pedestrian evacuation is considered
  Critical factors:
    Prior experience and knowledge of tsunamis
    Educating people to evacuate in a timely manner
    Effective tsunami warning systems

## Slide 13: Modifying Analysis Factors
  Analysis | Parameters menu allows the user to define casualty and building economic loss parameters.
  Casualty Parameters:
    Community Preparedness Level
    Walking Speed and Walking Speed Reduction
  Building Economic Parameters
    Percent Loss
    Repair Time
    Building Contents
    Income Loss Data
    Business Inventory Damage

## Slide 14: Community Preparedness Level
  Based on FEMAs methodology, concerning the time required between the warning and the evacuation of the community.
  The classifications of Good, Fair, or Poor are based on tsunami hazard preparedness level.
    Determined based on factors such as the condition of shore-protection structures, emergency loud speakers, preparation of evacuation routes and signs, a communitys risk management level, and/or the education level for tsunami awareness.

## Slide 15: Walking Speed
Based on the USGS Pedestrian Evacuation Analyst Tool for populations under age 65.
Walking Speed Reduction Parameter
  Included to account for the difference in evacuation walking speed for population over 65 years old.
  Can be used to reduce walking speeds for either category to represent local or post-earthquake conditions.

## Slide 16: Percent Loss
  Replacement costs (damage state = complete) were derived from Means Square Foot Costs, for Residential, Commercial, Industrial, and Institutional Buildings.
  Selected Means models have been chosen that represent the 33 occupancy types.
  Dollar values shown should only be used to represent costs of large aggregations of building types. If costs for single buildings or small groups (such as a college campus) are desired for more detailed loss analysis, local building-specific cost estimates should be used.
  Since a building has both structural and non-structural repair costs, those are provided for each occupancy type by damage state.

## Slide 17: Repair Time
  Default building repair and clean-up times are provided within Hazus.
  Presented as a function of both amount of damage and occupancy class.
  Default values are broken into two parts:
    Construction time (the time to do the actual construction or repair)
    Extended time (includes construction plus all of the additional delays)

## Slide 18: Building Contents
  Furniture or equipment that is not integral within the structure, computers and supplies.
  Does not include inventory or non-structural components (e.g., lighting, ceilings, mechanical/electrical equipment).
  Damage expressed in terms of the % damage based on depth of water at the building relative to the finished floor.
  Assumptions (complete damage state):
    EQ complete damage state - 50% of contents can be retrieved.
    Tsunami - as the saturated or washed away contents are less likely to be salvaged, it is assumed that 100% of the contents are lost.

## Slide 19: Income Loss Data
  Hazus only considers disruption costs that may include the cost of shifting and transferring and the rental of temporary space.
  Relocation expenses are assumed to be incurred only by building owners and measured in $/sf/month.
  Income losses occur when building damage disrupts commercial activity.
    Income will vary considerably depending on regional economic conditions.
    U.S. Department of Commerces Bureau of Economic Analysis reports regional estimates of capital-related income by economic sector.

## Slide 20: Business Inventory Damage
  Business inventories vary by occupancy.
  Default values are derived from annual gross sales by assuming that business inventory is some percentage of annual gross sales.

## Slide 21: Activity 10.2
Student Activity
  In this activity, you will change analysis parameters and see the difference between the results.

## Slide 22: Post-Earthquake DEM
When a Tsunami analysis involves a Near Source earthquake, it is recommended that the DEM used in the scenario be based on deformed (post-earthquake) topography.
  Allows for more accurate inundation modeling by factoring in any ground deformation caused by the earthquake.
  If the ground surface elevations relative to sea-level have decreased, the inundation and losses could be more extensive.
  See the Tsunami Model Technical Guidance document for more information.

## Slide 23: Combined EQ and Tsunami Scenario
  Build a multi-hazard (earthquake and tsunami) study region that includes a shoreline (i.e., must be a coastal region).
  Available for Near Source tsunami hazards, where the earthquake ground shaking impacts the study region in:
    Alaska
    Oregon
    Washington
    California
    Hawaii
    Puerto Rico

## Slide 24: Combined EQ and Tsunami Scenario (cont.)
  Results can be viewed only in the Tsunami Model.
  Output is in the form of results tables, maps, and reports.
  Accessible from the Results menu on the toolbar for
    Combined GBS
    Combined User Defined Facilities
    Casualties

## Slide 25: Combined Analysis Reports
  Combined Analysis reports are available under the following tabs in the Summary Report window:
  Losses
    Combined Direct Economic Losses for Building
    Combined User Defined Facility Economic Loss Report by General Occupancy
    Combined User Defined Facility Economic Loss Report by Building Type
  Other
    Combined Earthquake and Tsunami Global Risk Report

## Slide 26: Combined Direct Economic Losses
  Capital Stock Losses
    Structural and Non-structural Damage
    Contents Damage
    Inventory Loss
  Income Losses
    Relocation Losses
    Capital Related Losses
    Wage Losses
    Rental Income Loss
  Total Loss

## Slide 27: Combined UDF Economic Loss
Displays the combined exposure and losses by general occupancy or building type for:
  Capital Stock Exposure (Building and Contents)
  Capital Stock Losses (Building, Non-Structural, Contents, Total)
  Loss Ratio (Building % and Content %)

## Slide 28: Activity 10.3
Student Activity
  In this activity, you will create a combined earthquake and tsunami region and run the analysis.

## Slide 29: Review
  List the analysis parameters that may be edited.
  What does the current version of the Tsunami Model NOT estimate?

## Slide 30: Questions?