## Slide 1: Lesson 11: Uncertainties and Sensitivity Analyses

## Slide 2: Goal and Objectives
Goal
This lesson identifies ways to address the uncertainties associated with modeling. After completing this lesson you will be able to:
  Understand the difference between error and uncertainty.
  Understand potential sources of uncertainty in Hazus analyses.
  Develop a good sense of what meaningful sensitivity analyses to perform.

## Slide 3: Error versus Uncertainty
Error is generally defined as the deviation of a measurement from the correct value. However in modeling, error is generally considered a recognizable deficiency in any phase or activity of modeling that is not due to lack of knowledge.
  Systematic error error that is constant from one measurement to another (easily corrected).
  Random error error that is NOT constant from one measurement to another (very difficult to address).
Uncertainty is a potential deficiency in any phase or activity of the modeling process that is due to lack of knowledge.
Errors in data lead to uncertainty in model results.
Uncertainty in model results also arises from modeling assumptions.

## Slide 4: Uncertainty and Modeling
Models like Hazus, which try to predict a future event or condition, generally have the greatest uncertainty because parameterization of the model requires many assumptions that have cascading effects for the model results.
Due to all of the assumptions within the Hazus earthquake loss methodology and the modelers selected hazard scenario, even when there is validation of model estimations with observed damages, losses, and/or casualties, the difference should be referred to as uncertainty and not error.

## Slide 5: Sources of Uncertainty
  Modeling assumptions
  Empirical approach
  Default data
  Interpretation
  Incidental error

## Slide 6: Sources of Uncertainty (cont.)
Modeling assumptions
  Occupancy to model building type relationships
  Default classifications for site specific data
Empirical approach
  Ground motion computation
  Damage models
Simplified example of an attenuation function

## Slide 7: Sources of Uncertainty (cont.)
Default data
  Outdated information [e.g., building age distribution]
  Positional accuracy [e.g., hospitals, runways, faults, etc.]
  Incomplete GIS data [e.g., schools, fire stations, utility facilities, etc.]
  Default replacement values for some economic data

## Slide 8: Sources of Uncertainty (cont.)
Interpretation
  Classification of hazard or any other inventory data
  Interpretation of damage states
Incidental errors
  Assigning wrong projection system for GIS data

## Slide 9: Treatment of Uncertainties
Hazus produces credible results, but no explicit treatment of uncertainties.
Variability of models is best evaluated by conducting multiple sensitivity analyses.
  Use different attenuation functions.
  Use a mix of occupancy to building type distribution matrices.
  Use different soil assumptions if no such data is available.

## Slide 10: Treatment of Uncertainties (cont.)
  Understand dependency of modules and parameters
  Enhance inventory data
  Replace predicted results with observed results
    e.g., use the USGSs ShakeMap observed ground shaking data

## Slide 11: Sensitivity Analyses
  Hazard Parameters
  Fragility Curves
  Capacity Curves
  General Building Stock
  Casualty Rates
  Restoration Functions
  Economic Data
  Sheltering Factors

## Slide 12: Loss Ratio
Loss Ratio = total loss / total exposure
  Represents the impact of the disaster by normalizing the losses.
  Can be used as Ball Park Uncertainty Metric for Loss Estimates.
Losses < $20 Million and loss ratio < 1% Noise
5% < loss ratio < 20% -Results off by as much as 200%
20% < loss ratio < 50% -Results off by as much as 150%
50% < loss ratio < 75% -Results off by as much as 100%
75% < loss ratio < 100% -Results off by as much as 50%

## Slide 13: Summary: Important Parameters
  Completeness of inventory data
  Use of observed ground motion data that reflects soil conditions and potential for ground failure
  Vulnerability classification for inventory data (e.g., correct building type or appropriate mix of building types for aggregate data)
  Stakeholders data:
    Economic (cost to repair and/or replace, content value, income data, etc.)
    Social (number of occupants, shelter capacity, etc.)
    Functionality (contingency planning)

## Slide 14: Review
  What is the difference between error and uncertainty?
  Identify the major sources of uncertainty in the Hazus earthquake model.
  What is a sensitivity analysis and how can it be use to describe or quantify the uncertainty in Hazus earthquake loss estimations?

## Slide 15: Questions?