## Slide 1: Lesson 12: Applications for Hazus and Capstone Activity

## Slide 2: Goals and Objectives
Goals
  To explore the applicability of Hazus for mitigation.
  To understand the capacity of Hazus in response and recovery applications.
After this lesson, you will be able to:
  Explain the usefulness of probabilistic scenarios.
  Identify the type of analyses to run to simulate potential benefits that help in the assessment of mitigation alternatives.
  List examples of how Hazus results can be used to support decisions in post-disaster situations.
  Complete a Capstone Activity.

## Slide 3: What is Mitigation?
  Mitigation is the effort to reduce loss of life and property by lessening the impact of disasters.
  This is achieved through risk analysis, which results in information that provides a foundation for mitigation activities that reduce risk.
  Hazus provides the opportunity for detailed risk assessment useful for mitigation applications.

## Slide 4: Using Hazus in Mitigation Applications
Probabilistic Scenarios
  Mitigation implies cost-effectiveness solutions, which implies the acceptance of some risk, thus the probabilistic approach.
Use in order to minimize bias in decision support:
  Resource allocation [e.g., for response and recovery]
  Cost-effectiveness analyses
Best approach may be Average Annualized Loss (AAL)

## Slide 5: About Mitigation Activities
  May consist of physical projects that directly reduce future risk and disruption
    Acquisition
    Retrofitting
  Other activities consist of processes that lead to policies
    Floodplain management
    Building code updates
  Some risk is inevitable
  Eliminating all losses and disruption is not feasible

## Slide 6: About Mitigation Activities (cont.)
Mitigation activities are aimed at reducing losses to the built environment
  Keep buildings as undamaged and accessible as possible.
  Keep lifelines intact and functional.
  Save lives and protect people.

## Slide 7: Cost-Effectiveness Evaluation
Mitigation Project:
  Address specific targeted buildings (site-specific).
  Cost-effectiveness is localized.
  Only direct economic savings can be calculated.
  Could use AEBM
  Increase community preparedness.
  Add an evacuation route.
Mitigation Activity:
  Site-specific & aggregate
  Cost-effectiveness is regional
  Direct economic, social, and indirect economic consequences can be assessed

## Slide 8: Assessing a Mitigation Strategy
  Use AAL to evaluate the net benefits of the strategy for the targeted categories.
  Consider the cost to implement this strategy.
  Decision making also affected by:
    Time horizon (note that demographics, infrastructure, and economic facts vary with time)
    Targeted stakeholders
  Estimate the cost-effectiveness using the benefit-cost ratio.

## Slide 9: Cost-effectiveness Example
Given the costs below, is it beneficial to perform a retrofitting of tilt-up buildings?
Example of retrofitting costs
Building Type | Cost ($ / sq ft.)
Tilt-Up | 1 to 2
Steel Frame | 10 to 15
Concrete Frame | 25 to 30
Historical Building | 100
Parameter | Original Buildings | Retrofitted Buildings
Number | 100 | 100
Total Sq. Ft. | 1,000,000 | 1,200,000
Replacement Cost ($) | $125 million | $150 million
Average Annualized Loss | $0.40 million | $0.05 million
Cost-effectiveness Example
Example of 100 tilt-up buildings

## Slide 10: Hazus for Mitigation - Summary
What Hazus can do?
  Compute benefits as part of cost-effectiveness studies
  Identify sources of vulnerability in the infrastructure
  Model effects of future land use & development trends
  Evaluate and prioritize different mitigation alternatives
Several mitigation actions clearly supported:
  Building code regulations and enforcement
  Land use regulations and planning
  Prioritization for seismic upgrading, strengthening, retrofitting, and/or remodeling of targeted buildings

## Slide 11: Post-Earthquake Needs
  Understanding of magnitude and extent of impact.
  Assessment of social effects and shelter needs.
  Evaluation of economic consequences.
  Assessment of the status of critical infrastructure:
    Transportation
    Utilities
    Essential facilities
  Identification of additional emergency care needs.
  Drawing effective recovery plans.

## Slide 12: Post-Earthquake Applications - PDA
Hazus was deployed to support response to the M7.0 Alaskan Earthquake that struck near Anchorage on November 30, 2018.
Hazus analysis was incorporated into Alaskan Governor Dunleavy's Official Request to the White House for a Presidential Disaster Declaration.
FEMA IA leadership confirmed: Hazus estimates of building damage for the event (Hazus = Destroyed 5; Major 250) are a reasonable estimate of what is being found in the Preliminary Damage Assessments (PDA = 46 destroyed, 643 major) submitted by the State.

## Slide 13: Support for Recovery Applications

## Slide 14: Support for Recovery Applications (Cont.'d)
  Boundaries of damage from the earthquake ground shaking or tsunami inundation
  Understand which geographical areas need immediate attention
  E0179: Hazus for Disaster Operations has much more information about how Hazus can be used for response and recovery

## Slide 15: Damaged Structures & Utilities
  Residential, commercial, industrial, and non-residential buildings
  Essential and critical facility damage & functionality
  Utility systems impacts

## Slide 16: Community Needs
  Population at risk from hazardous materials releases
  Displaced population and shelter needs
  Hospital capacity to host injured victims
  Adequate shelter locations for displaced households
  Emergency water, power and ice for households without utilities
  Evacuation zones and routes

## Slide 17: Induced Hazards & Impacts
Inundation - Areas of flooding (potential dam or levee failure, etc.)
Debris - Information provided about the debris generated during the seismic event enabling users to prepare and to rapidly and efficiently manage debris removal and disposal

## Slide 18: Mitigation & Economic Recovery
  Residential and non-residential building repair and replacement costs
  Residential and non-residential contents losses
  Business interruption losses
  Transportation and utility system repair and replacement costs

## Slide 19: Hazus for R&R - Summary
The critical role of Hazus in supporting response and recovery activities is becoming more evident as disasters keep happening and the model evolves.
There is a need to automate some of these support functions to bridge the gap between:
  Technical details and expertise required to run Hazus effectively and efficiently, including modeling some of the critical parameters correctly.
  Easy-to-disseminate information in the most useful format for non-technical decision makers.

## Slide 20: Capstone Activity
  Break into groups of 4-6 persons.
  Use the Hazus Earthquake and/or Tsunami Model tools to address the scenario on the following slides.
  Deliver group presentations on the last day of class.
  The presentations will serve as the final exam for this course.

## Slide 21: Capstone Activity (Contd.)
  You will assume the role of consultants who have been asked by a county* how they should mitigate potential earthquake and/or tsunami damages and losses in their community
  You, as Hazus experts, have decided to use that tool to analyze the community's earthquake and/or tsunami risk.
  The results of your study will be presented at the monthly commissioners meeting (which happens to coincide with the last day of the class).
* The study area may be one of the class examples, or another example of your choosing.

## Slide 22: Capstone Activity (Contd.)
Required questions to answer: (Do not limit yourselves to these questions)
  What are the economic losses avoided?
  What are the number of lives saved?
  What is the reduction in the number of days the schools are potentially non-functional?
  What is the reduction in the number of students potentially needing shelter?

## Slide 23: Capstone Activity (Contd.)
Presenter guidelines
  Presentation should be prepared using PowerPoint slides and may include maps, tables, or other media as you deem appropriate.
  Information should be primarily derived from Hazus but may be supplemented by other sources.
  10 to 15 minutes in length
Commissioner's guidelines
  Class will assume the role of commissioners.
  Commissioners may ask any questions that they like related to the presentations.

## Slide 24: Review
  What is mitigation? How can Hazus be used in mitigation applications?
  What is the benefit of using a probabilistic scenario for mitigation projects in Hazus?
  What are five areas that Hazus can support in response and recovery after a disaster?
  How could Hazus be improved to be more efficient in response and recovery applications after a disaster?

## Slide 25: Questions?