## Slide 1: Lesson 2: Earthquake Inventory

## Slide 2: Goal and Objectives
Goal
This lesson provides a review of the inventory data included with the earthquake model, as well as an overview of tools and processes to update the inventory data.
After completing this lesson you will be able to:
  Describe the types of aggregate and site-specific inventory supported by the Hazus earthquake model
  List the options that Hazus provides for updating the default inventory

## Slide 3: Key Attributes
In general, earthquake results are sensitive to four categories of inventory parameters (among others):
  Location (longitude & latitude, whether site-specific or census-tract based)
  Classification (facility type, capacity, building type & other construction characteristics) with respect to earthquake vulnerability that affect seismic performance
  Valuation (cost of repair and replacement, business parameters)
  Societal (number of occupants)

## Slide 4: Activity 2.1
The Instructor will lead the class in exploring the Inventory Menu.

## Slide 5: What is the General Building Stock?
The GBS is an engineering based estimation of buildings for the US.
Represented by
  Floor area (Sq Ft)
  Replacement values ($)
  Building count
Data sources
  Residential from 2010 Census Data
  Commercial/Industrial from various sources
Northridge Earthquake, Calif., January 17, 1994 -- An aerial view of destruction caused by the 6.7 magnitude earthquake.

## Slide 6: General Building Stock - Occupancies
  7 General Occupancy Type Categories
  33 Specific Occupancy Categories
  You can view the categories from the Inventory menu
  Values are reported by their aggregated boundary

## Slide 7: General Building Stock - Building Types
General Building Types (All models)
  Concrete
  Steel
  Manufactured Housing
  Wood
  Masonry
Specific Building Types (Unique to each model)
  Flood
  Hurricane
  Earthquake
  Tsunami

## Slide 8: Specific Building Types - Examples
Specific Building Type | General Building Type | Description
C1H | Concrete | Concrete Moment Frame High-Rise
C1L | Concrete | Concrete Moment Frame Low-Rise
C1M | Concrete | Concrete Moment Frame Mid-Rise
C2H | Concrete | Concrete Shear Walls High-Rise
C2L | Concrete | Concrete Shear Walls Low-Rise
C2M | Concrete | Concrete Shear Walls Mid-Rise
C3H | Concrete | Concrete Frame with Unreinforced Masonry Infill Walls High-Rise

## Slide 9: Demographic Data
Selected information about populations and buildings necessary for one or more of the analysis functions in Hazus
Detailed by:
  Age
  Income
  Ethnicity
  Ownership
  Gender

## Slide 10: Activity 2.2
The Instructor will demonstrate how to:
  View General and Specific mapping schemes
  Modify a mapping scheme

## Slide 11: Site-Specific Inventory
  Provides specific locations of facilities
  Enables user to generate site-specific loss estimates versus an aggregated count of damages and losses

## Slide 12: Site-Specific Inventory Types
  Essential Facilities
  Transportation Systems
  Utility Systems
  User Defined Facilities
  Advanced Engineering Building Model (AEBM)

## Slide 13: Essential Facility Classes
Occupancy Class | Category | Description | Building Type | Building Height | Specific Occupancy
EFHS | Medical Care | Small Hospital | Concrete | Low | COM6
EFHM | Medical Care | Medium Hospital | Concrete | Mid | COM6
EFHL | Medical Care | Large Hospital | Concrete | Mid | COM6
EFMC | Medical Care | Medical Center | Concrete | Low | COM7
EFFS | Emergency Response | Fire Station | Concrete | Low | GOV2
EFPS | Emergency Response | Police Station | Concrete | Low | GOV2
EFEO | Emergency Response | Emergency Operations | Concrete | Low | GOV2
EFS1 | School | School | Brick | Low | EDU1
EFS2 | School | University | Concrete | Low | EDU2

## Slide 14: Transportation Systems
  Highway systems
  Railway systems
  Light rail systems
  Bus facilities
  Port facilities
  Ferry facilities
  Airport systems
* Each inventory grouping has multiple inventory items

## Slide 15: Utility Systems
  Potable water
  Waste water
  Oil
  Natural gas
  Electric power
  Communications
* Each inventory grouping has multiple inventory items

## Slide 16: User Defined Facilities
Used to perform a more refined site-specific analysis of inventory found in the General Building Stock.

## Slide 17: Advanced Engineering Building Model
(AEBM)
Create unique building models by choosing from:
  Specific occupancy class
  Specific building type
  Design level
* More on this later in the course

## Slide 18: Inventory Update Options
  Comprehensive Data Management System (CDMS)
  Study Region Update Tools
** The E0317: Comprehensive Data Management for Hazus course provides considerably more detail about inventory updates.

## Slide 19: CDMS
  System for integrating user provided site specific and aggregate data into the Hazus state databases.
  CDMS supported data includes:
    Site-specific
    Aggregate
    Building specific

## Slide 20: Study Region Update Tools
Edit Individual Records
  Most site specific and aggregate inventory tables can be edited within the Hazus study region Graphic User Interface (GUI).
  Useful for adding or editing individual records not practical for large inventory update projects.
Import Inventory
  Import MS Access feature classes.
  Hazus provides field mapping capabilities.

## Slide 21: Review
  The aggregate data is summarized by what geographic extent in the earthquake model?
  What is the difference between aggregate and site-specific inventory? List five examples each of aggregate and site-specific inventory.
  Why is it important to review the default Hazus data prior to running a model?
  How can the default data be updated?

## Slide 22: Questions?