## Slide 1: Lesson 3: Earthquake Specific Building Types

## Slide 2: Goal and Objectives
Goal
  Develop an understanding of how and when earthquake-specific building types impact the loss estimation process.
After completing this lesson, you will be able to:
  Explain the major differences between the building types contained within the Hazus inventory.
  Define the limitations of building classifications.
  List options for overcoming limitations.

## Slide 3: Importance of Specific Building Type
Specific Building Types (SBT) help identify in more detail:
  The type of framing
  Wall construction
  The building height (low, mid, high)
  Structural reinforcements
These components help us to better understand how a building will respond to ground shaking during an earthquake.

## Slide 4: EQ Specific Building Types
General Building Types are generally subdivided into SBT by:
  Number of stories
  Engineered / Non-engineered (design level, building quality)
Other implicit critical characteristics:
  Bracing
  Infill
  Cripple Walls
  Shear Walls
  Soft Story

## Slide 5: Mapping Schemes

## Slide 6: Building Height Classifications
Low Rise
  1 3 Stories
  (except URM 1-2 stories)
  The default assumption for all buildings in the Hazus inventory is that they are low rise
Mid Rise
  4 7 Stories
  (except URM 3+ stories)
High Rise
  8 Stories or more

## Slide 7: Design Levels
  Design Level reflects the relationship between quality and extent of damage…used to further classify each model building type.
  Design Levels:
    Pre - Code
    Low Seismic - Code
    Moderate Seismic - Code
    High Seismic - Code
    Low Seismic - Special
    Moderate Seismic - Special
    High Seismic - Special

## Slide 8: Summary of Model Building Types
Building Type | Description
W1 | Wood, Light Frame
W2 | Wood, Commercial and Industrial
S1 | Steel Moment Frame
S2 | Steel Braced Frame
S4 | Steel Frame w/ Cast-in-Place Concrete Shear Walls
S5 | Steel Frame w/ Unreinforced Masonry Infill Walls
C1 | Reinforced Concrete Moment Resisting Frame
C2 | Concrete Frame with Unreinforced Masonry Infill Walls Low-Rise
C3 | Concrete Frame Buildings w/ Unreinforced Masonry Infill Walls
PC1 | Precast-Concrete Tilt-Up Walls
PC2 | Concrete Shear Walls
RM1 | Reinforced Masonry Bearing Walls w/ Wood or Metal Deck
RM2 | Reinforced Masonry Bearing Walls w/ Precast Concrete Diaphragms
URM | Unreinforced Masonry Bearing Walls
MH | Mobile Home

## Slide 9: W1
Wood, Light Frame
  Usually residential
  Repetitive framing
  Often conventional construction
  Wood, plywood diaphragms
  Plywood, oriented strand board, wood, stucco, plaster, or gypsum board shear walls

## Slide 10: W2
Wood, Commercial and Industrial
  5000 square feet or more
  Few interior walls
  Beams or trusses over columns
  Plywood or wood diaphragms
  Shear walls or diagonal rod bracing

## Slide 11: S1 - L, M, H
Steel Moment Frame
  Frames of steel columns and girders
  All or selected frame bays have moment-resisting column-girder joints
  Non-bearing, non-shear enclosure walls
  Relatively flexible for lateral drift

## Slide 12: C1 - L, M, H
Reinforced Concrete Moment Resisting Frames
  Moment resisting frame of concrete columns and girders
  Older buildings generally have non-ductile frames
  Newer buildings generally have ductile frames
  Non-bearing, non-shear enclosure walls

## Slide 13: PC1
Precast Concrete Tilt-Up Wall
  Wood or metal deck roof diaphragm
  Reinforced concrete wall panels cast on floor slab and tilted up
  Interior columns typically steel posts

## Slide 14: PC2 - L, M, H
Precast Concrete Frames with Concrete Shear Walls
Precast Concrete Frames with Concrete Shear Walls
  Floor and roof diaphragms of precast elements with or without topping concrete
  Precast girders and columns for vertical loads
  Precast or cast-in-place concrete shear walls

## Slide 15: RM1 - L, M
Reinforced Masonry Bearing Walls with Wood or Metal Deck Diaphragms
  Reinforced brick or Concrete Masonry Unit (CMU) shear and bearing exterior walls
  Wood, plywood, steel deck diaphragms with or without concrete fill
  Steel or wood vertical load interior framing

## Slide 16: URM - L, M
Unreinforced Masonry Bearing Walls
  Unreinforced brick or concrete masonry unit shear and bearing exterior walls
  Wood or concrete diaphragms
  Wood, concrete or steel vertical load interior framing

## Slide 17: MH
Mobile Homes
  Lightweight, prefabricated housing units of light metal, wood and plywood
  At site, often placed on jacks or masonry piers

## Slide 18: Required Inventory Information
Occupancy Mapping
  By Building Type
  By Age (Year of Construction)
  By Seismic Design Level (Low, Moderate, High, Pre-Code)
  By Quality (Inferior, Typical, Superior)

## Slide 19: Building Classification Limitations
Assumes Average Characteristics
  Overestimates damage for better buildings and underestimates damage for poorer buildings
Grouped At Centroid of Census Tract
  In large tracts, both soil type and other hazard information changes
  Distance to event source could vary dramatically
Atypical buildings are not explicitly modeled.

## Slide 20: Overcoming Building Classification Limitations
  Add new building types
  Modify properties of a given building
  Model a hybrid building as a group of homogeneous buildings
  Sensitivity analyses
  Ground truthing

## Slide 21: Review
  Why is it important to understand the specific building types within the Earthquake Model?
  How does building design level influence potential earthquake damages?
  What are some of the limitations of building classification, and how can you overcome some of them? Think of a specific example.

## Slide 22: Questions?