## Slide 1: Lesson 4: Building Vulnerability and AEBM

## Slide 2: Goal and Objectives
Goal
  Explore the methodology by which Hazus assesses building vulnerability to earthquakes.
After completing this lesson, you will be able to:
  List the key parameters that affect the damage assessment of buildings in Hazus.

## Slide 3: Earthquake Damage Influences
Generation
  Large earthquakes happen less often than small earthquakes
Attenuation
  Seismic waves decay as they travel
Vulnerability
  Buildings suffer damage based on the intensity of the ground motion and the design of the building

## Slide 4: Earthquake Forces on Buildings
  Earthquakes only shake ground; they do NOT exert forces to buildings.
  Earthquake force is generated when super- and sub-structures fight.
  Substructures comply with shaking; superstructures do not.

## Slide 5: Building Capacity Curve
Building damage is primarily a function of displacement. Capacity curves are described by:
  Design capacity strength of a building
  Yield capacity point where a building experiences damage
  Ultimate capacity point where a building is completely destroyed
Capacity curves plot building displacement versus earthquake force.

## Slide 6: Response Spectrum Method
  Foundation of buildings EXACTLY copy the ground motion vibration.
  Tops of buildings vibrate ONLY at their own designated mode.
  Resonance happens when shaking & building mode match.

## Slide 7: Fragility Curves
Fragility curves are damage functions for earthquakes.
Lognormal distribution of being in or exceeding damage state.
Considers variability of damage state due to:
  Uncertainty of damage state threshold
  Variability in building capacity
  Spatial variability of ground motion

## Slide 8: Activity 4.1
The Instructor will explore:
  Damage function tables
  How to translate into these functions using beta and median values

## Slide 9: Primary Factors Affecting Damage
Building Type
  Structural Type and Height
Design Levels
  Pre-Code, High-Code, Moderate-Code, Low-Code, High-Special, Moderate-Special, Low Special
Seismic Design Level | Superior Seismic Performance Level | Superior Seismic Performance Level | Inferior Seismic Performance Level
High (UBC Zone 4) | Special High-Code Maximum Strength Maximum Ductility | High-Code High Strength High Ductility | Moderate Strength Moderate/Low Ductility
Moderate (UBC Zone 2B) | Special Moderate-Code High/Moderate Strength High Ductility | Moderate-Code Moderate Strength Moderate Ductility | Low Strength Low Ductility
Low (UBC Zone 1) | Special Low-Code Moderate/Low Strength Moderate Ductility | Low-Code Low Strength Low Ductility | Pre-Code Minimal Strength Minimal Ductility

## Slide 10: Nonstructural Damage
Nonstructural contents related to occupancy
  Repair costs
  Content value
Drift Sensitive
  Fragility curves of damage vs. displacement
  Varies by building type and design level
Acceleration Sensitive
  Fragility curves of damage vs. acceleration
  Varies by building type and design level

## Slide 11: Building Damage From Ground Failure
Slight and moderate damage states implicit in ground shaking damage.
No fragility relationship for slight and moderate damage states.
Damage dependant on foundation type.
Relationship for shallow foundation:
  10% extensive/complete for 2 inch settlement.
  50% extensive/complete for 10 inch settlement.

## Slide 12: Building Damage Guidelines
Likely Amount of Damage, Direct Economic Loss, or Building Condition
Damage State | Range of Possible Loss Ratios | Probability of Long-Term Building Closure | Probability of Partial or Full Collapse | Immediate Post-Earthquake Inspection
Slight | 0 - 5% | P = 0 | P = 0 | Green Tag
Moderate | 5 - 25% | P = 0 | P = 0 | Green Tag
Extensive | 25 - 100% | P 0.5 | P 0 | Yellow Tag
Complete | 100% | P 1.0 | P > 0 | Red Tag

## Slide 13: Building Damage States
Damage State | Description
Slight | Small plaster cracks at corners f door and window openings and wall-ceiling intersections; small cracks in masonry chimneys and masonry veneer. Small cracks are to be assumed to be visible with a maximum width of less than 1/8 inch (cracks wider than 1/8 inch are referred to as "large" cracks).
Moderate | Large plaster or gypsum-board cracks at corners of door and window openings; small diagonal cracks across shear wall panels exhibited by small cracks in stucco and gypsum wall panels; large cracks in brick chimneys; toppling of all masonry chimneys.
Extensive | Large diagonal cracks across shear wall panels or large cracks at plywood joints; permanent lateral movement of floors and roof; toppling of most brick chimneys; cracks in foundations; splitting of wood sill plates and/or slippage of structure over foundations.
Complete | Structure may have large permanent lateral displacement, or be in imminent danger of collapse due to cripple wall failure or the failure of the lateral load resisting system; some structures may slip and fall off the foundations; large foundation cracks. Three percent of the total area of buildings with Complete damage is expected to be collapsed, on average.

## Slide 14: Review
  What are the main factors affecting building damage?
  Building damage is primarily a function of what?
  What does the Capacity-Spectrum Method estimate?
  What do fragility curves estimate?

## Slide 15: Questions?