## Slide 1: Lesson 5: Earthquake Hazard Parameters

## Slide 2: Goal and Objectives
Goal
  Provide an overview of hazard parameters within the Earthquake Model and review the various Earthquake Model scenario options.
After completing this lesson, you will be able to:
  Explain the parameters used in characterizing ground motion.
  Describe the different earthquake scenario options and when they should be used.

## Slide 3: Earthquake Background
Hazard quantification is expressed as a function of:
  Size of event
  Location and depth of event
  Soil type
  Liquefaction susceptibility - amount of lateral spreading and settlement
  Water table depth
  Landslide susceptibility - amount of ground failure
  Proximity to fault and fault mechanism
  Regional attenuation characteristics of ground motion

## Slide 4: Hazus Approach
  Evaluates ground motion parameters for damage to structures: At the location for site-specific inventory
  At the centroid of the census tract for aggregate inventory
Ground shaking is characterized in terms of:
  Location-specific shaking
    Spectral response
    Peak ground values
  Regional attenuation functions
  Site-soil effects

## Slide 5: Hazus Approach (cont.)
Ground failure is expressed in terms of amount of ground deformation. The model accounts for the potential for settlement lateral spreading, and landslides.
Liquefaction and lateral spreading occurred along the west side of Sunset Lake trailer park in Tumwater. (Photo courtesy of USGS)

## Slide 6: Earthquake Hazard Parameters
  Attenuation Process
  Soil
    Types
    Classification
    Amplification Factors
  Ground Failure Susceptibility
  Liquefaction Susceptibility
  Landslide Susceptibility
Caution: there are no warnings if soils data are loaded improperly.

## Slide 7: Defining a New Earthquake Scenario
Deterministic
  USGS ShakeMap*
  Historical epicenter event
  Source event
  Arbitrary event
Probabilistic
User-supplied
*Preferred method

## Slide 8: ShakeMap Importing
  ShakeMap is a product of the USGS Earthquake Hazards Program in conjunction with regional seismic networks and additional localized data.
  Provides near-real-time maps and digital data of ground motion and shaking intensity following significant earthquakes.
  Hazus has the capability to dynamically input both scenario and event ShakeMaps.
A ShakeMap is a representation of ground shaking produced by an earthquake.

## Slide 9: ShakeMap Importing (Cont.'d)
  Using ShakeMaps typically produces more credible analysis that can lead to a wider range of purposes for which Hazus is applicable.
  Hazus can download a grid.xml file from the USGS containing the earthquake parameters from the selected ShakeMap.

## Slide 10: ShakeMaps for Hazus
  ShakeMaps for Hazus must include a minimum of 4 files:
    peak ground acceleration (PGA)
    peak ground velocity (PGV)
    spectral acceleration at 1 second (psa10)
    spectral acceleration at .03 seconds (psa03)
  Soil maps should not be used with ShakeMaps

## Slide 11: Where to find ShakeMaps?
  USGS Shakemap website

## Slide 12: Where to find ShakeMaps for California?
California Integrated Seismic Network (CISN)
Sample of ShakeMaps currently available on the CISN website:
Name/Epicenter | Date | Time | Lat | Long | Mag
15.9 km (9.9 mi) E of Oildale, CA | Jun 10, 2019 | 02:41:11 AM UTC | 35.41 | -118.84 | 3.5
12.4 km (7.7 mi) W of San Clemente Is. (SE tip), CA | Jun 6, 2019 | 11:25:36 AM UTC | 32.84 | -118.48 | 3.5
4.4 km (2.7 mi) NNW of Glen Avon, CA | Jun 6, 2019 | 12:20:57 AM UTC | 34.05 | -117.51 | 3.2
14.9 km (9.3 mi) W of San Clemente Is. (SE tip), CA | Jun 5, 2019 | 02:32:09 PM UTC | 32.84 | -118.50 | 4.3
12.9 km (8.0 mi) W of San Clemente Is. (SE tip), CA | Jun 5, 2019 | 10:47:18 AM UTC | 32.82 | -118.48 | 4.3

## Slide 13: Activity 5.1
Student Activity
  Complete a scenario using ShakeMap

## Slide 14: Additional Deterministic Events
Historical epicenter event
  Select the desired event from the Hazus database of 3,500 historical events.
Fault source event
  For the Western U.S., select the desired fault source from the Hazus database of faults.
Arbitrary event
  Defined by the location of its epicenter and by its magnitude.
  Epicenter is defined either by entry of latitude and longitude or graphically or a map.

## Slide 15: Probabilistic Scenarios
Probabilistic
  Specific Return Period
  Annualized Earthquake Loss (AEL)
Probabilistic seismic hazard contour maps developed by the USGS for the National Seismic Hazard Mapping Project

## Slide 16: FEMA P366
  FEMA P366 highlights the impacts of both high hazard and high exposure on losses caused by earthquakes.
  Access the FEMA P366 report here
  The P366 data can be viewed here

## Slide 17: Importing Hazard Maps
  Import user-defined maps to create more detailed analysis.
  Expertly generated ground motion and soils maps can enhance the quality of your results.

## Slide 18: EQ User-Defined Hazard Option

## Slide 19: EQ User-Defined Hazard Option (Cont.'d)

## Slide 20: Scenario Applications
  Historical and ShakeMap - useful for validation, calibration, benchmarking, analysis of repeat earthquake events, and mitigation analysis.
  Arbitrary - useful for areas with very limited seismic activity, events defined by geologists or other experts, mitigation analysis, and response and recovery in the absence of user- defined maps.
  User-defined - most useful when ground motion maps are available (e.g., post-disaster event or level 3 studies).

## Slide 21: Scenario Applications
  Probabilistic - useful for prioritization of seismic reduction measures and for simulating mitigation strategies.
  Annualized useful for comparisons of risk for large regions, states and the nation.

## Slide 22: Prioritizing EQ Hazard Data
Soil is most important:
  Affects shaking intensity
Liquefaction is important mostly for roads, tracks, tunnels, runways, bridges, and pipelines:
  Effect on buildings is very localized
  Water table depth affects the liquefaction potential
Landslide effects are localized and important mostly for roads, tracks, tunnels, bridges, and pipelines.

## Slide 23: Model Sensitivity
Hazus results are most sensitive to ground motion.
If no data is available for soil or liquefaction, you should run sensitivity tests. Examples:
  See how losses change if soil type was B (compared to the default class of D). This will provide a lower-bound loss.
  See what effects liquefaction has on results by changing the default assumption from "no potential" to "very high" by selecting the soil type as "E." This will provide an upper bound loss.

## Slide 24: Review
  What are the five main EQ model scenario options?
  What is a ShakeMap?
  What is the most important hazard parameter to include and why?

## Slide 25: Questions?