## Slide 1: Lesson 7: Bridge and Pipeline Loss Models

## Slide 2: Goal and Objectives
Goal
This lesson will discuss the components that operate the bridge and pipeline loss models and how to alter the various components.
After this lesson you will be able to:
  Explore the bridge classification system.
  Explore the bridge loss estimation methodology.
  Understand the pipeline model and key parameters.
  Explore options for customizing damage models for pipelines.

## Slide 3: Key Components
Inventory
  Location information obtained from the National Bridge Inventory (NBI)
Classification/Damage Functions
  Some attributes based on characteristics per NBI data
  Other attributes developed based on historical seismic performance of bridges
Valuation (cost of repair & replacement)
Restoration functions
Economic loss of functions

## Slide 4: Bridge Classification
National Bridge Inventory (NBI) data provides a variety of information.
  # Spans
  Structural Type
  Pier Type
  Abutment Type & Bearing Type
  Span Continuity

## Slide 5: Bridge Classification (cont.)
Material and/or Construction
  Concrete, Steel, Masonry, etc...
  10 classes
Bridge Type
  Slab, Tee Beam, Suspension, etc...
  23 classes
*For further detail refer to the Earthquake Technical Guidance.

## Slide 6: Bridge Classification (cont.)
Conventional Bridges
  Codes based on material and type
  Unique options for California
  Damage State Thresholds - Slight, Moderate, Extensive, Complete
Description | Codes | Non-California | California
Multi-column Bents, Simply Supported | 101-106 301-306 501-506 | 0.26, 0.35, 0.44, 0.65 | 0.33, 0.46, 0.56, 0.83
Single-column Bents, Box Girders | 205-206 605-606 | Not Applicable | 0.35, 0.42, 0.50, 0.74

## Slide 7: Bridge Classification (cont.)
Seismically Designed Bridges
  Codes based on material and type
  Unique options for California due to earthquake susceptibility
  Damage State Thresholds - Slight, Moderate, Extensive, Complete
Description | Codes | Non-California | California
Multi-column Bents, Simply Supported | 101-106 301-306 501-506 | 0.45, 0.76, 1.05, 1.53 | 
Single-column Bents, Box Girders | 205-206 605-606 | Not Applicable | 0.54, 0.88, 1.22, 1.45

## Slide 8: Bridge Classification (cont.)
3-D Effects on Bridges
  The 3-D effects refer to the "out-of-plane" motion that the bridge may feel during an earthquake that tends to cause more damage.
Description | Codes | Conventional | Seismic
Concrete | 101-106 | 1 + 0.25 / np | 1 + 0.25 / np
Continuous Concrete | 201-206 | 1 + 0.33 / n | 1 + 0.33 / np
Steel | 301-310 | 1 + 0.25 / np; L > 20m 1 + 0.25 / np; L < 20m | 1 + 0.25 / np

## Slide 9: Hazus Simplified Classification
Excerpt from Hazus Earthquake Technical Manual

## Slide 10: Hazus Damage Methodology
  Know the location (lat & long)
  Know the soil, liquefaction and landslide potential at that site.
  Categorize the vulnerability by choosing the appropriate class.
  Estimate the replacement cost of the bridge.
  Compute the ground shaking and amount of ground failure expected at the site.
  Assess the damage due to ground shaking and ground failure.
  Translate the damage to loss of function and cost of repair.

## Slide 11: Economic Loss Evaluation

## Slide 12: Restoration Function for Bridges

## Slide 13: Activity 7.1
Student Activity
  Explore the effects of Different Parameters on Bridge Damage

## Slide 14: Summary
  Background information presented on how the bridge model functions
  Key step is in assigning the right classification, which is based on attributes specific to a given bridge
  Default replacement values are editable and can be replaced
  Likewise, all other parameters (damage, loss of function and economic parameters) could be edited. This would be an advanced type of analysis.

## Slide 15: About the Pipeline Model
Same methodology used in Hazus for:
  Potable water pipelines
  Storm water pipelines
  Sewers
  Crude oil pipelines
  Refined oil pipelines
  Natural gas pipelines
Understanding the architectural design of the model in the Hazus software will help you figure out how to refine the model when needed.

## Slide 16: Key Components
Inventory
  No baseline site-specific data, only placeholders
  Users can add pipeline data if available locally
  Hazus will model damage if inventory is provided
  Aggregate data at 2010 census tract level is provided for water, sewer, & gas distribution pipelines (based on street proxy)
Classification / Damage Functions
  Over-simplified classification into brittle or ductile pipes
  Damage is expressed in terms of leaks and breaks

## Slide 17: Key Components
Economic loss
  Cost of repair is a function of whether the pipe has suffered a leak or a break.
Functionality
  Restoration depends on the number of repair crews available.

## Slide 18: Key Pipeline Attributes
  Diameter (required)
  Elevation
  Pressure
  Flow
  Class (required)
    Material (Type, Roughness, etc...)
    Joint type
  Replacement value (required)
  Linkage to facilities

## Slide 19: Damage Model
Damage model has two components
  Ground shaking
    PGV
  Ground failure
    Lateral spreading
    Settlement
    Landslide
Damage = # Leaks + # Breaks

## Slide 20: Functionality Model
Based on # of crews available

## Slide 21: Economic Loss Model
Function of # leaks and # breaks

## Slide 22: System Performance
Potable water only
# Households without water

## Slide 23: Pipeline Loss Model Summary
  Background information presented on how the Pipeline Model works
  Key component of the critical utility infrastructure
  Challenging issues :
    Obtaining actual data for pipelines
    Expanding classes if needed
    Defining the number of qualified crews available to do repair

## Slide 24: Activity 7.2
Student Activity:
  Explore the effects of Pipeline Parameters on Damage

## Slide 25: Review
  What are some of the data types that the NBI provides?
  Why are there unique codes for California compared to the rest of the United States for bridge classification?
  How are the repair costs calculated for bridges?
  How is damage expressed within the Pipeline Loss Model?
  What are the two components that contribute to the damage model for pipelines?

## Slide 26: Questions?