## Slide 1: Lesson 8: AEBM and Site Specific Inventory

## Slide 2: Goal and Objectives
Goal
Explore the methodology used in the Advanced Engineering Building Model (AEBM).
After completing this lesson you will be able to:
  Describe the usefulness of the AEBM functionality in Hazus to do portfolio analyses to buildings.
  See how to create AEBM profiles and a portfolio of buildings.

## Slide 3: Introduction to AEBM Capabilities
Advanced Engineering Building Module (AEBM) allows site-specific analyses for a portfolio of buildings:
  Ground shaking and ground failure quantification
  Damage state probabilities assessment
  Economic loss computations
  Casualties estimates
Inventory items can be entered individually or imported through CDMS into State or Study Region databases.

## Slide 4: AEBM: Choose or Define a Profile
Choose from over 16,000 unique building characteristics profiles.
Based upon:
  Occupancy
  Building type
  Design level
Linked to:
  Capacity curves
  Fragility curves

## Slide 5: AEBM: Creating a Portfolio
  Location-specific
  Must be linked to a previously created profile
  Input for square footage, number of occupants, and economic values (replacement value, content value, and business income)

## Slide 6: AEBM: Betas - Shakemap vs. Any Other Scenario
  Hazus building fragility functions employ lognormal standard deviation parameters, or betas
  Betas describe the total uncertainty of the fragility-curve damage states
  When populating ProfileName field in your AEBM database:
    if using a Shakemap to analyze your AEBM inventory, you must use "-1" (ex. RES1W1MC-1)
    if using any other Scenario to analyze your AEBM inventory, you must use "0" (ex. RES1W1MC0)

## Slide 7: Merits of AEBM
  It can model any desired type or use of a building
  Total flexibility on defining the properties of buildings
  Fastest and most comprehensive way to analyze a portfolio of buildings with different characteristics
  Very powerful to use to estimate the benefits of a given mitigation strategy (eg., benefits of retrofitting a URM building, etc.)

## Slide 8: Import AEBM with CDMS
  Use CDMS to import an AEBM inventory
  Update the State Data folder using CDMS with the imported AEBM inventory
  Create a Study Region with the updated State Data with AEBM
  The new Study Region will now contain an AEBM inventory

## Slide 9: Activity 8.1
Student Activity:
  Building Type and Vulnerability Effects on Results

## Slide 10: Review
  How does an AEBM analysis differ from an aggregate earthquake analysis in Hazus, and for what types of investigations would the AEBM model be best suited?
  What are building characteristic profiles based upon?
  What are the two types of impact assessment that AEBM provides?

## Slide 11: Questions?