## Slide 1: Lesson 9: Tsunami Background and Analysis

## Slide 2: Goal and Objectives
Goal
This lesson will review the tsunami hazard, inventory, and analysis options in Hazus.
After completing this lesson you will be able to:
  Describe near and distance source tsunamis
  Understand tsunami-specific inventory
  Review tsunami analysis options

## Slide 3: Background
  The Hazus Tsunami Model represents the first new disaster module for the Hazus software in almost 15 years.
  It is the culmination of work completed on the Hazus Tsunami Methodology Development (FEMA, 2013).
  The team consisted of tsunami experts, engineers, modelers, emergency planners, economists, social scientists, geographic information system (GIS) analysts, and software developers.

## Slide 4: New Features
New features within the model include:
  Territory Analysis: This release represents the first time that analysis will be available for U.S. territories (Puerto Rico, Guam, American Samoa, Commonwealth of Northern Mariana Islands, and U.S. Virgin Islands).
  New Point Format: The Hazus General Building Stock (GBS) for the Tsunami release will use a new National Structure Inventory (NSI) point format (details in User Release Notes available with download).
  Case Studies: The Tsunami Module will require user-provided data, so the Hazus Team has provided five case study datasets for users, which will be available on the Map Service Center (MSC) download site.
  Two Types of Damage Analysis: Users will be able to run both near-source (Earthquake + Tsunami) and distant-source (Tsunami only) damage analysis.

## Slide 5: Hazus Tsunami Model
  Loss estimation model that provides state-of-the-art decision support software for estimating potential losses from tsunamis
  Available for five Very High-risk states (AK, WA, OR, CA, HI) and the five High-risk U.S. territories
  Combined Earthquake/Tsunami analysis functionality available for the five states and Puerto Rico

## Slide 6: Tsunami Near vs Distant Source
Near Source (local source)
  Those generated within 100 km of a locality of interest
  Earthquake ground shaking precedes the tsunami
  Earthquake damage possible
  Subsidence (lowering) of coastal area possible
  Lead time - a few minutes to an hour
Credit: USGS

## Slide 7: Tsunami Near vs Distant Source (cont.)
Distant Source
  Those generated more than 1,000 km from a locality
  No ground shaking precedes the tsunami
  Lead time - few to several hours
Credit: USGS (Image: https://teara.govt.nz/en)

## Slide 8: National Structure Inventory
  U.S. Army Corp of Engineers' National Structural Inventory point data. Developed with FEMA.
  Creates notional structures, or 'points,' in the developed portion of each census block to represent the numbers and types of buildings that occur based on size, occupancy type, construction materials, etc.

## Slide 9: National Structure Inventory (cont’d)
  Tsunami model General Building Stock (GBS) does not directly use the aggregated Census Tract or Block data.
  The tsunami loss model capability is not currently available for Essential Facilities.
  Users can evaluate Essential Facilities by incorporating them as User-Defined Facilities.

## Slide 10: User Defined Facilities
  Enables user specific datasets to be analyzed through the Hazus methodologies providing more accurate results
  Use CDMS to assist in creation of your UDF database
  Attributes include:
    Occupancy type
    Earthquake building type
    Design level
    First floor height
    Building replacement cost
    Content replacement cost
    Location of structure

## Slide 11: Tsunami Runup Height R
  The height at the maximum tsunami penetration
  Inundation/evacuation map boundaries
  For determining content and nonstructural losses - based on depth only

## Slide 12: Momentum Flux (ft3s2)
  Rate of transfer of momentum across a unit area
  Used to determine structural damage to buildings
  Calculated by Hazus (Basic Analysis) using the maximum runup height and topography (DEM)
  Provided by user for Advanced Analysis - Level 2 and 3
  SIFT (Short-term Inundation Forecasting for Tsunamis) system is the numerical estimate of amplitude, travel time, and additional tsunami properties using an inundation model constrained by real-time tsunami observations.

## Slide 13: Digital Elevation Model (DEM)
Determine Required DEM extent:
  Merge the DEMs if there is more than one for the area of interest.
  Mask the DEM to the study region, which is a time saving technique especially useful for island regions.

## Slide 14: Near Source Deformed DEM
  Post-earthquake event deformed topography should be used in the case of a near source scenario.
  Earthquake could result in several meters of ground deformation, which may substantially change the inundation area and affect potential losses resulting from a tsunami.

## Slide 15: Masking DEM
ESRI ArcMap Extract by Mask tool:
  Clips the DEM to the Study Region Boundary
  Removes all of shore sections
  Reduces processing time

## Slide 16: Levels of Tsunami Analysis
Basic (Level 1)
  Out-of-the-box default infrastructure
  Basic user input
Advanced (Level 2/3)
  User-provided data - more accurate to the region
  Data provided by third-party studies/hazard models

## Slide 17: Hazus Analysis Components

## Slide 18: Hazus Analysis Components (Cont.'d)
Hazard Input
  Tsunami inundation depth
  Velocity or momentum flux
  Topography
Infrastructure
  NSI data (point location aggregated)
  User defined structures
Damage and Losses
  Direct damage to structures, contents and nonstructural elements
  Direct economic losses
Casualties
  Evacuation times
  Injury/Fatality estimates
    Age, time of day, community preparedness

## Slide 19: Analysis Options - Tsunami
Options:
  General Building Stock
    Direct Damages
    Direct Economic Loss
  User Defined Facilities
    Direct Damages
    Functionality and Economic Loss

## Slide 20: Results
Tsunami Inundation layers
  Inundation/Hazard Boundary polygon (depth>0)
  Fatality Boundary (depth >= 2m)
General Building Stock
  Direct Damages
  Direct and Indirect Economic Losses
User Defined Facilities
  Infrastructure damage probabilities
  Direct and Indirect Economic Losses

## Slide 21: Casualty Scenario
Level 1 - Input:
  Fatality Boundary (depth > 2m)
  Hazard Boundary (Depth > 0)
  Road Network Data
  Topography (DEM)
  Estimated time of tsunami arrival and maximum runup
Level 2 - Input:
  Output travel time results provided by the USGS Pedestrian Evacuation Analyst Tool

## Slide 22: Hazard/Fatality Boundary Layers
Hazard Boundary
  Entire Inundation area
  Where depth > 0
  Zone with 50% fatality and 50% injury
Fatality Boundary
  Where depth >= 2m
  Zone with 99% fatality and 1% injury

## Slide 23: Available Case Studies
NOAA PMEL Sample Data
Available for download here: http://tools.hazards.fema.gov/hazus/maps/data/HazardSampleData.zip
Community | County | Scenario | Level 1 | Level 2 | Level 3
Homer, AK | Kenai | M 9.2 1964 Alaska | hom_dem_ft hom_maxR_ft | hom_maxdg_ft hom_maxv_ftsec | hom_dg_ft_median hom_flux_ft3sec2_median
Crescent City, CA | Del Norte | M 9.0 Cascadia | crc_dem_ft crc_maxR_ft | crc_maxdg_ft crc_maxv_ftsec | crc_dg_ft_median crc_flux_ft3sec2_median
Kahului, HI | Maui | M 9.0 Cascadia | kah_dem_ft kah_maxR_ft | kah_maxdg_ft kah_maxv_ftsec | kah_dg_ft_median kah_flux_ft3sec2_median
Garibaldi, OR | Tillamook | M 9.0 Cascadia | gar_dem_ft gar_maxR_ft | gar_maxdg_ft gar_maxv_ftsec | gar_dg_ft_median gar_flux_ft3sec2_median
Westport, WA | Grays Harbor | M 9.0 Cascadia | wes_dem_ft wes_maxR_ft | wes_maxdg_ft wes_maxv_ftsec | wes_dg_ft_median wes_flux_ft3sec2_median

## Slide 24: Where To Find Level 1 & 2 Data
  A sample of level 2 data are available here: https://tools.hazards.fema.gov/hazus/maps/data/HazardSampleData.zip
  Other data sources, FEMA, NOAA PMEL, Tsunami Warning Center, and State and Local Evacuation Plans

## Slide 25: Additional Resources
  https://www.fema.gov/hazus
  Hazus Tsunami Manuals
    Hazus Tsunami Model User Guidance
    Hazus Tsunami Technical Guidance
  Hazus Support (hazus-support@riskmapcds.com)
    FAQs
    Help Desk

## Slide 26: Review
  How might a tsunami be triggered?
  What is the difference between a near and distant source tsunami?
  Which type of tsunami offers the most warning time?
  Describe the tsunami-specific inventory in Hazus.
  What states/territories are included in the Hazus tsunami model?
  Name the two analysis options of the tsunami hazard model.

## Slide 27: Questions?