## Slide 1: Lesson 10: Hazus Flood for Recovery

## Slide 2: Lesson 10: Goal and Objectives
Goal: To review the applications of Hazus for flood recovery.
After completing this lesson you will be able to:
  Explain the ways that FEMA provides help according to the Individual Assistance Program.
  List the components of site-specific flood inventory.
  Determine the minimal construction design characteristics required by Hazus.

## Slide 3: Flood Results: Results (1 of 4)
500 Year Flood Map Explained:
  Dark border lines (here in orange) designates the flood boundaries.
  The shaded areas adjacent to the flood boundary line, which tends to be packed closer together in terms of their hidden contour lines, are unflooded areas at a higher elevation such as slopes, hills, mountains, and ideal population settlements.
  For example, the northern and central areas of the map and the southeast area of the map.
  The shaded areas (here in light to dark blue), which tends to be spread out or flatter in terms of their hidden contour lines, are flooded areas of the map.
  For example, the southern and central areas of the map.
  The lighter blue (shaded) areas that are closer to the flood boundary and higher ground depicts less than 1 foot of flooding. In contrast are the darker blue (shaded) areas further away from the flood boundary representing a decreasing slope in elevation resulting in a high of 32.776 feet of flooding above the ground elevation.

## Slide 4: Flood Results
  GBS: by amount of damage and by dollar losses
  Essential facilities: building and content losses, functionality assessment, and restoration time
  Lifeline losses: losses to structures, functionality assessment
  Vehicle losses: day and night, by car or truck
  Agriculture losses (Not reimbursed under FEMA PA)
  Shelter requirements: displaced households and short-term needs

## Slide 5: Individual Assistance Program
Provides:
  Immediate Assistance (partners with other organizations)
  FEMA help
    Home/Primary Residence
    Business/Secondary Home
    Other (medical, dental, child care, storage, etc.)
  Additional Assistance
    Small Business Administration Application
    Home Inspection
    After the Inspection

## Slide 6: Final High Water Marks (HWM)
  A measure of the event water surface elevation
  Collected by either USGS or local governments
  During periods of flooding, HWM elevations may be collected at the peak elevation using high-resolution GPS systems.
  Values represent the most accurate depiction of the flood event.
  Represent the highest extent of riverine flood or coastal storm surge inundation.
  Represents the elevation of the water during the flood event and fills in the gaps where water marks are not present
  HWMs can be interpolated into depth grids for loss estimation

## Slide 7: Exercise 10.1: HWM Depth Grid
Goal: Create a high water mark depth grid.
Time: 30 minutes

## Slide 8: Exercise 10.1: Tasks
Task 1: Insert Interpolation of the Water Surface; Create Depth Grid.
Task 2: Subtract Water Surface Grid from the DEM.
Task 3: Remove Negative Values.
Task 4: Create the Flood Boundary.

## Slide 9: Site-Specific Flood Inventory
  Essential Facilities
  Transportation Infrastructure: All inventory can be entered, but only bridges are analyzed
  Utilities: Additional classifications include control vaults and control stations
  User-Defined Facilities: Used to perform a more refined site-specific analysis of inventory found in the GBS

## Slide 10: User-Defined Facilities
Hazus requires minimal construction design characteristics to select the correct damage curve for damage and loss analysis for each facility:
  Foundation type
  Number of stories
  First floor elevation
  Specific occupancy
  Building and contents valuations
Applications: Explore
  Explore Impact of fewer homes in floodplain
  Outcome of elevating at-risk homes

## Slide 11: Lesson 10: Review
  What are some of the ways that FEMA provides help according to the Individual Assistance Program?
  What components are used for a site-specific flood inventory?
  What are the minimal construction design characteristics required by Hazus?

## Slide 12
Questions