## Slide 1: Lesson 11: Basic Earthquake

## Slide 2: Lesson 11: Goal and Objectives
Goal: To provide a review of the earthquake model within Hazus.
After completing this lesson you will be able to:
  Explain earthquake basics and inventory parameters.
  Describe the function and necessities of ShakeMap.
  Differentiate between Fragility and Capacity Curves.

## Slide 3: Where Do Earthquakes Happen?
Most of world's active faults are located along or near boundaries between shifting plates
  Plate Boundary earthquakes
Other active faults are not associated with plate boundaries and are inside plates
  Intra-plate earthquakes

## Slide 4: GBS for Earthquakes
  In addition to standard inventory, the GBS has attributes particular to the earthquake hazard
  37 unique building types based on frame and height
    Steel, concrete, masonry, wood, mobile homes
    Low-rise, mid-rise, high-rise
  Seven different design levels
Notes: GBS for Earthquakes
In addition to standard inventory, the GBS has attributes particular to the earthquake hazard
37 unique building types based on frame and height
  Steel, concrete, masonry, wood, mobile homes
  Low-rise, mid-rise, high-rise
Seven different design levels

## Slide 5: Earthquake Data Sources
  National Earthquake Information Center (NEIC)
  USCG: ShakeMaps for actual and scenario events
  Regional earthquake consortia
    CUSEC: soils and liquefaction susceptibility maps
  State geologists
  Local universities

## Slide 6: Hazus Earthquake Basics
  Catastrophic Response Planning
  Annualized Earthquake Loss Study (FEMA P.-366)
  Earthquake results are sensitive to categories of inventory parameters
    Location
    Classification to earthquake vulnerability
    Valuation
    Societal

## Slide 7: Hazus Approach
Evaluates ground motion parameters
  At the location for site-specific inventory
  At the centroid of the census tract for aggregate inventory
Ground shaking characterized in terms of
  Location-specific shaking
  Spectral response
  Peak ground values
  Regional attenuation functions
  Site-soil effects

## Slide 8: Hazus Approach (Cont'd.)
Ground Failure shaking is characterized in terms of amount of ground failure due to liquefaction and landslide.

## Slide 9: USGS PAGER
  Prompt Assessment of Global Earthquakes for Response
  Provides fatality and economic loss impact estimates following significant earthquakes worldwide.
  onePAGER: concise, printable version of the rapid assessment of estimated fatalities and economic losses delivered online and via email
  NOTE: There is currently a joint USGS-FEMA effort underway to develop a PAGER 2nd page, providing Hazus results for significant US earthquakes.

## Slide 13: PAGER vs. Hazus
PAGER: Exposure Model
  Shaking intensity, population exposure, and loss estimates
  Ground shaking impacts
  Fatality and economic loss estimates given the exposure
  Estimated results only
Hazus: Loss Estimation Model
  Ground shaking, fault rupture, liquefaction, land sliding, and tsunami impacts
  Considers building density and composition
  Site-specific and user-defined capabilities
  Results options:
    Quantitative estimates of direct and indirect losses
    Functionality losses
    Extent of induced hazards

## Slide 14: Defining a New Earthquake Scenario
Deterministic
  USGS ShakeMap*
  Historical epicenter event
  Source event
  Arbitrary event
Probabilistic
User-Supplied
*Preferred method

## Slide 15: ShakeMap
ShakeMap is a product of the USGS Earthquake Hazards Program
  Provide near-real-time maps of ground motion and shaking intensity following earthquakes
  Used by federal, state, and local organizations (private and public) for:
    Post-earthquake response and recover
    Public and scientific information
    Preparedness exercises
    Disaster planning
  Provides maps on intensity, acceleration, velocity, and uncertainty of earthquakes
  ShakeMap data download options include: XML grids, rock grid, uncertainty grid, text ASCII grids, KML, KMZ, Shapefiles, general-purpose GIS files, ESRI raster files, text metadata, and other supplementary maps and images

## Slide 16: ShakeMap
ShakeMaps for Hazus must include a file with the following parameters:
  Peak Ground Acceleration (PGA)
  Peak Ground Velocity (PGV)
  Spectral Acceleration at 1 second (psa10)
  Spectral Acceleration at 0.3 seconds (psa03)

## Slide 17: Demonstration 11.1: ShakeMap
Goal: Use the Hazus interface to find a ShakeMap.
Time: 25 minutes

## Slide 18: Demonstration 11.1: Tasks
Task 1: Create a New Salt Lake City Study Region.
Task 2: Open Salt Lake City Study Region.
Task 3: Use Hazus Interface to Define USGS ShakeMap.
Task 4: View Direct Economic Loss.

## Slide 19: Using Hazard Maps
Simplified hazard maps are automatically generated during the creation of the study region. These approximate hazard maps are based on default soil maps and the census tract boundaries.
Users can modify and enhance soils, liquefaction, landslide and water depth if spatial data is available from experts or other agencies.
If available, these expert-generated maps should be used to replace the simplified maps.
Hazard maps should be used when default data may not represent actual conditions or to model historical scenarios. If improved hazard maps are not available, the site class of each hazard for the study region can be changed.
Note: Soil hazard maps should not be used with ShakeMaps.

## Slide 20: Importing Hazard Maps
  Import user-defined maps to create more detailed analysis
  Expertly generated ground motion and soils maps can enhance the quality of your results.

## Slide 21: Define Hazard Maps Option
Hazard map options:
  Apply same value to the entire region
  Import hazard maps so that Hazus can generate more accurate ground motion data

## Slide 22: User-Defined Hazard Option

## Slide 23: Exercise 11.2: Source Event
Goals:
  Create a Source Event Scenario.
  Create a map of economic loss.
Time: 25 minutes

## Slide 24: Exercise 11.2: Tasks
Task 1: Open Study Region Salt_Lake_City_EQ.
Task 2: Define the Scenario.
Task 3: Add a Soil Map and Define the Data.
Task 4: Run Analysis.
Task 5: View Direct Economic Loss Results.

## Slide 25: Capacity Curves
  Characterize building response (e.g. displacement) resulting from input ground motion
  Lognormal distribution of being in or exceeding damage state
  Estimated displacement is used with the Fragility Curve to determine damage state probabilities
  Capacity curves are described by:
    Design capacity strength of a building
    Yield capacity point where a building experiences damage
    Ultimate capacity point where a building is completely destroyed

## Slide 26: Fragility Curves
  Damage functions for earthquakes
  Lognormal distribution of being in or exceeding damage state
  Considers variability of damage state due to:
    Uncertainty of damage state threshold
    Variability in building capacity
    Spatial variability of ground motion
  Depending on the level of earthquake forces, damage to building can range from no damage to complete damage
    Uncertainty

## Slide 27: Lesson 11: Review
  List four categories of inventory parameters that earthquake results are sensitive to.
  What is a ShakeMap and what types of data does it use?
  What parameters must be included in ShakeMap for Hazus?
  What is the difference between a Fragility Curve and a Capacity Curve?

## Slide 28
Questions