## Slide 1: Lesson 12: Hazus Earthquake for Response

## Slide 2: Lesson 12: Goal and Objectives
Goal: To understand basics of modeling earthquakes for response in Hazus.
After completing this lesson you will be able to:
  Describe the earthquake response timeline.
  Summarize the quantification of the hazards for an earthquake.
  Explain the characteristics of ground shaking.
  List the data sources used for Hazus for Earthquakes.

## Slide 3: Federal Response
  USGS Earthquake Notification Service (ENS)
    Free email notification service
    Default magnitude of 6.0 in U.S. (can be user modified)
  PAGER Yellow Alert: regional impact and response
  PAGER Orange Alert: national-scale impact and response
    Support efforts of state and local governments
  FEMAs Natural Hazards Risk Assessment program will contain loss data scenarios beginning 2019
    Based on ShakeMaps, Hazus Loss results, PAGER (page 1) and PAGER (page 2)
  Earthquake Notification Service: earthquake.usgs.gov/ens/userhome_map

## Slide 4: USGS ShakeMap
  ShakeMaps provide near-real-time maps of ground motion and shaking intensity following significant earthquakes
  ShakeMaps also contain archives of previous earthquakes
  Will show earthquakes in the last 90 days by default - to add historic or scenario events, make selection and expand search parameters.

## Slide 5: Direct Physical Damage
Hazus assesses the maximum displacement that a building will undergo and the damages that would result
Damages vary according to
  Uncertainty of damage state threshold
  Variations in building capacity
  Geographic variations of ground motion
Analyzes both structural and non-structural elements

## Slide 6: Direct Physical Damage
  Essential Facilities
    Fire Stations, Police Stations, Hospitals and Clinics, Schools, Emergency Operations Centers
What can Hazus provide the community/State decision-makers?
  Parameters
    Facility Damage
    Restoration Time
    Based on ground shaking and ground failure
Why is this data critical for emergency planning?

## Slide 7: Direct Physical Damage
Transportation:
  Highway, Railway, Light Rail, Bus, Port, Ferry, Airport
Parameters
  Facility Damage
  Time to Restore Facility
  Economic Loss Estimations
When and in what form should this be provided to leadership?

## Slide 8: Direct Physical Damage
Utilities:
  Potable Water, Waste Water, Oil Systems, Natural Gas, Electric Power and Communication
Parameters
  Facility Damage
  Time to Restore Facility
  Economic Loss Estimations
Following an earthquake, how can Hazus facilitate recovery operations? Broken utilities, Watsonville Area, Loma Prieta, 1989 (USGS)

## Slide 9: Social Losses - Casualties
Calculates multiple levels of casualties based on severity and time of day
Parameters
  Damage to various Building Types
  Bridge Damage Contribution
  Time Dependent
Spence and So. 2009. Estimating Shaking-Induced Casualties and Building Damage for Global Earthquake Events"

## Slide 10: Social Losses - Shelter
Calculates need for public shelters
Parameters
  Age
  Ethnicity
  Income
  Home Ownership
  Damage states of different types of buildings
What information and recommendations can Hazus provide leadership?
Red Cross shelter; Minot, ND; June 24, 2011

## Slide 11: Debris
Parameters
  Weight of structural and nonstructural model building types
  Probabilities of damage states for structural and nonstructural elements by census tract
Why is this information critical for recovery operations?
Damage in the Old Town historical district, City of Salinas, Loma Prieta, 1989 (USGS).

## Slide 12: Direct Economic Loss
Parameters
  Annual Gross Sales
  Restoration Time
  Income and Wage Losses

## Slide 13: Running the Analysis
User picks modules they wish to run
Modules can be re-run as needed
Only select the analysis you need (speeds up processing time)

## Slide 14: Exercise 12.1: ShakeMap
Goals:
  Import a ShakeMap.
  Create a map of economic loss.
Time: 25 minutes

## Slide 15: Exercise 12.1: Tasks
Task 1: Open study region Salt_Lake_City_EQ.
Task 2: Define the Scenario.
Task 3: Run Analysis.
Task 4: View Direct Economic Loss Results.

## Slide 16: Lesson 12: Review
  How is the hazard of an earthquake quantified?
  How is ground shaking characterized?
  What are the data sources used for Hazus for Earthquake

## Slide 17
Questions