## Slide 1: Lesson 14: Basic Tsunami

## Slide 2: Lesson 14: Goal and Objectives
Goal: To provide a review of the tsunami model within Hazus
After completing this lesson you will be able to:
  Define tsunami.
  Differentiate between near and distant source tsunamis.
  Understand tsunami-specific inventory.

## Slide 3: Tsunami Overview
A series of long-period waves that are usually generated by an impulsive disturbance that displaces massive amounts of water
  Travels at speeds of > 450 mph across the ocean, slowing as it approaches shallower water
  A series of waves with minutes to hours between the first wave may not be the largest
  Encompass the entire water column in open ocean, with an average surface height of 0.5 m

## Slide 4: Tsunami Overview
Tsunamis can be triggered by
  earthquakes
  volcanic activity
  submarine landslides
  onshore landslides in which large volumes of debris fall into the water
All of these triggers can occur in the United States
Most of the tsunamis (88%) in the Global Historical Tsunami Database were generated by earthquakes or landslides caused by earthquakes

## Slide 5: Hazus Tsunami Model
  Loss estimation model that provides state-of-the-art decision support software for estimating potential losses from tsunamis.
  Available for 5 Very High-risk states (AK, WA, OR, CA, HI) and the 5 High Risk U.S. territories
  Combined Earthquake/Tsunami analysis functionality available for the 5 states and PR

## Slide 6: Tsunami - Near vs Distant Source
Near Source (local source)
  Those generated within 100 km of a locality of interest
  Earthquake ground shaking precedes the tsunami
  Earthquake damage possible
  Subsidence (lowering) of coastal area possible
  Lead time a few minutes to an hourCredit: USGS

## Slide 7: Tsunami - Near vs Distant Source
Distant Source
  Those generated far away (>1,000 km from a locality)
  No ground shaking precedes the tsunami
  Lead time few to several hours

## Slide 8: Available Data
  Census Bureau: road networks
  NOAA
    National Center for Environmental Information: tsunami events, runups, deposits
    Bathymetry, seismic activity, real-time data
  State governments
    Hawaii: tsunami zones, evacuation zones, wave heights, parcels, terrestrial
  US Tsunami Warning System

## Slide 9: National Structure Inventory (NSI)
  U.S. Army Corp of Engineers National Structural Inventory point data. Developed with FEMA.
  Creates notional structures, or points, in the developed portion of each census block to represent the numbers and types of buildings that occur based on size, occupancy type, construction materials, etc.

## Slide 10: User Defined Facilities
  Enables user specific datasets to be analyzed through the Hazus methodologies providing more accurate results
  User populated table using Hazus CDMS
  Attributes include:
    Occupancy type
    Earthquake building type
    Design level
    First floor height
    Building replacement cost
    Content replacement cost
    Location of structure

## Slide 11: Exercise 14.1: Tsunami Study Region
Goal: Build a tsunami study region.
Time: 15 minutes

## Slide 12: Exercise 14.1: Tasks
Task 1: Build a Tsunami Study Region.
Task 2: Open the Region and Input Tsunami User Data.

## Slide 13: Lesson 14: Review
  What are the characteristics of a tsunami?
  List the incidents that can trigger a tsunami.
  What is the differences between a tsunami approaching the coast and tsunamis occurring near the coast?
  How does the National Structure Inventory work with Hazus?

## Slide 14
Questions