## Slide 1: Lesson 15: Hazus Tsunami for Response and Recovery

## Slide 2: Lesson 15: Goal and Objectives
Goal: To describe the levels of analysis and applications for estimating losses and casualties.
After completing this lesson you will be able to:
  List the steps for estimating tsunami losses.
  Describe the steps for estimating tsunami casualties.

## Slide 3: Levels of Tsunami Analysis
Basic (Level 1)
  Out-of-the-box default infrastructure
  Basic user input
Advanced (Level 2/3)
  User-provided data - more accurate to the region
  Data provided by third-party studies/hazard models

## Slide 4: Hazus Analysis Components
Hazard Input
  Tsunami inundation depth
  Velocity or momentum flux
  Topography
  Run-up Height
Infrastructure
  NSI data (point location aggregated)
  User defined structures

## Slide 5: Hazus Analysis Components
Damage and Losses
  Direct damage to structures, contents and nonstructural elements
  Direct economic losses
Casualties
  Evacuation times
  Injury/Fatality estimates
    Age, time of day, community preparedness

## Slide 6: Hazard Analysis - User Input

## Slide 7: Level 1 Analysis
  Requires user input data
  Level 1 outputs are the inputs needed for levels 2 and 3 analysis
  Runup Only-Mean Sea Level (MSL) and Quick Look-Single Maximum Runup outputs:
    Median Inundation Depth (ft)
    Median Momentum Flux (ft3/sec2)

## Slide 8: Casualty Scenario
Level 1 - Input:
  Fatality Boundary (depth > 2m)
  Hazard Boundary (depth > 0)
  Road Network Data
  Topography (DEM)
  Estimated time of tsunami arrival and maximum runup
Level 2 - Input:
  Output travel time results provided by the USGS Pedestrian Evacuation Analyst Tool

## Slide 9: Road Network Data
Casualty Level 1 assumes a roads only analysis, in that the population will follow the road network to safety
  The Census TIGER road networks data may be downloaded through the Hazus Tsunami model from the Analysis Menu, under Casualty
  Or directly from the Census website at: 2016 TIGER/Line Shapefiles: Roads (https://www.census.gov/cgi-bin/geo/shapefiles/index.php?year=2016&layergroup=Roads)

## Slide 10: Casualty Assessment Results
  Estimates pedestrian evacuation, and warning times to evaluate potential loss of life and injuries
  Two levels of analysis: Basic and Advanced
  Results:
    Evacuation Travel Time (Age Under/Over 65)
    Day/Night population exposure
    Day/Night probability of casualties
    Casualties based on Community Preparedness Level (good, fair, poor)

## Slide 11: Exercise 15.1: Tsunami
Goal: Run a Tsunami Level-1 analysis.
Time: 30 minutes

## Slide 12: Exercise 15.1: Tsunami
Task 1: Open the Study Region.
Task 2: Run a Level 1 Analysis: Runup Only-Mean Sea Level.
Task 3: Run a Level 1 Casualty Analysis.

## Slide 13: Lesson 15: Review
  What are the steps for estimating tsunami losses?
  How does Hazus estimate tsunami casualties?

## Slide 14
Questions