## Slide 1: Lesson 16: Hazus Earthquake and Tsunami Combined Analysis

## Slide 2: Lesson 16: Goal and Objectives
Goal: To understand the interrelationships between earthquakes and tsunamis in Hazus modeling.
After completing this lesson you will be able to:
  Explain the relationship between earthquakes and tsunamis.
  Identify the factors necessary for a combined analysis.

## Slide 3: Earthquake and Tsunami Basics
  Near source scenarios: earthquake starts the tsunami
  Strike-slip fault: vertical fractures where the blocks have mostly moved horizontally
  Thrust fault: reverse fault with a dip of 45 degrees or less

## Slide 4: Earthquake Strength
Magnitude | Effect
< 6.5 | Earthquakes of this magnitude are very unlikely to trigger a tsunami.
6.5 - 7.5 | Earthquakes of this size do not usually produce destructive tsunamis. However, small sea level changes may be observed in the vicinity of the epicenter. Tsunamis capable of producing damage or casualties are rare in this magnitude range but have occurred due to secondary effects such as landslides or submarine slumps.
7.6 - 7.8 | Earthquakes of this size may produce destructive tsunamis especially near the epicenter; at greater distances small sea level changes may be observed. Tsunamis capable of producing damage at great distances are rare in this magnitude range.
> 7.8 | Destructive local tsunamis are possible near the epicenter, and significant sea level changes and damage may occur in a broader region. Note that with a magnitude 9.0 earthquake, the probability of an aftershock with a magnitude exceeding 7.5 is not negligible.

## Slide 5: Near Source Deformed DEM
  Post-earthquake event deformed topography should be used in the case of a near source scenario
  Earthquake could result in several meters of ground deformation, which may substantially change the inundation area and affect potential losses resulting from a tsunami

## Slide 6: Analysis Options
 | Earthquake | Tsunami
 | General buildings Essential facilities Military installation: Advanced Engineering Building Module (AEBM) User-defined structures Utility systems Induced physical damage Direct social losses Indirect economic impact | General Building Stock User-defined facilities Direct damages Functionality and economic loss

## Slide 7: Combined Analysis Options
  Combined General Building Stock
    Direct damages (by count and by square footage)
    Direct economic loss
  Combined User-Defined Facilities
    Direct damages (damage state)
    Functionality
    Economic loss

## Slide 8: Exercise 16.1: Combined Earthquake and Tsunami
Goal: Run a combined near source earthquake and tsunami analysis.
Time: 60 minutes

## Slide 9: Exercise 16.1: Combined Earthquake and Tsunami
Task 1: Open your Tsunami Study Region.
Task 2: Download Near Source Earthquake ShakeMap.
Task 3: Open ShakeMap in Hazus and Run an Analysis.
Task 4: Explore Earthquake Results.
Task 5: Run a Tsunami Analysis.
Task 6: Run the Combined Analysis.
Task 7: Download the Roadways and Run a Level 1 Casualty Analysis.
Task 8: Explore Tsunami and Combined Analysis Results.

## Slide 10: Lesson 16: Review
  How are earthquakes and tsunamis related?
  What type of model is most appropriate for a combined analysis?
  What are the analysis options for a combined tsunami and earthquake scenario?

## Slide 11
Questions