## Slide 1: Lesson 3: Basic Hurricane

## Slide 2: Lesson 3: Goal and Objectives
Goal: To provide a review of the hurricane wind and storm surge model within Hazus.
After completing this lesson you will be able to:
  Review conditions for hurricane development and the parts of a hurricane.
  Describe the areas of the U.S. mainland that have the highest risk to major hurricanes.
  Provide four scenario types that a user can select to run the hurricane model.
  List databases used in the hurricane model.
  Explain damage and loss modeling.

## Slide 3: Hurricane Basics
  Rotate counter-clockwise in the Northern Hemisphere
  Require ocean temperatures around 80 F or 27 C
  Occurs between 5N and 40N in the Atlantic Ocean
  Hurricane season: June 1 through November 30

## Slide 4: Converted Wind Speeds
Typical Storm Parameters
Hazus Input Wind Speeds = 1 Min Mean
Hazus Output Wind Speeds = 3 Sec Gust
Saffir-Simpson Scale | 1 Min Mean (mph) | 3 Sec Gust (mph) | Min Central Pressure (mb)
1 | 74-95 | 90-116 | 980 and up
2 | 96-110 | 117-134 | 965-979
3 | 111-129 | 135-159 | 945-964
4 | 130-156 | 160-189 | 921-944
5 | 157+ | 189+ | 920 and below

## Slide 5: Hurricane Geography
Hurricanes impact the US often follow one of two general paths
  Staying in the Atlantic and tracking up the East Coast
  Tracking the West Coast of Florida and entering the Gulf of Mexico
Major hurricane U.S. strikes:
  Florida has the greatest number
  North Carolina, Louisiana, Mississippi, Alabama, and Texas are also high frequency areas

## Slide 6: Hurricane Impacts
  Hurricane risks and impacts are dependent on the geography
  Different states and regions will have different needs for response, recovery, and mitigation
  The three storms in 2017 affected diverse geographic areas of varying size and population density

## Slide 7: Hurricane Anatomy
  Rain bands
  Eye
  Eye wall*
  Counterclockwise rotation
  *NOTE: A second outer eye wall may develop, but it can be difficult to differentiate from the inner eye wall.

## Slide 8: Hurricane Wind Hazard Model: Wind Field
Wind Field Model:
  Updated version of model used for design windspeeds in ASCE-7-98
  Used in International Building Code Series
  Allows for asymmetries (or unevenly distributed windfields)
Asymmetric Katrina (2005). Cooperative Institute for Meteorological Studies (CIMSS). University of Wisconsin.

## Slide 9: Hurricane Wind Model Scenarios
Probabilistic wind speed database:
  100,000 years of simulated storms

## Slide 10: Hurricane Wind Model Scenarios
Deterministic:
  Historical
  Forecast/Advisory
  User-defined

## Slide 11: Wind Field Model
Solves full non-linear equations of motion for translating hurricane; then establishes parameters for fast running simulation

## Slide 12: Hurricane Wind and Surge Analysis Options
  Wind: losses created first in hurricane model
  Surge: depths are input into the flood model
  Combined flood and wind losses: sub-assembly loss tables

## Slide 13: Hurricane-Specific Inventory
4 regions in Florida and 4 Regions in Hawaii have Hurricane-Specific Inventory and 4 regions for other states
Based on:
  Review of building codes
  Census data
  Aerial photos review
  MLS and tax data samples
Florida/Hawaii building stock regions:
  Different building codes
  Different building practices

## Slide 14: Hurricane Inventory
  Terrain Database: surface roughness
  State-Specific:
    Land-Use: Florida Water Management District
    Elevation: Hawaii Statewide GIS Program
  Historic and Deterministic Storm Models:
    HURDAT or Historic Database
    Hurrevac
  Tree Database: types, height, density
  Hurricane Surge Model: flood depth damage curves

## Slide 15: Damage and Loss Modeling
Damage includes effects of:
  Wind pressures
  Wind-borne debris
  Tree blow-down
  Rainfall
  Storm duration
Models damage explicitly to:
  Roof cover
  Roof deck
  Whole roof failures
  Window and door failures
  Wall damageJacksonville, FL, December 5, 2017 Pockets of debris from Hurricane Irma can still be seen all over the state. Counties are working hard to remove all hurricane related debris as quickly as possible.

## Slide 16: Damage and Loss Modeling
Loss model based on:
  Insurance loss data
  Correlation of financial damage with observed water infiltration and building damage
Current model now includes storm surge:
  Hurricane and flooding analysis is coupled
Debris from Hurricane Irma in Marathon, Florida has been scheduled for removal to clear waterway in this canal, which is surrounded by a full time commercial trailer park.

## Slide 17: Exercise 3.1: Hurricane Study Region
Goal: Build a hurricane study region for Hurricane Harvey (2017).
Time: 10 minutes

## Slide 18: Exercise 3.1: Tasks
Task 1: Create a New Hurricane Study Region.
Task 2: Select Areas Affected (Aransas County) by Hurricane Harvey.

## Slide 19: Lesson 3: Review
  Explain hurricane basics (components needed for development and four parts of a hurricane).
  What areas of the U.S. mainland have the highest risk to major hurricanes?
  Which four scenario types can a user select to run the hurricane model?
  Which databases are used in the hurricane model?
  Explain damage and loss modeling.

## Slide 20
Questions