## Slide 1: Lesson 7: Site-Specific Data and User-Defined Facilities

## Slide 2: Lesson 7: Goal and Objectives
Goal: To explore datasets that effectively support disaster operations.
After completing this lesson you will be able to:
  Explain the differences between GBS and UDF.
  Identify what data is required to complete an assessment.
  Differentiate between the different hazards analysis data.

## Slide 3: Difference Between GBS and UDF
General Building Stock: an engineering based estimation of structures by occupancy
  Aggregate data by Census geography according to hazard type
  Reported by square footage, dollar exposure, building count
  Linked during development, but not in software
User-Defined Facilities: building or structure specific data
  Must be imported through CDMS by the user
  Provides actual locations of buildings
  Replacement value rather than appraisal value of buildings
Site-Specific Data: building or structure specific data
  Some data included in Hazus inventory, such as hospitals, fire stations, and schools
  May include user-defined, AEBM, high potential loss, essential, transportation and utility facilities
  Damages assessed on an individual building basis

## Slide 4: UDF Data
  Produces results and loss estimates at the structure level
  Can often help facilitate risk discussions with individual homeowners or business owners in a community
  Provides valuable information to help pre-screen properties and projects before going through a more in-depth Benefit-Cost Analysis (BCA)
  Generally the best and most accurate approach to analyzing and communicating risk

## Slide 5: Site-Specific Inventory
  Provides actual locations of buildings rather than aggregated General Building Stock tables (site-specific GBS data are referred to as user-defined facilities)
  Sources vary by inventory type:
    Essential Facilities: medical, fire, police, schools, etc.
    High Potential Loss Facilities: dams, nuclear, military
    Transportation Systems: bridges, highways, rail, airports, etc.
    Utility Systems: water, oil, gas, electric, etc.
    Hazardous Material Sites
    User-Defined Facility

## Slide 6: Hazard-Specific Data: Debris Analysis
To complete an assessment of situation, the following data is needed:
  Hazard areas of impact
  Demographics (# of households/density/land use)
  Vegetation coverage
  Critical infrastructure/assets

## Slide 7: Assessor Data
  Data can often be downloaded from county or city governments.
    May be free or require payment
    Will require pre-processing for import to Hazus
  Converting assessor data to user-defined facilities:
    Build appropriate study region
    Create building footprint centroids feature class

## Slide 8: Demonstration 7.1: Tax Assessor Data
Goal: Explore Tax Assessor Data.
Time: 10 minutes

## Slide 9: Hazard-Specific Data: Hurricane Analysis
  Trees: U.S. Forestry Service, LiDAR-derived tree locations, State Department of Natural Resources
  Terrain: Land cover datasets obtained from State Departments of Natural Resources, USGS, or locally derived
  Shelter: Red Cross National Shelter System, State Homeland Security and local shelter personnel. Examine a historic disaster and the sheltering demographics and adjust the parameters
  Economic Loss: U.S. Dept. of Commerces Bureau of Economic Analysis

## Slide 10: Hazard-Specific Data: Flood Analysis
  Debris Weight (no vegetative): R.S. Means
  Shelter: State Homeland Security and local shelter personnel.
  Economic Loss: U.S. Dept. of Commerces Bureau of Economic Analysis
  Agriculture products: damage functions from the U.S. Army Corps of Engineers
  Vehicles: count based on building occupancies in each census block

## Slide 11: Hazard-Specific Data: Earthquake Analysis
  Debris Weight (no vegetative): R.S. Means
  Shelter: State Homeland Security and local shelter personnel.
  Economic Loss: U.S. Dept. of Commerces Bureau of Economic Analysis
  Fire Following: Local fire departments, universities (geology and earthquake hazard research)
  Transportation Economic Loss: Regional and local planning agencies
  Utility Economic Loss: Utility companies (private and local)

## Slide 12: Hazard-Specific Data: Tsunami Analysis
  General Building Stock: US Army Corps of Engineers National Structure (NSI) point data
  Essential User-Defined Facilities
  Casualty analysis: hazard boundary and fatality boundary
  Pedestrian evacuation: travel and warning times
  Community preparedness level (evacuation): FEMA rating of good, fair, or poor
  Traffic factor (evacuation): travel speed and road networks

## Slide 13: Exercise 7.2: UDF Database
Goal: Load UDF into Hazus through CDMS.
Time: 20 minutes

## Slide 14: Exercise 7.2: Tasks
Task 1: Open CDMS and confirm or change State Database.
Task 2: Import the UDF data with CDMS and set Import Parameters.
Task 3: Complete Data Field Mapping.
Task 4: View Table and Import into State Geodatabase.

## Slide 15: Lesson 7: Review
  What is the difference between GBS and UDF?
  What data is required to complete an assessment?
  Describe the different analysis data for the various hazards.

## Slide 16
Questions