## Slide 1: Lesson 8: Basic Flood

## Slide 2: Lesson 8: Goal and Objectives
Goal: To provide a review of the flood model within Hazus.
After completing this lesson you will be able to:
  List the inputs of Flood Hazard.
  Describe the Depth Damage Functions (DDFs).
  Identify the factors that influence flood damage to buildings.
  Explain dasymetric inventory.

## Slide 3: Flood Basics
Flood Hazard Inputs:
  User-Defined analysis options (Quick Look and Enhanced Quick Look)?
  User-Defined depth grid?
  Digital Flood Insurance Rate Map (DFIRM)?
  High Water Mark Data?
  HEC-RAS

## Slide 4: Flood-Specific Inventory
Dasymetric Inventory:
  Flood Model only
  Assumes building exposure only exists within areas which satellite and land-use data confirm there exists a built environment
  Based upon the 2011 National Land Cover Dataset (NLCD)

## Slide 5: Flood-Specific Inventory
General Building Stock:
  Depreciated Replacement Costs
    Estimates depreciated value of structures (used for insurance purposes)
  Distribution of foundation types and first-floor heights
  Estimates the first floor height based upon the foundation type
Models differ for riverine, coastal, and Great Lakes census blocks, as well as for Pre-FIRM and Post-FIRM structures

## Slide 6: Depth-Damage Functions
Default depth-damage functions are assigned based on building characteristics

## Slide 7: Depth-Damage Functions (DDFs)
  Assigned based on building characteristics
  Factors influencing flood damage to buildings:
    Water (most important)
    Duration
    Velocity
    Salinity
  Applied to relevant depth
    Buildings: first-floor height
    Equipment: Height above first floor
  NOTE:
    Low water depths: steep slopes
    High water depths: flatter sections

## Slide 8: GBS Loss Estimation Methodology
Hazus performs an area weighted assessment of damage for aggregate inventory
  Number of grid cells at a given depth is counted and then divided by total number of cells within census block
  Result is used to weight damage at that flood depth for each occupancy

## Slide 9: GBS Loss Estimation Methodology (Cont'd.)
Assumes that inventory is evenly distributed across each census block.
Example: If 25% of the block has 2 ft. of water, it is assumed that 25% of the four single-family dwellings in the block are in 2 ft. of water.
Losses are reported as totals for each occupancy and building type rather than for each building.

## Slide 10: Exercise 8.1: Depth Grid
Goals: Import a 100-year depth grid.
Time: 25 minutes

## Slide 11: Exercise 8.1: Tasks
Task 1: Create a new Salt Lake City Study Region.
Task 2: Open Salt Lake City Study Region.
Task 3: Use Hazus Interface to Define a DFIRM.
Task 4: View Results.

## Slide 12: Lesson 8: Review
  What are the inputs of the Flood Hazard?
  What are the Depth Damage Functions (DDFs) based on?
  What factors influence flood damage to buildings?
  What is dasymetric inventory?

## Slide 13
Questions