## Slide 1: Lesson 9: Hazus Flood for Response

## Slide 2: Lesson 9: Goal and Objectives
Goal: To review the applications of Hazus in flood response.
After completing this lesson you will be able to:
  Understand the flood response timeline.
  Identify when and when not to use Hazus for flood.
  Describe a flood depth grid.

## Slide 3: Flood Response Timeline and Coordination
Preparation for Flooding:
  Identify jurisdictions susceptibility to floods
  Estimating vulnerable zones
  Flood fighting
  NWS issues flood warnings
Once Flooding Occurs:
  Search and Rescue
  Continuity of Operations
  Inspection and Condemnation

## Slide 4: When to Use Hazus for Floods
Use Hazus to create:
  Identify areas with differential impacts
  Create user-defined scenarios
  Utilize depth grids for damage and loss estimations

## Slide 5: When Not to Use Hazus for Floods
  Regulated Streams:
    Not computed in Hazus unless gage available
    Must use user-defined hazard input
  Hydrologic analysis is NOT necessary if you are providing results from another flood study, such as:
    Entering discharges
    Quick Look: drawing a polygon having a constant flood depth
    Enhanced Quick Look: providing a flood plain boundary and DEM
    Providing a flood depth grid
    HEC-RAS input
  Dam Failures - Hazus does not model dam failures
  Creating the flood hazard or anything that is not loss estimation
  Level 1 hydraulic and hydrologic modeling should not be used during response

## Slide 6: Hazus Flood Data Sources
  National Oceanic and Atmospheric Administration (NOAA)
  Federal Emergency Management Agency (FEMA)
  Map Service Center (MSC)
  Flood Insurance Studies
  Risk MAP non-regulatory products
  HEC-RAS (US Army Corps of Engineers)
  National Elevation Dataset (US Geological Survey)
    Bare earth digital elevation models (DEM)
    Source lidar point clouds
    Ifsar digital source models (DSM)
  User-defined depth grids
  Shapefiles, rasters, depth grids, and imagery from state and local governments
Notes: Hazus Flood Data Sources
National Oceanic and Atmospheric Administration (NOAA)
Federal Emergency Management Agency (FEMA)
Map Service Center (MSC)
Flood Insurance Studies
Risk MAP non-regulatory products
HEC-RAS (US Army Corps of Engineers)
National Elevation Dataset (US Geological Survey)
  Bare earth digital elevation models (DEM)
  Source lidar point clouds
  Ifsar digital source models (DSM)
User-defined depth grids
Shapefiles, rasters, depth grids, and imagery from state and local governments

## Slide 7: Depth Grid
  Raster surface with depth value for each pixel
  Interpolates elevation between cross-sections
  Creates a flood elevation surface
  Flood Depth Grid = Flood Surface Ground Elevation
  Sources may include digital flood insurance rate maps, high water mark data, and many are available for download from FEMA MSCDepth grid derived from DFIRM data for Denver, Colorado. Darker shaded areas designate deeper water. For example, the areas adjacent to the river stream. Lighter shaded areas designate shallow water. For example, urban street grids further away from river stream.

## Slide 8: Exercise 9.1: DFIRM Depth Grid
Goals:
  Create a depth grid based off the DFIRM dataset and the Esri ArcMap Spatial Analyst toolset.
  Keep track of the name of the files generated.
Time: 30 minutes

## Slide 9: Exercise 9.1: Tasks
Task 1: Prepare the Data in ArcMap.
Task 2: Interpolate the Water Surface.
Task 3: Prepare the Depth Grid.
Task 4: Understand the DFIRM Database.

## Slide 10: Running the Analysis
  User selects desired analysis lessons to run
  Lessons can be re-run as needed
  Hint: Select only the analysis you need (speeds up processing time)

## Slide 11: Viewing Depth-Damage Functions
Instructor Demonstration
  Open the Depth-Damage Functions viewer for buildings
  Change default damage functions
  View the library
  Demonstrate creating a new damage function

## Slide 12: Agriculture Products
User must input a calendar date (e.g., May 25 that is converted to Julian Calendar (1 to 365) to define relation to crop cycle.
Damage is not flood-depth dependent.
  Area of impacted crop is determined.
No duration estimate is calculated.
  Flood Model estimates flood damage if duration is 0 days, 3 days, 7 days, or 14 days.
Based on USACE's AGDAM method.

## Slide 13: Vehicles
  Damages are based on type of vehicle and depth of water relative to critical vehicle components
  Hazus developed damage functions are based on expert opinion and historical damage data
VehicleType | VehicleID | Description | VehicleHeight | 0 ft | 0.5 ft | 1 ft | 1.5 ft | 2 ft | 2.5 ft
Car | Passenger Car | Damage to car from inundation only | 1.5 | 0 | 7.5 | 15 | 20 | 40 | 60
LtTrk | Light Truck | Damage to light truck from inundation only | 2.7 | 0 | 3 | 6 | 9 | 12 | 15
HvTrk | Heavy Truck | Damage to heavy truck from inundation only | 7 | 0 | 1.9 | 3 | 5 | 7 | 8.3

## Slide 14: Flood Warning
  Warning of imminent flooding can reduce damage up to 35% (The Day Curve)
  Hazus will reduce losses by user-defined percentage

## Slide 15: Debris Parameters
Debris analysis can be modified to account for
  Occupancy and Foundation Type
  Finish, Structure, and Foundation Weight
Specific Occupancy | Foundation Type | Minimum Depth | Maximum Depth | Finish Weight Per Thous Sq Ft | Structure Weight Per Thous Sq Ft | Foundation Weight Per Thous Sq Ft
RES1 | Slab | 0 | 4 | 4.1 | 0 | 0
RES1 | Slab | 4 | 8 | 6.8 | 0 | 0
RES1 | Slab | 8 | 25 | 6.8 | 6.5 | 25

## Slide 16: Shelter
Parameters
  Evacuation buffer
  Income
  Age

## Slide 17: Direct Economic Losses
Parameters:
  Annual Gross Sales
  Restoration Time
  Income and Wage Losses
  Inventory Value

## Slide 18: Lesson 9: Review
  Summarize the flood response timeline.
  When should Hazus for Flood be used? When should it not be used?
  What is a flood depth grid and how is it created?

## Slide 19
Questions