## Slide 1: Lesson 10: Tsunami Analysis

## Slide 2: Goal and Objectives
Goal
This lesson will describe how to conduct a basic tsunami analysis for losses and casualties.
After completing this lesson, you will be able to:
  List the steps for estimating tsunami losses
  Describe the steps for estimating tsunami casualties

## Slide 3: Levels of Tsunami Analysis
Basic (Level 1)
  Out-of-the-box default infrastructure
  Basic user input
Advanced (Level 2/3)
  User-provided data - more accurate to the region
  Data provided by third-party studies/hazard models

## Slide 4: Hazus Analysis Components
Hazard Input
  Tsunami inundation depth
  Velocity or momentum flux
  Topography
  Run-up Height
Infrastructure
  NSI data (point location aggregated)
  User defined structures

## Slide 5: Hazus Analysis Components
Damage and Losses
  Direct damage to structures, contents and nonstructural elements
  Direct economic losses
Casualties
  Evacuation times
  Injury/Fatality estimates
    Age, time of day, community preparedness

## Slide 6: Hazard Analysis - User Input

## Slide 7: Momentum Flux
  Rate of transfer of momentum across a unit area
  Used to determine structural damage to buildings
  Calculated by Hazus (Basic Analysis) using the maximum runup height and topography (DEM)
  Provided by user for Advanced Analysis Level 2 and 3

## Slide 8: Near Source Deformed DEM
  Post-earthquake event deformed topography should be used in the case of a near source scenario
  Earthquake could result in several meters of ground deformation, which may substantially change the inundation area and affect potential losses resulting from a tsunami

## Slide 9: Basic Tsunami Scenario
Two Options:
Level 1: Runup Only-Mean Sea Level (MSL)
  User provided Tsunami runup height raster
Level 1: Quick Look-Single Maximum Runup
  User entered single runup value

## Slide 10: Runup Only - Mean Sea Level (MSL)
Tsunami runup height(R)
  The vertical elevation of the most landward penetration of the tsunami with respect to initial sea level
  Used in combination with the topography raster (DEM) to estimate velocity and for determining content and nonstructural losses based on depth only
  Can be used to create inundation/evacuation map boundaries

## Slide 11: Runup Only-Mean Sea Level (MSL)
Input:
  User provided Tsunami runup height in raster format
  Digital Elevation Map (DEM)
Raster units are defined using the drop down tabs under Metadata

## Slide 12: Digital Elevation Model (DEM)
Determine Required DEM extent
  Model will determine the required DEM extent and extract the rasters from the NED database
  Model will also Download and Unzip the NED data to a working directory under the C://HazardInput/TS/(study region) folder on the users computer

## Slide 13: Digital Elevation Model (DEM)
Determine Required DEM extent
  Merge the DEMs if there is more than one for the area of interest
  Mask the DEM to the study region, which is a time saving technique especially useful for island regions

## Slide 14: Masking DEM
ESRI ArcMap Extract by Mask tool
  Clips the DEM to the Study Region Boundary
  Removes all off shore sections
  Reduces processing time

## Slide 15: Runup Only-Mean Sea Level (MSL)
  Median Inundation Depth (ft)
  Median Momentum Flux (ft3/sec2)

## Slide 16: Quick Look - Single Maximum Runup
Input:
  Maximum Runup Height Value
    Units defined in drop down menu
  Topography Raster (DEM)
Used in combination with the topography raster (DEM) to estimate velocity
*Note: User must merge all DEMs to successfully execute this option.

## Slide 17: Quick Look Single Maximum Runup
Outputs from the process:
  Median Inundation Depth (ft)
  Median Momentum Flux (ft3/sec2)

## Slide 18: Current Hazard Selection
Output data from the User Defined Hazard
  Depth
  Flux
  Hazard Boundary
  Fatality Boundary

## Slide 19: Analysis Options - Tsunami
Options:
General Building Stock
  Direct Damages
  Direct Economic Loss
User Defined Facilities
  Direct Damages
  Functionality and Economic Loss

## Slide 20: Casualty Scenario
Level 1 - Input:
  Fatality Boundary (depth > 2m)
  Hazard Boundary (depth > 0)
  Road Network Data
  Topography (DEM)
  Estimated time of tsunami arrival and maximum runup
Level 2 - Input:
  Output travel time results provided by the USGS Pedestrian Evacuation Analyst Tool

## Slide 21: Road Network Data
Casualty Level 1 assumes a roads only analysis, in that the population will follow the road network to safety
  The Census TIGER road networks data may be downloaded through the Hazus Tsunami model from the Analysis Menu, under Casualty
  Or directly from the Census website at: 2016 TIGER/Line Shapefiles: Roads (https://www.census.gov/cgi-bin/geo/shapefiles/index.php?year=2016&layergroup=Roads)

## Slide 22: Hazard/Fatality Boundary Layers
Hazard Boundary
  Entire Inundation area
  Where depth > 0
  Zone with 50% fatality and 50% injury
Fatality Boundary
  Where depth > 2m
  Zone with 99% fatality and 1% injury

## Slide 23: Beware of Boundary Slivers
  Review the Hazard Boundaries to determine if slivers along the coast or other small pockets intersect with the roads, and remove them
  The model could interpret these areas as safe zones

## Slide 24: Casualty Time Parameters
Arrival Time
  Estimated arrival of first tsunami wave
Time to Maximum Runup
  Time to the estimated maximum inundation
Warning Time
  Estimated time to warn the population (this may be 0 in the case where ground shaking provides the warning)

## Slide 25: Speed Conservation Value
Speed Conservation Value
  Resistance factor
Default value is 1 which assumes that all of the roads are clear and open

## Slide 26: Travel Speed
Travel Speed of evacuation population
  Based on the USGS Pedestrian Evacuation Model Parameters
Default value is Average Walk
  Assumes average speed is 1.22 m/s
Option to set the maximum travel time in minutes required to reach safety

## Slide 27: Activity 10.1
  Defining a Basic Level Analysis
  Defining a Casualty Level 1 Analysis

## Slide 28: Review
  What inputs are required for a Level 1 analysis?
  Why is it important to check the Fatality and Hazard boundaries prior to running the Casualty Analysis?
  What does the current version of the Tsunami Model NOT estimate?

## Slide 29: Questions?