## Slide 1: Lesson 12: Hurricane Hazard

## Slide 2: Goal and Objectives
Goal
This lesson will provide an overview of the hurricane wind hazard.
After completing this lesson, you will be able to:
  List the steps and purpose for completing a historic storm analysis.
  List the steps and purpose for completing a User-Defined scenario.
  Explain the steps and purpose for completing a probabilistic hurricane analysis.

## Slide 3: Hurricane Hazard Model
Storms initiated in:
  Atlantic
  Caribbean
  Gulf of Mexico
  Eastern Pacific
  Central Pacific
The Wind Model allows for the following hurricane behaviors:
  Storm curvature
  Multiple land falls
  Changes in intensity
  Updated version of model used for design wind speeds in ASCE-7-98
Only available in Hurricane States in the Atlantic and Hawaii. Puerto Rico and USVI are in the process of being built out.

## Slide 4: Hurricane Wind Hazard Model - 3 Parts
Wind field model
  Upper level mean flow field
  Boundary layer model that relates upper level winds to surface level winds
Track model
  Determines starting point, path, translation speed
Rainfall model
  Estimates amount of precipitation associated over duration of event

## Slide 5: Wind Field Model
Solves full non-linear equations of motion for translating hurricane; then establishes parameters for fast running simulation

## Slide 6: Hurricane Hazard: Hurricane Track Model
Models entire track of tropical storm:
  Allows storms to curve and change speed and intensity as they move
  Models hurricane wind risk over large regions
  Based on HURDAT database from National Hurricane Center (NHC)

## Slide 7: Hurricane Hazard: Rainfall Model
One of most difficult items to simulate
  Non-linear interactions of weather fronts and topography
Model uses following parameters:
  Central pressure deficit
  Storm category
  Storm translation speed
Validation done with rainfall measurements from Hurricane Hugo (1989), Bertha (1996), Fran (1996), and Bonnie (1998)
Current model produces reasonable estimates of rainfall.
Expect significant variation with actual events due to un-modeled effects.

## Slide 8: Terrain Model
Surface roughness slows wind down due to friction
Roughness elements:
  Buildings
  Trees
  Vegetation
  Hills

## Slide 9: Tree Blow Down Model
Tree effects during wind storms
  Positive
    Provide shelter to structures, reducing wind pressure
  Negative
    Falling trees produce a strike hazard to structure
    Fallen trees add to amount of debris to dispose of after storm

## Slide 10: Tree Database in Hazus
Three tree types
  Deciduous
  Coniferous
  Mixed
Tree Density (stems per acre)
3 broad height categories
  30 - 40 ft
  40 - 60 ft
  60+ ft

## Slide 11: Tree Database in Hazus
Census Block | Predominate Tree Type | Stems Per Acre | Tree Height <40ft | Tree Height 40ft-60ft | Tree Height 60ft+ | Tree Collection Factor
130259601001000 | Mixed | 62 | 9 | 64 | 27 | 0.16
130259601001001 | Mixed | 114 | 9 | 64 | 27 | 0.15
130259601001002 | Mixed | 101 | 9 | 64 | 27 | 0.25
130259601001003 | Mixed | 121 | 9 | 64 | 27 | 1
130259601001004 | Mixed | 26 | 9 | 64 | 27 | 1
130259601001005 | Mixed | 89 | 9 | 64 | 27 | 0.33
130259601001006 | Mixed | 77 | 9 | 64 | 27 | 0.38
130259601001007 | Mixed | 115 | 9 | 64 | 27 | 0.02
130259601001008 | Coniferous | 39 | 9 | 64 | 27 | 0.06
130259601001009 | Mixed | 102 | 9 | 64 | 27 | 0.07

## Slide 12: Historic Storm Scenario
Pre-computed wind fields and storm tracks for many US landfalling hurricanes
Region Filter button
  Only those storms that affect study region state
Peak Gust
  Largest modeled gust speed over land anywhere in US
  Hurricanes Sandy, Harvey, Irma, Maria, and Nate are based on observed winds

## Slide 13: Exercise 12.1
Student Activity
  Run Historic Scenario Hurricane

## Slide 14: Review
Historic Storm Scenarios:
  Describe the softwares storm database
  Define peak gusts
  What are the major steps for defining a historic storm scenario?
  In what type of situation would you want to use a historic scenario?
Answer the following questions using your activity study region:
  Which storm that affected North Carolina had the highest peak gust winds?
  Which census tract had the highest maximum sustained winds?

## Slide 15: Probabilistic Storm Set
What if we ran every possible scenario?
Probabilistic storm set
  100,000 years worth of storms
  Vary in size, strength, speed, direction
Provides objective way to compare risk of different areas

## Slide 16: Probabilistic Results
Return Period Event
7 Return Period Events
  7 single storm scenarios from 100,000 year storm database
  Representation of the return period losses for study region
    10, 20, 50, 100, 200, 500, 1000 years
  Return periods are based on total direct economic loss for entire study region
Full set of results provided
  Damage, debris, shelter, etc.
  Dollar losses

## Slide 17: 7 Return Period Events
Events Sorted by Total Loss

## Slide 18: Selecting Probabilistic Analysis
Click Hazard | Scenario | Activate
Select
Probabilistic

## Slide 19: Probabilistic TOC versus Scenarios

## Slide 20: Activity 12.2
Student Activity
  Run Probabilistic Scenario Hurricane
  Compare Historic and Probabilistic Hurricane Scenario Results

## Slide 21: Review
Probabilistic Storm Scenarios
  What are the seven return period events that are represented in a probabilistic scenario?
  In what type of situation would you want to use a probabilistic scenario?
  Explain the difference between the TOC and results menu return period peak gust maps and data?
Answer the following questions using your activity study region:
  What are the total direct economic losses for a 1000 year event?
  What is the 1000 year return period peak wind gust?
  Which Census Tract has the highest peak wind gust?

## Slide 22: User Defined Scenario
4 options
  Define manually.
  Import from exported file (other Hazus users)
  Import from Hurrevac*
Select Define Storm Track Manually and click the Next button
*Preferred Method

## Slide 23: Define Storm Track Manually

## Slide 24: Parameters - Translation Speed
How fast is the storm moving?

## Slide 25: Interaction of Translation and Rotation Speeds
Increase in rotation speed means different % increase on right and left side of storms

## Slide 26: Parameters Storm Size
Radius to Max Winds:
  Radius to maximum wind speed indicates the size of the storm
  Range of 6-60 miles
Radius to 64kt/50kt/34kt
Force Winds:
  Maximum radius from center of storm to 64Kt (74 mph) wind speeds (1 min mean)
  Range of 10-200 miles

## Slide 27: Parameters - Storm Intensity
Maximum Wind Speed
Profile Parameter (B)
  Parameter that describes the rate of pressure drop in the storm
  Pressure drop determines the maximum wind speed

## Slide 28: Converted Wind Speeds
Typical Storm Parameters
Hazus Input Wind Speeds = 1 Min Mean
Hazus Output Wind Speeds = 3 Sec Gust
Saffir-Simpson Scale | 1 Min Mean (mph) | 3 Sec Gust (mph) | Min Central Pressure (mb)
1 | 74-95 | 90-116 | 980 and up
2 | 96-110 | 117-134 | 965-979
3 | 111-129 | 135-159 | 945-964
4 | 130-156 | 160-189 | 921-944
5 | 157+ | 189+ | 920 and below

## Slide 29: Hurricane Advisories
  Current and past forecast advisory information is available from the National Hurricane Center (NHC)
  Forecast advisories can be entered into Hazus for analysis
  Forecast points will generate a range of potential losses in the Rapid Loss Assessment Report

## Slide 30: When to Start Running Hazus

## Slide 31: Storm Track Definition

## Slide 32: Activity 12.3
The Instructor will
  Walk through the scenario definition wizard where a user can enter their own user defined scenario
  Discuss the differences between a HURREVAC Import, import from exported file, and a user defined scenario

## Slide 33: Show Current Scenario
Select Hazard | Show Current
Brings up window with your current active scenario.

## Slide 34: Review
User Defined Storm Scenarios
  What are the four primary options for user defined scenarios?
  To use a NHC Advisory, which Storm Track Definitions would you pick?
  What does the storm's location at specific times or translation speeds tell the model?
  What do the radius inputs tell the model?
  What do the Maximum Wind Speeds or Profile Parameters tell the model?

## Slide 35: Questions?