## Slide 1: Lesson 13: Hurricane Analysis

## Slide 2: Goal and Objectives
Goal
This lesson will provide an overview of the methodologies used for hurricane wind analysis.
After completing this lesson, you will be able to:
  Understand hurricane-specific inventory
  Explain the basic process by which Hazus calculates hurricane-related losses
  Provide examples of hurricane analysis parameters that the user can define

## Slide 3: Hurricane-Specific Inventory
4 regions in Florida and 4 Regions in Hawaii have Hurricane-Specific Inventory and 4 regions for other states
Based on:
  Review of building codes
  Census data
  Aerial photos review
  MLS and tax data samples
Florida/Hawaii building stock regions:
  Different building codes
  Different building practices

## Slide 4: Wind Loads (Pressure)
In practice, design wind loads on buildings are determined, using:
  Wind tunnel data, or...
  Building code provisions based on wind tunnel data
Wind pressure is a function of:
  Wind speed
  Wind direction
  Location on building

## Slide 5: Wind-Borne Debris
Two wind-borne missile models used in Hazus
  Residential
    Shingles, wood, sheathing type missiles
  Commercial
    Grave missiles from built-up roofing

## Slide 6: Building Resistance
  Water Resistance
  Masonry Reinforcements
  Shuttering
  Roof - Wall Connections
  Roof - Deck Attachments
  Tie Downs
  Manufactured Housing Roof Covers

## Slide 7: Loss Model
Physically based damage-to-loss model
Computes direct economic losses, using
  Explicit cost
    Windows, doors, sheathing, roof cover, etc.
  Implicit cost
    Estimates of volume of water entering through failed windows, doors, etc.
Details of loss models found in the Hurricane Technical Manual

## Slide 8: Activity 13.1
The Instructor will lead the class to
  Explore the Analysis Menu
  Answer the following questions:
    In the Building Damage Function Viewer, for a masonry single-family 1-story home with default characteristics, what is the probability of moderate damage at 130 mph?
    In the Building Loss of Use Function Viewer, for a manufactured home built between 1976 and 1994 with tie downs but without shutters, what is the loss of use in days at 120 mph in light suburban terrain?

## Slide 9: Building Debris Model
Building Debris model is based on:
  Damage state for structural and non-structural components of Hazus model buildings
  Weight statistics for components
    ASCE 7-98 Commentary
    Manufacturer's manuals
    RSMeans 2001
  Typical density of debris type

## Slide 10: Activity 13.2
The Instructor will
  Explore the Debris Function Viewer

## Slide 11: Tree Analysis Parameters
Estimates based on:
  Tree coverage database (can be edited)
  Tree Blowdown model
Expected green weight of tree stems for trees greater than 30-ft tall
Eligible tree debris
Debris estimates made for all areas
  Unpopulated areas may not be collected
Volume based on 10 cubic yards/ton

## Slide 12: Terrain Analysis Parameters
Roughness lengths
  Higher roughness creates more drag at surface, which yields lower wind speeds at surface.
Wind speed increases with height.

## Slide 13: Social Losses - Shelter
Calculates need for public shelters.
Parameters:
  Age
  Ethnicity
  Income
  Home Ownership
  Damage States of different types of buildings.

## Slide 14: Economic Impacts
Direct Economic Loss Parameters include:
  Annual Gross Sales
  Business Inventory
  Disruption
  Restoration Time
  Income and Wage Losses

## Slide 15: Activity 13.3
Explore the hurricane analysis options:
  Run the Hurricane Fran hazard and complete the analysis.
  View the windfield model outputs.
  Explore the Hazus provided tree inventory and review the results of the analysis for tree debris.
  Modify the tree inventory and review the updated tree debris results.

## Slide 16: Review
Briefly summarize how the physical damage model works.
What kinds of building characteristics can you alter in the building damage function viewers?
What are the parameters for sheltering that can be altered by the user?
What are the two wind-borne missile models used in Hazus?

## Slide 17: Questions?