## Slide 1: Lesson 14: Hurricane Wind Results

## Slide 2: Goal and Objectives
Goal
This lesson will provide an overview of the results of a hurricane wind model results.
After completing this lesson you will be able to:
  List the key outputs of the aggregate inventory analysis
  List the key outputs of the site-specific inventory analysis
  Identify the key guidelines for properly interpreting and applying the outputs of the hurricane wind model

## Slide 3: Viewing Results
Results menu is enabled when a hurricane scenario has been run

## Slide 4: Hazard Maps
To show the hazard map, choose:
  Results | Wind Speeds
Click on the column you wish to map
Click the Map button

## Slide 5: Direct Physical Damage
Structural Damage for Buildings:
  Damage State Probability Counts and Losses by Occupancy and Building Type
  The Technical Manual describes damage states for building types

## Slide 6: Direct Physical Damage: Example of Damage States for Residential Building
Damage State | Qualitative Damage Description | Roof Cover Failure | Window Door Failures | Roof Deck | Missile Impacts on Walls | Roof Structure Failure | Wall Structure Failure
1 | No Damage or Very Minor Damage: Little or no visible damage from the outside. No broken windows, or failed roof deck. Minimal loss of roof cover, with no or very limited water penetration | = 2% | No | No | No | No | No
2 | Minor Damage: Maximum of one broken window, door or garage door. Moderate roof cover loss that can be covered to prevent additional water entering the building. Marks or dents on walls requiring painting or patching for repair. | > 2% and = 15% | One window, door, or garage door failure | No | < 5 impacts | No | No
3 | Moderate Damage: Major roof cover damage, moderate window breakage. Minor roof sheathing failure. Some resulting damage to interior of building from water. | > 15% and = 50% | > one and = the larger of 20% & 3 | 1 to 3 panels | Typically 10 to 20 impacts | No | No
4 | Severe Damage: Major window damage or roof sheathing loss. Major roof cover loss. Extensive damage to interior from water. | > 50% | > the larger of 20% & 3 and = 50% | > 3 and = 25% | Typically 10 to 20 impacts | No | No
5 | Destruction: Complete failure and/or, failure of wall frame. Loss of more than 50% of roof sheathing. | Typically > 50% | > 50% | > 25% | Typically > 20 impacts | Yes | Yes

## Slide 7: Direct Physical Damage
Essential Facilities:
  Loss of Use (Days)
  Damage State Probability

## Slide 8: Debris
Building Debris
  Wood and Masonry
  Steel and Concrete
Tree Blowdown
  Tree Debris
  Eligible Tree Debris
    Determined by building density, length of roads, and census block shapes
    Trees downed in close proximity to streets, highways, or buildings make up the great majority of trees brought to the curb for collection and disposal

## Slide 9: Debris
Census Tract | Brick/ Wood (tons) | Concrete/ Steel (tons) | Eligible Tree Weight (tons) | Eligible Tree Volume (cubic yards) | Trees (tons) | Tree Volume (cubic yards)
13039010100 | 10,331 | 179 | 48,007 | 480,069 | 1,077,596 | 10,775,960
13039010200 | 31,804 | 872 | 43,345 | 433,450 | 732,303 | 7,323,028
13039010301 | 20,059 | 482 | 14,618 | 146,181 | 106,484 | 1,064,839
13039010302 | 7,954 | 103 | 18,329 | 183,294 | 295,683 | 2,956,830
13039010401 | 64,311 | 444 | 17,089 | 170,894 | 57,399 | 573,990
13039010402 | 33,085 | 805 | 14,127 | 141,267 | 67,878 | 678,778
13039010403 | 27,653 | 515 | 11,459 | 114,594 | 57,794 | 577,938

## Slide 10: Shelter
Shelter:
  Number of Displaced Households
  Temporary Housing Requirements
  Based on Demographic Considerations (Ethnicity, Income, Age, Ownership)

## Slide 11: Direct Economic Losses
General Building Stock Loss
  Building Losses:
    Structural
    Non-Structural
    Content
    Business Inventory
  Business Interruption Losses:
    Wage
    Income
    Rental & Relocation
    Proprietor

## Slide 12: Uncertainty Analysis
The Forecast Uncertainties Model uses statistics to forecast errors compiled from the period 1993- 2004 to simulate a range of possible outcomes. This report displays the 5th and 95th percentiles of the simulated outcomes.

## Slide 13: Automated Output Options
Automatically save reports.
Create thematic maps of results on the fly.
Drawback: Increases analysis processing time.
Uncheck Automated Output Options to make analysis faster

## Slide 14: Automated Output Options
  Auto-generated reports are saved in the study region folder
  Reports can be saved as PDF, Word, Excel, or HTML files
  User can also auto generate map layers

## Slide 15: Activity 14.1
Explore the results:
  Duplicate a study region
  Define the Hurricane Fran scenario
  Run the analysis
  Explore single family residential structure damage
  Explore the building damage summary reports.
  Explore the debris result
  Explore the estimated shelter requirements
  View the exported reports

## Slide 16: Review
Answer the following questions in groups:
  Which school is estimated to be unusable for the longest period of time after the hurricane?
  Which Census Tracts are expected to have the highest need for tree collection by the government for this event?
  For estimated Moderate building damage, rank the Building Types based on the loss ratio (not building counts).

## Slide 17: Questions?