## Slide 1: Lesson 15: Hurricane Storm Surge Results

## Slide 2: Goal and Objectives
Goal
This lesson provides an overview of the storm surge model within Hazus.
After completing this lesson you will be able to:
  Describe the purpose of the Hazus surge model
  Understand the procedure for running a storm surge analysis in Hazus

## Slide 3: Factors Influencing a Surge's Size
Storm surge
  Abnormal rise in the water level by a storm that is above the predicted astronomical tide
Storm tide
  The combination of the storm surge at high tide
Wave breaking
  Can increase the height of the surge and is dependent on the continental shelf

## Slide 4: Factors Influencing a Surge's Size
Wind and Storm Motion
  Strongest winds and thus highest surge (without coastline effects) occur in the right - front quadrant of hurricane
  Here the forward speed of the hurricane is added to the rotational winds of the hurricane to get the highest wind speeds

## Slide 5: Coastline Effects and Surge Size
  The orientation of the hurricane with respect to the coastline can influence the surge magnitude
  Water can pile up with favorable orientations. If hurricane winds are pushing against the coastline, water is caught along the coast.
  Water can also be trapped in bays

## Slide 6: Storm Surge Modeling in Hazus
User works in Hurricane Wind model then in Flood model
Utilizes industry standard models:
  SLOSH - Sea, Lake, and Overland Surges from Hurricanes, National Weather Service's Meteorological Development Laboratory.
  SWAN - Simulating Waves Nearshore, Delft University of Technology
  Modified WHAFIS - to propagate waves inland from the shoreline
Allows for estimation of combined economic losses to general building stock for hurricane scenarios on coastal flood regions
Avoids double counting of flood and wind losses

## Slide 7: Storm Surge Steps
Create study region with Hurricane and Flood
Hurricane: Define/Select Hurricane Scenario
  Surge supported for: Historic, User-Defined, HurrEvac Import, Hazus Import
  NOT supported for: Probabilistic, H*Wind Import
Hurricane: Run Analysis with
  Surge with coupled deep water and near shore waves
  Surge with coupled near shore waves (SLOSH + SWAN)
Surge only (SLOSH only)

## Slide 8: Storm Surge Steps (Cont'd.)
Hurricane: Enter Initial Water Level
Hurricane: Can display Wind-Only Loss Results at this point
Hurricane: Can check status of coastal surge
Switch to Flood Hazard
Flood: Select Coastal surge
Flood: Define Topography (DEM)
Flood: Define Scenario

## Slide 9: Storm Surge Steps (Cont'd.)
Flood: Delineate Floodplain
Flood: Run General Building Stock Analysis*
Flood: Run Combined Loss Analysis
View Results
* Run any additional flood-only results you want, but GBS is all that is needed to support combined surge analysis - ONLY GBS is analyzed in a surge analysis.

## Slide 10: View Results
Hurricane: View Hurricane Wind Only Results
  Includes any analysis chosen
Flood: View Flood Only Results
  Includes any analysis chosen
Hurricane or Flood: View Combined Wind and Surge Results
  Direct Economic Losses Only
  As a table or report

## Slide 11: Activity 15.1
Student Activity
  Import a completed hurricane wind/ storm surge combined loss study region
  Explore the results of the analysis

## Slide 12: Review
What is the purpose of the Hazus surge model?
Which hazard do you analyze first when doing a combined wind/storm surge analysis in Hazus?

## Slide 13: Questions?