## Slide 1: Lesson 2: Hazus Inventory

## Slide 2: Goal and Objectives
Goal
This lesson will explore the features of the Hazus inventory.
After completing this lesson, you will be able to:
  Explain the difference between site-specific and aggregate inventory
  List examples of inventory that are common across all hazard models
  Navigate the Inventory menu

## Slide 3: Hazus Inventory Types
Aggregate
Information about demographics and the general building stock (GBS) in census tracts or census blocks represented by polygons
Site-specific
Information about the built-environment, such as essential facilities, transportation and utilities represented by points and lines

## Slide 4: Aggregate Inventory
General Occupancy Types
  Residential
  Commercial
  Industrial
  Religion/Non-profit
  Government
  Education
  Agriculture

## Slide 5: Aggregate Inventory
33 Specific Occupancy Categories
  Residential (11)
  Commercial (10)
  Industrial (6)
  Religion/Non-profit (1)
  Government (2)
  Education (2)
  Agriculture (1)
View the categories from the Inventory menu

## Slide 6: Aggregate Inventory
Specific Occupancy Types - Residential
  RES1 Single Family Dwelling
  RES2 Mobile Home
  RES3 Multi-Family Dwellings
    RES3A Duplex
    RES3B 3-4 Units
    RES3C 5-9 Units
    RES3D 10-19 Units
    RES3E 20-49 Units
    RES3F 50+ Units
  RES4 Temporary Lodging
  RES5 Institutional Dormitory
  RES6 Nursing Home
Specific Occupancy Types - Commercial
  COM1 Retail Trade
  COM2 Wholesale Trade
  COM3 Personal and Repair Services
  COM4 Professional/Technical Service
  COM5 Banks
  COM6 Hospitals
  COM7 Medical Office/Clinic
  COM8 Entertainment and Recreation
  COM9 Theaters COM10 Parking

## Slide 7: Examples - Occupancy Type

## Slide 8: Aggregate Inventory
Building Types:
General Building Types (All Models)
  Concrete
  Steel
  Manufactured Housing
  Wood
  Masonry
Specific Building Types
  Unique to each model

## Slide 9: Aggregate Inventory
Example of Specific Building Type for Earthquake Inventory
Specific Building Type | General Description | Specific Description
W1 | Wood | Wood, Light Frame, All heights
W2 | Wood | Wood, Commercial and Industrial, All heights
S1L | Steel | Steel Moment Frame, Low-rise, 1-3 stories
S1M | Steel | Steel Moment Frame, Mid-rise, 4-7 stories
S1H | Steel | Steel Moment Frame, High-rise, 8+ stories

## Slide 10: Mapping Schemes
Mapping schemes describe characteristics of buildings within a census tract or block
Examples:
  Foundation type
  First-floor elevation
  Construction materials
Generally expressed as a percentage
The default mapping schemes of your study area may be updated to better represent the accurate distribution of buildings using local data

## Slide 11: Activity 2.1
The Instructor will
  Explore the aggregate inventory and mapping schemes
  Lead students to answer the following questions:
    Where might you find information to update the Hazus-provided building inventory?
    Why does Hazus collect information about how a building is used as well as information about the materials from which it is constructed?

## Slide 12
O = Mapping Only
/ = Some Analysis X= Analysis
Inventory | Earthquake | Flood | Hurricane | Tsunami
Essential facilities | X | X | X | O
Transportation Systems | X | / | O | O
Utility Systems | X | X | O | O
High Potential Loss Facilities | / | O | O | O
User Defined Facilities | X | X | X | X
Hazardous Materials Facilities | O | O | O | O
Advanced Engineering Building Module | X |  |  | 

## Slide 13: User-Defined Facilities
  User-Defined Facilities (UDFs) are any individual buildings that you may wish to add to the study region
  UDFs are not designed to replace engineering models or knowledge
  UDF results are best used by summing all the UDF results for an area rather than using individual structure results

## Slide 14: GBS Results
Earthquake | Flood | Hurricane | Tsunami
Damage by Building Type | Damage by Occupancy | Damage Probabilities by Occupancy | Damage by Count
Damage by Building Count | Damage by Building Type | Damage Probabilities by Building Type | Damage by Square Footage
Damage by Square Footage | Damage by Building Count | Cost of Building Repair or Replacement | Building Economic Loss
Direct Economic Loss | Economic Loss by Full Replacement | Loss of Contents | 
Building Loss by Damage State | Economic Loss by Depreciated Replacement | Business Inventory Loss, Business Income Loss, Employee Wage Loss | 
 |  | Loss of Rental Income, Relocation Costs | 

## Slide 15: Activity 2.2
The Instructor will
  Explore the site-specific inventory
  Lead students to answer the following questions:
    How many fire stations are in your county?
    Based on the values in the EfClass field, how many types of schools are in your study region?
    How many different classes of bridges does Hazus support?
    What unit of measurement is used for the length field in the highway bridge table?

## Slide 16: Review
What are examples of Hazus site-specific inventory?
What are examples of Hazus aggregate inventory?
What is the difference between building occupancies and building types? Give examples of each.
Where would you look in Hazus for a definition of a RES2 occupancy?

## Slide 17: Updating the Default Hazus Data
Comprehensive Data Management System (CDMS)
A Hazus support tool providing the ability to move data to and from Hazus state datasets
Enables users to assess the impacts of mitigation strategies used to help address issues generated by hazards

## Slide 18: CDMS Workflow
CDMS Workflow

## Slide 19: CDMS Usage Example
Example: Update Essential Facilities
  Export the default data from Hazus using CDMS
  Update the default data using local data
  Import the updated data into the CDMS Repository
  Use the updated data in a new Hazus analysis
  Package and distribute data, if necessary

## Slide 20: Activity 2.3
Use CDMS to update the Charleston County Fire Station inventory:
  Setup the CDMS state data location
  Review the Hazus-MH default Fire Stations
  Export the Hazus-MH Fire Stations to an Excel file
  Review a 'Hazus-ready' user-provided Fire Stations inventory created in Excel
  Import the user provided Fire Stations into CDMS
  Transfer the updated Fire Station inventory to the state database
HINT: If the Excel sheet is larger than the data extents, you will import empty fields and/or records

## Slide 21: Questions?