## Slide 1: Lesson 3: Flood Hazard

## Slide 2: Goal and Objectives
Goal
This lesson will provide an overview of the flood hazard.
After completing this lesson, you will be able to:
  Understand how Hazus creates a flood depth grid based on a return period or discharge analysis
  List the user-defined hazard options
  Provide examples of the What-If features
  Describe the key inputs for defining a coastal flood hazard

## Slide 3: Basic Concept of Hazard Determination
Subtract ground surface from flood surface to determine flood depth throughout the study area.

## Slide 4: Riverine Hazard Delineation Options

## Slide 5: User-Defined Hazard Options
User-Defined Hazard Options
  Quick Analysis
  Quick Look
  Enhanced Quick Look
  Flood Information Tool
  User-Defined Depth Grid
  HEC-RAS
User-defined hazard options are covered in E0172: Hazus for Floods Course

## Slide 6: User-Defined Hazard Options
Users can import custom depth grids into Hazus to replace USGS DEMs and using Hazus to model the floodplain

## Slide 7: HEC-RAS
Users can import HEC-RAS models into Hazus to replace USGS DEMs

## Slide 8: Riverine Flood Hazard Process - Return Period and Discharge Riverine Flood Hazard Process

## Slide 9: Return Period and Discharge
Defining Topography
  Required DEM extents are automatically determined by Hazus.
  Hazus downloads and unzips files to be used.

## Slide 10: Return Period and Discharge Process
Defining Topography (Cont'd.)
  Hazus clips the portion of the DEM that is needed to perform flood modeling
  DEM is shaded to show elevation changes

## Slide 11: Return Period and Discharge Process
User defines drainage area
  Larger drainage area generates fewer, larger streams (faster)
  Smaller drainage area generates more, smaller streams (slower)
Hazus uses topography to identify stream locations

## Slide 12: Return Period and Discharge Process
Define a Scenario
  Identify the reaches to be analyzed
  Study regions can contain multiple scenarios
  Reaches can be assigned to one or more scenarios
Example of selected reaches

## Slide 13: Hydrologic Analysis
Determines discharge-frequency relationship for each reach in study region

## Slide 14: Hydrologic Analysis
Hazus Approach:
  Gaged reaches: Derive curves from the USGS Streamflow Basin Characteristics File
  Hazus provided database includes approximately 11,000 gage locations and associated statistics
USGS Gage Location

## Slide 15: Hydrologic Analysis
Hazus Approach:
  Ungaged reaches: Apply USGS regression equations
  Input to equations comes from DEM as well as a number of Hazus-MH provided datasets such as temperature, snowfall, and others

## Slide 16: Hydrologic Analysis
Hazus Approach:
  Includes a database of reaches - based on 100-square mile drainage areas - used to identify the selected reaches that are on major streams
  Discharge values are interpolated from the corresponding values in the default flood frequency database
Reach Network

## Slide 17: Hydraulic Analysis
Hazus Approach:
  Given discharge and stream channel morphology, compute flood elevations
Hazus Output:
  Flood elevations
  Flood depth grid for each user-defined frequency or discharge

## Slide 18: Hydraulic Analysis
Select type of flood analysis for each reach in the scenario
Analysis Types:
  Full suite of return periods
  Single return period *
  Single discharge *
* Each reach can have a different return period or discharge
Numbered stream reaches

## Slide 19: Annualized Loss
  The average annualized loss (AAL) is the estimated direct economic losses averaged on an annual basis using estimated direct economic losses
  AAL provides a community with a common economic frame of reference they can use to compare flood losses against other hazards
  AAL can be used in determining the financial feasibility of mitigation projects

## Slide 20: Annualized Loss - Steps
1. Select to run the Full Suite of Return Periods during the Hydraulic Analysis (Produces 5 sets of depth grids for each reach that was selected in the scenario)
2. Run the General Building Stock analysis and/or the User Defined Facility Analysis
3. Run the Annualized Loss Analysis

## Slide 21: Riverine What-Ifs: Levees
DEMs generally do not capture levees because of their narrow width
Hazus Benefits:
  Determine inundation area with and without levee
  Assess impact with and without levee

## Slide 22: Riverine What-Ifs: Levees (Cont'd.)
  Draw levee so that it crosses the floodplain twice
  Enter flood recurrence interval levee protects against (e.g., 200-year)

## Slide 23: Coastal Model Overview
Level 1

## Slide 24: Coastal Hazard Data
National shoreline
  Includes a smoothed shoreline for transect development
Attribution of census blocks as coastal or great lakes

## Slide 25: Modeled Wave Effects
Wave setup:
  Increase in the Stillwater level caused by waves breaking near the shoreline
Simplified overland waves:
  Affected by water depth
  Results from wave height analyses combined to develop a single water surface

## Slide 26: Coastal Transect Analysis
  Analyses performed along shore-normal transects, affected by an increased inference line
  Transect spacing is uniform based on shoreline characteristics that are closer in complex terrain

## Slide 27: Coastal Hazard Setup

## Slide 28: Coastal Hazard Setup - FIS
FEMA Flood Insurance Study (FIS)
  100-year still water elevations can be found in the FIS
  Other return periods are sometimes provided too
  Vertical datum is provided at the top of the table
  Each record in the table is associated with a transect location provided in a FIS map

## Slide 29: Coastal Hazard Output
Model calculates
  Flood surface, considering wave height
  Flood depth
Flood model develops A, Coastal A, and V zones.

## Slide 30: Review
What are the steps for defining a riverine flood hazard based on a return period?
When defining the drainage area, which would create a denser stream network: 2 or 5 square miles?
If you define a flood hazard that is based on a stream discharge, do you need to run the hydrology?
What are the two required parameters for defining a coastal flood hazard?

## Slide 31: Questions?