## Slide 1: Lesson 4: Flood Analysis

## Slide 2: Goal and Objectives
Goal
This lesson will provide an overview of the methodologies used for food analysis.
After completing this lesson, you will be able to:
  Understand flood-specific inventory
  Explain the process by which Hazus calculates flood-related losses
  Summarize analyses that can be completed in the flood model
  Provide examples of flood analysis parameters that the user can define

## Slide 3: Flood-Specific Inventory
Dasymetric Inventory:
  Flood Model only
  Assumes building exposure only exists within areas which satellite and land-use data confirm there exists a built environment
  Based upon the 2011 National Land Cover Dataset (NLCD)

## Slide 4: Flood-Specific Inventory
General Building Stock:
  Depreciated Replacement Costs
    Estimates depreciated value of structures (used for insurance purposes)
  Distribution of foundation types and first-floor heights
  Estimates the first floor height based upon the foundation type
Models differ for riverine, coastal, and Great Lakes census blocks, as well as for Pre-FIRM and Post-FIRM structures

## Slide 5: Flood-Specific Inventory
Agriculture:
Data are provided by National Agriculture Statistical Survey (NASS) and National Resources Inventory (NRI)
  Sub-County Polygons with average crop production, cost, and value
  Top 20 crops for each NRI Region
  Does not include livestock

## Slide 6: Flood-Specific Inventory
Vehicles:
Data developed, using standard traffic models for planning
  Based on census block floor area by specific occupancy (e.g., RES1, COM1)
  Valuation based on average new and used vehicles
  Three occupancy classifications: Car, LtTrk (light truck), and HvyTrk (heavy truck)
Includes day and night estimates

## Slide 7: Damage Estimates
Damage estimated for:
  General Building Stock
  Essential Facilities
  Bridges
  Selected utility facilities
  Vehicles
  Agriculture products

## Slide 8: Depth-Damage Functions
Default depth-damage functions are assigned based on building characteristics

## Slide 9: Depth-Damage Functions (Cont'd.)
Depth-damage functions are applied to relevant depth, e.g.,
  For buildings, first-floor height (bottom of first finished floor for coastal)
  For equipment, height above first floor

## Slide 10: GBS Loss Estimation Methodology
Hazus performs an area weighted assessment of damage for aggregate inventory
  Number of grid cells at a given depth is counted and then divided by total number of cells within census block
  Result is used to weight damage at that flood depth for each occupancy

## Slide 11: GBS Loss Estimation Methodology (Cont'd.)
Assumes that inventory is evenly distributed across each census block.
Example: If 25% of the block has 2 ft. of water, it is assumed that 25% of the four single-family dwellings in the block are in 2 ft. of water.
Losses are reported as totals for each occupancy and building type rather than for each building.

## Slide 12: Activity - GBS Advantages and Disadvantages
Answer the following questions:
  What are some of the advantages of using General Building Stock?
  What are some of the disadvantages of using General Building Stock?

## Slide 13: GBS Related Analysis
The following analysis options are driven by the General Building Stock:
  Debris
  Direct Social Loss (Shelters)
  Direct Economic Loss
Why are these outputs important to communities?

## Slide 14: User-Defined Facilities
  Damages are determined by the depth of water at the location of the point representing a facility.
  Building and content damages and losses are reported on a structure-by-structure basis.
  Losses do not include business interruption, only direct loss
  UDFs are not designed to replace engineering models or knowledge.
  UDF results are best used by summing all the UDF results for an area rather than using individual structure results.

## Slide 15: Viewing Depth-Damage Functions
Instructor Demonstration
  Open the Depth-Damage Functions viewer for buildings
  Change default damage functions
  View the library
  Demonstrate creating a new damage function

## Slide 16: Agriculture Products
User must input a calendar date (e.g., May 25 that is converted to Julian Calendar (1 to 365) to define relation to crop cycle.
Damage is not flood-depth dependent.
  Area of impacted crop is determined.
No duration estimate is calculated.
  Flood Model estimates flood damage if duration is 0 days, 3 days, 7 days, or 14 days.
Based on USACE's AGDAM method.

## Slide 17: Vehicles
  Damages are based on type of vehicle and depth of water relative to critical vehicle components
  Hazus developed damage functions are based on expert opinion and historical damage data
Vehicle Type | Vehicle ID | Description | Vehicle Height | 0 ft | 0.5 ft | 1 ft | 1.5 ft | 2 ft | 2.5 ft
Car | Passenger Car | Damage to car from Inundation only | 1.5 | 0 | 7.5 | 15 | 20 | 40 | 60
LtTrk | Light Truck | Damage to light truck from Inundation only | 2.7 | 0 | 3 | 6 | 9 | 12 | 15
HvTrk | Heavy Truck | Damage to Heavy truck from Inundation only | 5 | 0 | 1.9 | 3 | 5 | 7 | 8.3

## Slide 18: Flood Warning
  Warning of imminent flooding can reduce damage up to 35% (The Day Curve)
  Hazus will reduce losses by user-defined percentage

## Slide 19: Debris Parameters
Debris analysis can be modified to account for
  Occupancy and Foundation Type
  Finish, Structure, and Foundation Weight
Specific Occupancy | Foundation Type | Minimum Depth | Maximum Depth | Finish Weight Per Thous Sq Ft | Structure Weight Per Thous Sq Ft | Foundation Weight Per Thous Sq Ft
RES1 | Slab | 0 | 4 | 4.1 | 0 | 0
RES1 | Slab | 4 | 8 | 6.8 | 0 | 0
RES1 | Slab | 8 | 25 | 6.8 | 6.5 | 25

## Slide 20: Shelter
Parameters
  Evacuation buffer
  Income
  Age

## Slide 21: Direct Economic Losses
Parameters:
  Annual Gross Sales
  Restoration Time
  Income and Wage Losses
  Inventory Value

## Slide 22: Running the Analysis
  User selects desired analysis lessons to run
  Lessons can be re-run as needed
  Hint: Select only the analysis you need (speeds up processing time)

## Slide 23: Activity 4.1
Explore the flood model analysis parameters and run the analysis for a 100-year return period scenario.
  Select a census block to explore during the exercise.
  Explore the flood occupancy mapping scheme.
  Explore the damage curves.
  Run the flood analysis.

## Slide 24: Review
What process is used to estimate damages for the general building stock?
When viewing a Building depth-damage function, why does -1 foot of water produce more damage than -3 feet of water?
What type of flood analysis do you have to run to obtain bridge damages?
What are utility damages based on in the flood model?
What Hazus inventory components are analyzed for damages only in the flood model?
Name a weighted factor for shelter that the user can alter.

## Slide 25: Questions?