## Slide 1: Lesson 6: Earthquake Hazard

## Slide 2: Goal and Objectives
Goal
This lesson will provide an overview of the earthquake hazard.
After completing this lesson, you will be able to:
  Identify at least two hazards associated with an earthquake
  List the process for completing a Level 1 Basic deterministic analysis in Hazus
  List the process for completing a Level 1 Basic probabilistic analysis in Hazus

## Slide 3: Where Do Earthquakes Happen?
Most of world's active faults are located along or near boundaries between shifting plates
  Plate Boundary earthquakes
Other active faults are not associated with plate boundaries and are inside plates
  Intra-plate earthquakes

## Slide 4: Faults
What is a fault?
  Thin zone of crushed rock between two blocks of rock
Fault lines are intersection of two planes
  Plane of fault with plane of earths surface
When earthquakes occur along these faults, rock on one side of the fault slips with respect to the other.
http://www.geology.wisc.edu/courses/g112/rock_deformation.html

## Slide 5: Types of Stress
Stresses are related to the amount of energy release, which defines the strength of an earthquake (measured in moment magnitude)

## Slide 6: Ground Shaking: Seismic Waves
Ground shaking
  Caused by four main types of body and surface seismic waves
Body waves
  Propagate through Earth's interior
    Primary/Compressional, or P waves
    Shear, or S waves

## Slide 7: Ground Shaking: Seismic Waves
Surface waves
  Arrive last, mainly cause low-frequency vibrations
    Rayleigh waves
    Love waves

## Slide 8: Ground Shaking Intensity Parameters
Magnitude
  Measure of earthquake's size
  Several scales have been defined, but the most commonly used are (1) local magnitude, commonly referred to as "Richter magnitude," (2) surface-wave magnitude, (3) body-wave magnitude, and (4) moment magnitude
  The moment magnitude (Mw) scale is uniformly applicable to all sizes of earthquakes
  Hazus uses moment magnitude

## Slide 9: Ground Shaking Intensity Parameters
Ground Motion Parameters
  PGD - Peak Ground Displacement
  PGA - Peak Ground Acceleration
    Highest amount of ground motion at the base of the structure
    Measured in g's
  PGV - Peak Ground Velocity
    Measured in inches per second

## Slide 10: Ground Shaking Intensity Parameters
Ground Motion Parameters
  Acceleration
    Accounts for the structure filtering the input ground motion
    Sa1.0 - more applicable to tall buildings
    Sa0.3 - more applicable to short buildings, shorter period of shaking

## Slide 11: Ground Shaking Intensity Parameters
Attenuation:
  Earthquake waves die off as they travel through Earth, so shaking becomes less intense farther from the fault
Local soil conditions:
  Certain soils greatly amplify shaking in earthquakes
  Passing from rock to soil, waves slow down but get bigger
  Soft and loose soil will shake more intensely than hard rock at the same distance from the source

## Slide 12: Ground Shaking Intensity Parameters
Hazus soil types A-E are based on the shear wave velocities in the first 30 m of the soil profile
Site Class | Site Class Description | Vs Min (m/s) | Vs Max
A | Hard Rock | 1500 | 
B | Rock | 760 | 1500
C | Very Dense Soil and Soft Rock | 360 | 760
D | Stiff Soils | 180 | 360
E | Soft Soils |  | 180

## Slide 13: Ground Failure
Liquefaction:
  Saturated soils (usually loose sands) lose their bearing capacity and become fluid like "quick sand" during severe ground shaking.
  Structures built on liquefiable soils "sink" in and may even topple over.
  Dependent in part on water table depth.
Landslide - Ground Failure on uneven surfaces resulting in an avalanche of soil
Surface Fault Rupture - Permanent Ground Displacements due to ground shaking

## Slide 14: Ground Failure

## Slide 15: Activity 6.1
Student activity
  Create a new study region for Salt Lake County, Utah

## Slide 16: Hazus Approach
Evaluates ground motion parameters
  At the location for site-specific inventory
  At the centroid of the census tract for aggregate inventory
Ground shaking characterized in terms of
  Location-specific shaking
  Spectral response
  Peak ground values
  Regional attenuation functions
  Site-soil effects

## Slide 17: Hazus Approach (Cont'd.)
Ground Failure shaking is characterized in terms of amount of ground failure due to liquefaction and landslide.

## Slide 18: Earthquake Scenario Wizard
  Under Hazard > Scenario... Next... Define New Scenario

## Slide 19: Defining a New Earthquake Scenario
Deterministic
  USGS ShakeMap*
  Historical epicenter event
  Source event
  Arbitrary event
Probabilistic
User-Supplied
*Preferred method

## Slide 20: USGS ShakeMap
  ShakeMaps provide near-real-time maps of ground motion and shaking intensity following significant earthquakes
  ShakeMaps also contain archives of previous earthquakes
  Will show earthquakes in the last 90 days by default - to add historic or scenario events, make selection and expand search parameters.

## Slide 21: Deterministic Events
ShakeMap - Preferred (already discussed)
  Import official USGS earthquake ground motions for credible scenarios
Historical epicenter event
  Select the desired event from the Hazus database of 3,500 historical events
Fault source event
  For the Western U.S., select the desired fault source from the Hazus database of faults
Arbitrary event
  Defined by the location of its epicenter and by its magnitude
  Epicenter is defined either by entry of latitude and longitude or graphically on a map

## Slide 22: Deterministic: Arbitrary Event
This method should only be used if ShakeMaps are not available.
  Manually enter the location of the event or define a point on a map
  Enter the Moment Magnitude and the depth of the event
  Note: Width and Fault Rupture parameters are grayed out for CEUS events

## Slide 23: Deterministic: Historical Epicenter
  View Historical Earthquakes 1755 2009 (6,200+ events)
  Sort Fields
  Map the Epicenters
  Use ArcGIS tools
    Zoom In/Out
    Add layers
    Select
    Organize Layer Visibility
    Information Tool

## Slide 24: Deterministic: Source Event
  View Known Earthquake Faults (Western US)
  Source events are only possible for the WUS areas
  Allows user to indicate location on a specific fault at which an earthquake originates

## Slide 25: Finalizing Deterministic Scenarios
  Choose which Attenuation Function to use
  Must do this for all deterministic scenarios
  Guidance is found in TM for filtering attenuation functions at the time of scenario definition

## Slide 26: Finalizing Deterministic Scenarios
Name the scenario, review the parameters, and then click Finish.
Hazus screenshot from scenario wizard where user can enter the name for the scenario event (40 characters max)

## Slide 27: Activity 6.2
Student Activity
  Complete a scenario using an arbitrary event
  Complete a scenario using ShakeMap
  Compare the results

## Slide 28: Probabilistic Scenarios
Probabilistic
  Specific Return Period
  Annualized Loss
Probabilistic seismic hazard contour maps developed by the USGS for the National Seismic Hazard Mapping Project.

## Slide 29: FEMA P366
  FEMA P366 - Hazus Annualized Earthquake Losses
  FEMA P366 highlights the impacts of both high hazard and high exposure on losses caused by earthquakes
  The FEMA P366 report can be downloaded by clicking here
  The FEMA P366 data can be viewed in an ArcGIS online web map here
Cover of FEMA publication P-366 Hazus Estimated Annualized Earthquake Losses for the United States, April 2017.

## Slide 30: Using Hazard Maps
Simplified hazard maps are automatically generated during the creation of the study region. These approximate hazard maps are based on default soil maps and the census tract boundaries.
Users can modify and enhance soils, liquefaction, landslide and water depth if spatial data is available from experts or other agencies.
If available, these expert-generated maps should be used to replace the simplified maps.

## Slide 31: Importing Hazard Maps
  Import user-defined maps to create more detailed analysis
  Expertly generated ground motion and soils maps can enhance the quality of your results.

## Slide 32: Define Hazard Maps Option
Hazard map options:
  Apply same value to the entire region
  Import hazard maps so that Hazus can generate more accurate ground motion data

## Slide 33: User-Defined Hazard Option

## Slide 34: Activity 6.3
Student Activity
  Explore the impact of modifying hazard parameters
    Soil impacts
    Magnitude impacts
  For each case
    Set the hazard parameters
    Run the analysis
    Explore the results

## Slide 35: Review
List at least two hazards associated with an earthquake.
What type of soils map can you bring into Hazus to increase the quality of the hazard definition?
What scale does Hazus use to describe the severity of an earthquake?
What is the minimum magnitude represented in the Hazus historic earthquake database?
What is the preferred Hazus earthquake data source?
What is the source event option? Why might it be grayed out?
For more advanced study, E0174 Hazus for Earthquake and Tsunami

## Slide 36: Questions?